Waste Subcommittee

Summary of Work Plans Recommended for Quantification

| Work Plan No. | Work Plan Name | Annual Results (2020) | Cumulative Results (2009–2020) |
| --- | --- | --- | --- |
|  |  | GHG Reductions (MMtCO2e) | Costs (Million $) | Cost-Effectiveness ($/tCO2e) | GHG Reductions (MMtCO2e) | Costs (NPV, Million $) | Cost-Effectiveness ($/tCO2e) |
| 1 | Landfill Methane Displacement of Fossil Fuels | 0.1 | -$0.1 | -$0.8 | 0.56 | -$11 | -$19 |
| 2 | Statewide Recycling Initiative | 5.44 | -$75 | -$14 | 34.4 | -$451 | -$13 |
| 3 | Reduced Transportation of Waste-Solid Waste Management Initiative1 | NQ | NQ | NQ | NQ | NQ | NQ |
| 4 | Improved Efficiency at Wastewater Treatment Facilities | 3.8 x 10-3 | -$0.50 | -$254 | 0.023 | -$3.2 | -$143 |
| 5 | Waste-to-Energy Digesters | 0.1 | $0.1 | $1.0 | 0.6 | $0.7 | $1.2 |
| 6 | Waste-to-Energy MSW | 0.24 | -$8.1 | -$34 | 1.42 | -$40 | -$28 |
| Sector Total After Adjusting for Overlaps | 5.9 | -$83 | -$14 | 37 | -$504 | -$14 |
| Reductions From Recent State and Federal Actions | 0.0 | $0.0 | $0.0 | 0.0 | $0.0 | $0.0 |
| Sector Total Plus Recent Actions | 5.9 | -$83 | -$14 | 37 | -$504 | -$14 |

1The Subcommittee recommends that the goals be reviewed again in 3 years.

GHG = greenhouse gas; MMtCO2e = million metric tons of carbon dioxide equivalent; $/tCO2e = dollars per metric ton of carbon dioxide equivalent; NPV = net present value; NQ = not quantified; MSW = municipal solid waste.

Negative values in the Cost and the Cost-Effectiveness columns represent net cost savings.

The numbering used to denote the above work plans is for reference purposes only; it does not reflect prioritization among these important work plans.

Waste-1. Landfill Methane Displacement of Fossil Fuels

Lead Staff Contact: Richard Illig (717) 772-5834

Summary: Landfill methane (CH4) resources and projects will be identified, assessed, and promoted to decrease fossil fuel use in business thermal applications, or otherwise displace the use of commercial natural gas resources. Maximizing the use of landfill CH4 as a fuel reduces greenhouse gas (GHG) emission of CH4 and serves to offset emissions of carbon dioxide (CO2) from the use of fossil fuels, such as coal, oil, and natural gas.

Goals: Increase landfill gas (LFG) utilization from the current 69% beneficial use to 80% beneficial use.

The term “beneficial use” applies to LFG that is combusted for the purposes of generating energy that can be used in place of energy generated from traditional sources (i.e., fossil fuels).

Implementation Period: Achieve 80% beneficial use of LFG collected by 2025.

Parties Affected/Implementing Parties: Pennsylvania Department of Environmental Protection (DEP), Pennsylvania Department of Transportation (PennDOT), Public Utility Commission (PUC), Department of Community and Economic Development (DCED), landfill owners and operators.

Data Sources/Assumptions/Methods for GHG:

LFG resources will be assessed to determine the degree to which fossil fuel use for the purpose of generating heat can be displaced. LFG thermal use projects include conversion to commercial-grade “pipeline-quality” methane (natural gas), and direct-use applications in industrial or commercial equipment. For the purposes of this report, the most common beneficial use of LFG (to generate electricity) projects will not be expanded.

Operating municipal waste landfills are evaluated annually. Key data collected from DEP Solid Waste Program Landfill Annual Operation Reports include:

- Site total waste capacity and the volume of waste disposed of,

- Landfill gas collection rates and gas quality relative to CH4 content,

- Details of LFG projects, and

- Thermal energy benefits.

LFG collection system efficiency is estimated between 60% and 85% by the U.S. Environmental Protection Agency (EPA). Collection efficiencies up to 99% have been calculated for closed, plastic-covered cells at modern landfill operations. For the purposes of this report LFG collection efficiency will be estimated at 75% for the following reasons:

- At any given time, only portions of operating landfills are closed, while other portions are open with limited practical means of collecting LFG.

- LFG collection project investments rely on optimizing LFG volume and quality relative to methane content. Overly aggressive gas collection will result in dilution with air, which can reduce the utility of the collected gas for beneficial use.

- PA landfills are well maintained. Installed gas collection systems are relatively new.

- Improved technologies and operational practices are used in landfill construction. Gas wells are routinely monitored and calibrated.

Data Sources/Assumptions/Methods for Costs:

- Direct-use project capital costs include:

  - $260/standard cubic foot per minute (scfm) of LFG for a gas treatment and compression system, plus the cost of installing the equipment.

  - $280,000 million per mile of pipeline.

  - Retrofit costs for burners and boilers to utilize LFG for fuel approximately $30,000–300,000 depending on size and type of retrofit.

- $111/scfm of LFG for annual operation and maintenance (O&M) costs.

- State permitting costs, which are not included in the analysis of this work plan, are undetermined but may include:

  - Solid waste beneficial use permit for landfill gas utilization.

  - Air Quality Program notifications and operational permit for LFG processing and gas end-use equipment.

  - Stormwater permitting and/or erosion and sedimentation controls may be needed.

  - Historic preservation or Endangered Species Act may apply to pipeline rights of way. Pipeline costs would increase accordingly.

  - Local permitting may also apply.

Historical Inventory of Landfill Emissions: A historical GHG emissions inventory was developed based on DEP waste reports from 1990 to 2008 and historical per-capita waste generation. Historical landfilling rates were estimated by back calculating from current rates. Waste receipts were then entered into EPA’s Landfill Gas Emissions Model (LandGEM) (a first-order decay model) for purposes of estimating LFG generation rates for the period of interest.

Recovery and beneficial use of methane from landfills increased sharply in the United States between 1990 and 2001, with the result that estimated emissions of methane from landfills fell 38% from 258 million metric tons of carbon dioxide equivalent (MMtCO2e) to 161 MMtCO2e in that period. There are several reasons for these increases in LFG collection (and corresponding decreases in GHG emissions from landfills):

- Passage of the Energy Policy Act of 1992 and President Clinton’s Climate Change Action Plan which included four initiatives relating to LFG collection.

- Establishment of EPA’s Landfill Methane Outreach Program (LMOP) in 1995.

- Promulgation in March 1996 of New Source Performance Standards by EPA under the Clean Air Act for large landfills that required LFG collection and control systems.

- Availability of tax credits under Section 29 of the Internal Revenue Code for LFG beneficial use projects constructed by 1998.

Pennsylvania has moved aggressively to require large landfills to collect and control LFG emissions, and it is believed that results at Pennsylvania landfills between 1990 and 2001 were even better than the national averages reported above. Since 2001, CH4 emissions from landfills in the United States are estimated to have remained roughly flat, despite a growing amount of solid waste disposed to landfills.

Figure 1-1 summarizes historical landfill emissions in Pennsylvania. It assumes that 35% of the landfill gas generated in Pennsylvania in 1990 was collected and controlled, and that collection efficiency for LFG improved in a linear function to 75% by 2001 (holding steady at 75% thereafter).

Figure 1-1. Historical Methane Emissions From Pennsylvania Landfills

Table 1-1 summarizes emissions attributable to municipal solid waste (MSW) disposal in Pennsylvania landfills in baseline year 2000, using the approach described above.

Table 1-1. 2000 Emissions of GHGs by Pennsylvania Landfills

|  | Gross Methane Generation by WIP (million cubic meters CH4) | Methane Collected for Flaring or Beneficial Use (million cubic meters CH4) | Oxidation (million cubic meters CH4) | Fugitive and Net Emissions after Thermal Destruction and Oxidation (MMtCO2e) |
| --- | --- | --- | --- | --- |
| All Landfills | 724 | 516 | 20 | 2.74 |

(note: 1 cubic meter = 35.3 cubic feet)

In calendar year 2007, active Pennsylvania landfills reported collecting over 62,700 million standard cubic feet per year (MMscf/yr) of LFG. Assuming this LFG was 50% methane, this would equate to collection of about 888 million cubic meters (MMm3) of CH4 in 2007. The LandGEM model for Pennsylvania based upon assumed waste receipts and 75% collection efficiency predicted that only 663 MMm3 of CH4 would be collected in 2007.

This may mean that actual collection efficiency in 2007 was higher (e.g., in excess of 90%), or that the model underestimates the LFG generated, or some combination of factors. The model is intended to estimate only LFG generation attributable to MSW disposal, and many MSW landfills accept waste materials that are not MSW, but that would be expected to generate landfill gas. Examples include construction and demolition debris, vegetative wastes, and some sludge and residual wastes. Thus, it is likely that the reports for 2007 included collection and destruction of gas not strictly generated by decomposition of MSW.

The 2007 DEP reports provide the best measure of LFG utilization by active landfills in Pennsylvania. Based on those reports, in 2007:

- Over 11,700 MMscf (~19%) of collected LFG was used in thermal projects that displace fossil fuel use,

- Over 19,500 MMscf (31%) was flared, and

- About 31,500 MMscf (50%) was used to generate electricity.

The 43,200 MMscf of LFG beneficially used for thermal and electrical generation applications offset more than 1 MMtCO2e emissions that otherwise would have been produced from combustion of fossil fuels.

While the volumes of LFG reported for 2007 are somewhat higher than those estimated by the LandGEM model for decomposition of MSW, the percentages reported are assumed to apply equally to LFG produced by all wastes as well as to LFG produced by MSW alone. The percentages reported for flaring and beneficial use will be used as the baseline for the business-as-usual (BAU) case.

GHG Emissions Reduction Analysis: The goal of this work plan is to increase the percentage of LFG applied to a beneficial use (rather than flaring) from 69% to 80% by 2025.

The 2009–2020 LFG emissions were estimated using the both the BAU and the “Policy” waste management scenario outlined in the Waste-2 Statewide Recycling Initiative Work Plan see below). It was assumed that any uncontrolled landfills would be converted to landfill gas-to-energy (LFGTE)/flared collection over the policy period as part of the BAU assumptions. Tables 1-2 and 1-3 summarize the methane emissions that would be captured by LFGTE projects and flares for beneficial use according to the 2025 target of 80% beneficial use. Table 1-2 presents the results for the BAU scenario for MSW landfill disposal, while Table 1-3 presents the results using the projected emissions resulting from the Policy scenario from the Statewide Recycling Initiative Work Plan. The term “beneficial use” applies to LFG that is combusted for the purposes of generating energy (direct heat, in this case) that can be used in place of energy generated from traditional sources (i.e., fossil fuels).

Table 1-2. Methane Emissions Captured by GTE and Flares for Beneficial Use (Stand-Alone Analysis)

| Year | Emissions captured by LFGTE & Flares (million m3 CH4) | Beneficial Use Goal (% of LFG Collected) | BAU Beneficial Use (% of LFG Collected) | LFG Applied to Beneficial Use (million m3 CH4) | Difference Over BAU (million m3 CH4) | MMtCO2e of Difference After Thermal Destruction | GHG Reduction |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2009 | 680 | 69% | 69% | 469 | - | - | - |
| 2010 | 687 | 70% | 69% | 478 | 4.72 | 0.07 | 0.01 |
| 2011 | 693 | 70% | 69% | 488 | 9.53 | 0.14 | 0.02 |
| 2012 | 700 | 71% | 69% | 498 | 14.44 | 0.21 | 0.02 |
| 2013 | 707 | 72% | 69% | 508 | 19.45 | 0.28 | 0.03 |
| 2014 | 715 | 72% | 69% | 518 | 24.57 | 0.35 | 0.04 |
| 2015 | 722 | 73% | 69% | 528 | 29.80 | 0.43 | 0.05 |
| 2016 | 730 | 74% | 69% | 539 | 35.15 | 0.50 | 0.06 |
| 2017 | 738 | 75% | 69% | 550 | 40.61 | 0.58 | 0.07 |
| 2018 | 747 | 75% | 69% | 561 | 46.20 | 0.66 | 0.08 |
| 2019 | 755 | 76% | 69% | 573 | 51.92 | 0.74 | 0.09 |
| 2020 | 764 | 77% | 69% | 585 | 57.77 | 0.82 | 0.10 |
| 2021 | 773 | 77% | 69% | 597 | 63.75 | 0.91 | 0.11 |
| 2022 | 782 | 78% | 69% | 609 | 69.88 | 1.00 | 0.12 |
| 2023 | 791 | 79% | 69% | 622 | 76.16 | 1.09 | 0.13 |
| 2024 | 801 | 79% | 69% | 635 | 82.58 | 1.18 | 0.14 |
| 2025 | 811 | 80% | 69% | 648 | 89.16 | 1.27 | 0.15 |
|  |  |  | Total (2009-2020) | 334 | 4.77 | 0.56 |
|  |  |  | Total (2009-2025) | 715.69 | 10.22 | 1.20 |

Table 1-3. Methane Emissions Captured by GTE and Flares for Beneficial Use (Integrated Analysis)

| Year | Emissions captured by LFGTE & Flares (million m3 CH4) | Beneficial Use Goal (% of LFG Collected) | BAU Beneficial Use (% of LFG Collected) | LFG Applied to Beneficial Use (million m3 CH4) | Difference over BAU (million m3 CH4) | MMtCO2e of difference after thermal destruction | GHG Reduction |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2009 | 680 | 69% | 69% | 469 | 0.00 | 0.00 | - |
| 2010 | 687 | 70% | 69% | 478 | 4.72 | 0.07 | 0.01 |
| 2011 | 693 | 70% | 69% | 488 | 9.53 | 0.14 | 0.02 |
| 2012 | 699 | 71% | 69% | 496 | 14.41 | 0.21 | 0.02 |
| 2013 | 704 | 72% | 69% | 505 | 19.37 | 0.28 | 0.03 |
| 2014 | 709 | 72% | 69% | 514 | 24.38 | 0.35 | 0.04 |
| 2015 | 714 | 73% | 69% | 522 | 29.45 | 0.42 | 0.05 |
| 2016 | 718 | 74% | 69% | 530 | 34.57 | 0.49 | 0.06 |
| 2017 | 722 | 75% | 69% | 538 | 39.73 | 0.57 | 0.07 |
| 2018 | 726 | 75% | 69% | 546 | 44.93 | 0.64 | 0.08 |
| 2019 | 730 | 76% | 69% | 554 | 50.18 | 0.72 | 0.08 |
| 2020 | 733 | 77% | 69% | 562 | 55.46 | 0.79 | 0.09 |
| 2021 | 737 | 77% | 69% | 569 | 60.78 | 0.87 | 0.10 |
| 2022 | 740 | 78% | 69% | 577 | 66.16 | 0.94 | 0.11 |
| 2023 | 744 | 79% | 69% | 585 | 71.58 | 1.02 | 0.12 |
| 2024 | 747 | 79% | 69% | 593 | 77.06 | 1.10 | 0.13 |
| 2025 | 751 | 80% | 69% | 601 | 82.60 | 1.18 | 0.14 |
|  |  |  | Total (2009–2020) | 327 | 4.67 | 0.55 |
|  |  |  | Total (2009–2025) | 685 | 9.78 | 1.15 |

Assuming full implementation of all other waste sector work plans, the amount of LFG that would be applied to beneficial use through 2020 as a result of this work plan’s target is 334 MMm3 CH4 (stand-alone). Assuming a heat content of 35,700 British thermal units (Btu)/m3 CH4, 348 MMm3 of CH4 would have a heat content of 11.9 x 106 MMBtu, the equivalent of 11.6 x 103 MMscf/yr of natural gas, 86 MMgal heating oil, or 591,900 shorts tons of coal.

However, in terms of GHG emissions, the 334 MMm3 CH4 shifted from flaring to thermal projects yields no direct benefit—the CH4 gas would be destroyed either in a flare or in a thermal project. The only GHG reduction quantified under this work plan is for the offset of CO2 from avoiding the use of fossil fuels (about 0.12 lb CO2/scf of natural gas).

Therefore, the estimated GHG reduction of this work plan is 1.15 MMtCO2e through 2025, with a maximum annual reduction of 0.14 MMtCO2e in 2025. These savings would be seen in the industry or residential/commercial sectors, depending on what kind of beneficial use project they are applied to. However, the GHG reduction from this work plan is presented in the summary table at the beginning of the plan, with the intersector overlaps addressed in the sector total.

Cost-Effectiveness Analysis

The cost-effectiveness estimates are based on the cost figures provided by EPA’s LMOP Project Handbook (see “Data Sources/Assumptions/Methods for Costs” section, above). These estimates ($0.98/MMBtu project cost, $0.42/MMBtu O&M cost) are applied to the values in the “Incremental LFG Applied to Beneficial Use” columns in Tables 1-2 and 1-3 to determine the capital and O&M costs for the stand-alone and integrated analyses of this work plan, respectively. The capital costs are annualized using the Cost Recovery Factor (CRF) method, assuming a 5% interest rate and 15-year loan period and multiplied by a factor of two to account for installation cost. As additional energy production capacity is added, the annualized capital cost figure represents the annualized capital cost for additional capacity added in that year, plus the annualized capital cost for capacity added in all previous years.

The social savings yielded from beneficial use of methane combusted in LFG is assumed to be equal to the difference between the avoided levelized costs of natural gas, as reported by the Residential and Commercial Subcommittee, and the assumed value of gas produced at LFGTE facilities ($3/MMBtu). The estimates are variable from year to year, and are presented in Tables 1-4 and 1-5, along with the cost estimates. The assumed discount rate for the net project cost (savings) is 5%.

The estimated levelized cost-effectiveness of this work plan is estimated to be –$5/tCO2e for the stand-alone analysis and –$2/tCO2e for the integrated analysis. Tables 1-4 and 1-5 present the detailed cost analysis results.

Table 1-4. Cost-Effectiveness of Additional LFG Beneficial Use (Stand-Alone)

| Year | Incremental LFG Available for Beneficial Use (million m^3 CH4) | Direct Heat Generation (MMBtu) | Levelized Cost Savings of Avoided Natural Gas ($/MMBtu) | Annualized Capital Costs ($MM) | O&M Cost ($MM) | Beneficial Use Revenue ($MM) | Net Work Plan Cost ($MM) | Discounted Work Plan Cost ($MM) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2009 | 0.00 | - | $8.21 | $0.00 | $0.00 | $0.00 | $0.00 | $0.00 |
| 2010 | 4.72 | 168,613 | $8.17 | $0.15 | $0.07 | $0.87 | -$0.65 | -$0.56 |
| 2011 | 9.53 | 340,540 | $8.24 | $0.45 | $0.14 | $1.78 | -$1.19 | -$0.98 |
| 2012 | 14.44 | 515,946 | $8.17 | $0.91 | $0.22 | $2.67 | -$1.54 | -$1.21 |
| 2013 | 19.45 | 694,992 | $8.14 | $1.51 | $0.29 | $3.57 | -$1.77 | -$1.32 |
| 2014 | 24.57 | 877,839 | $8.18 | $2.27 | $0.37 | $4.54 | -$1.91 | -$1.36 |
| 2015 | 29.80 | 1,064,646 | $8.22 | $3.18 | $0.45 | $5.55 | -$1.93 | -$1.31 |
| 2016 | 35.15 | 1,255,572 | $8.31 | $4.24 | $0.53 | $6.67 | -$1.90 | -$1.22 |
| 2017 | 40.61 | 1,450,775 | $8.42 | $5.46 | $0.61 | $7.87 | -$1.80 | -$1.11 |
| 2018 | 46.20 | 1,650,410 | $8.51 | $6.83 | $0.69 | $9.09 | -$1.6 | -$0.92 |
| 2019 | 51.92 | 1,854,635 | $8.45 | $8.35 | $0.78 | $10.11 | -$1.0 | -$0.55 |
| 2020 | 57.77 | 2,063,604 | $8.35 | $10.03 | $0.87 | $11.04 | -$0.1 | -$0.1 |
| 2021 | 63.75 | 2,277,475 | $8.35 | $11.86 | $0.96 | $12.18 | $0.6 | $0.3 |
| 2022 | 69.88 | 2,496,402 | $8.35 | $13.85 | $1.05 | $13.35 | $1.5 | $0.7 |
| 2023 | 76.16 | 2,720,541 | $8.35 | $16.00 | $1.14 | $14.55 | $2.6 | $1.2 |
| 2024 | 82.58 | 2,950,048 | $8.35 | $18.30 | $1.24 | $15.78 | $3.8 | $1.6 |
| 2025 | 89.16 | 3,185,080 | $8.35 | $20.76 | $1.34 | $17.04 | $5.1 | $2.1 |
|  | Total (2009-2020) | 11,937,571 |  | $43.4 | $5.0 | $63.8 | -$15.4 | -$11 |
|  | Total (2009-2025) | 25,567,117 |  | $124.1 | $10.7 | $136.7 | -$1.8 | -$5 |

Table 1-5. Cost-Effectiveness of Additional LFG Beneficial Use (Integrated Analysis)

| Year | Incremental LFG Available for Beneficial Use (million m^3 CH4) | Direct Heat Generation (MMBtu) | Levelized Cost Savings of Avoided Natural Gas ($/MMBtu) | Annualized Capital Costs ($MM) | O&M Cost ($MM) | Beneficial Use Revenue ($MM) | Net Work Plan Cost ($MM) | Discounted Work Plan Cost ($MM) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2009 | 0.00 | - | $8.21 | $0.00 | $0.00 | $0.00 | $0.00 | $0.00 |
| 2010 | 4.72 | 168,613 | $8.17 | $0.15 | $0.07 | $0.87 | -$0.65 | -$0.56 |
| 2011 | 9.53 | 340,276 | $8.24 | $0.45 | $0.14 | $1.78 | -$1.19 | -$0.98 |
| 2012 | 14.41 | 514,758 | $8.17 | $0.91 | $0.22 | $2.66 | -$1.54 | -$1.20 |
| 2013 | 19.37 | 691,843 | $8.14 | $1.51 | $0.29 | $3.55 | -$1.75 | -$1.31 |
| 2014 | 24.38 | 871,099 | $8.18 | $2.27 | $0.37 | $4.51 | -$1.88 | -$1.33 |
| 2015 | 29.45 | 1,052,204 | $8.22 | $3.18 | $0.44 | $5.49 | -$1.87 | -$1.27 |
| 2016 | 34.57 | 1,234,854 | $8.31 | $4.24 | $0.52 | $6.56 | -$1.80 | -$1.16 |
| 2017 | 39.73 | 1,419,205 | $8.42 | $5.45 | $0.60 | $7.70 | -$1.65 | -$1.01 |
| 2018 | 44.93 | 1,605,138 | $8.51 | $6.82 | $0.67 | $8.84 | -$1.35 | -$0.79 |
| 2019 | 50.18 | 1,792,545 | $8.45 | $8.33 | $0.75 | $9.77 | -$0.69 | -$0.38 |
| 2020 | 55.46 | 1,981,326 | $8.35 | $10.00 | $0.83 | $10.60 | $0.24 | $0.13 |
| 2021 | 60.78 | 2,171,393 | $8.35 | $11.83 | $0.91 | $11.61 | $1.13 | $0.57 |
| 2022 | 66.16 | 2,363,319 | $8.35 | $13.80 | $0.99 | $12.64 | $2.16 | $1.04 |
| 2023 | 71.58 | 2,557,164 | $8.35 | $15.93 | $1.07 | $13.68 | $3.33 | $1.53 |
| 2024 | 77.06 | 2,752,987 | $8.35 | $18.22 | $1.16 | $14.73 | $4.65 | $2.03 |
| 2025 | 82.60 | 2,950,852 | $8.35 | $20.65 | $1.24 | $15.78 | $6.11 | $2.54 |
|  | Total (2009-2020) | 11,671,862 |  | $43.3 | $4.9 | $62.3 | -$14.1 | -$10 |
|  | Total (2009-2025) | 24,467,577 |  | $123.7 | $10.3 | $130.8 | $3.2 | -$2 |

Implementation Steps:

- Provide tax credits to municipalities for the installation of beneficial use projects.

- Installation of beneficial use projects is dependent on landfill permitting.

- Require all active and recently closed landfills containing greater than 1 million tons of disposed of waste to install gas collection systems.

- Do not apply to closed landfills.

- Prioritize right-of-way access for LFG pipeline projects.

- Work with LFG project developers to identify the nearest economical end uses.

- Prioritize LFG projects presenting economic development benefits or that otherwise enhance the application of renewable energy technologies.

- Require LFG electrical and thermal use projects to incorporate waste heat recovery. This could help maximize fossil fuel displacement.

- Encourage projects that utilize all LFG generated at a site and/or projects able to grow with landfill site gas generation.

- Promote the high reliability of LFG projects. Most projects are able to operate continuously over extended periods of time, other than for periodic maintenance.

- Prioritize self-powered thermal LFG projects that include an electric generation component.

- Compared to incentives available for LFG to electricity projects (in the range of $2.50/MMBtu for a typical project), the incentives available for LFG to thermal projects (essentially zero) are notable by their absence.

Potential Overlap:

- Recycling work plan (see integrated analysis, above).

- Waste-to-energy MSW (see integrated analysis, above).

- Industry and/or Residential/Commercial sectors, depending on what fuels the beneficial use projects would replace.

Waste-2. Statewide Recycling Initiative

Lead Staff Contact:	Todd Pejack (717) 783-2630

Larry Holley (717) 787-7382

Summary: Support the expansion of statewide recycling to increase the amount of materials recycled. Increase the 2000 baseline MSW diversion rate of 28.2% by a factor of 0.50 by 2025. The resulting target diversion rate is 42.4%. This rate represents the total mass of MSW diverted (recycled or composted) divided by the total MSW generated in Pennsylvania.

Goals: Achieve a 42.4% diversion rate in Pennsylvania by 2025.

Implementation Period:

Table 2-1. Implementation Schedule for Goal

| YEAR | ACTION | % OF GOAL |
| --- | --- | --- |
| 2000 | Historical |  |
| 2012 | Legislation and Regulations in Place | 20% |
| 2015 | Increased Non-regulatory Enhancements | 50% |
| 2020 | Program Maintained and Improvement | 80% |
| 2025 | Completion | 100% |

Parties Affected/Implementing Parties: DEP, counties and municipalities, recycling companies, end users of recycled materials.

Background Discussion on Recycling in PA: Based on data analyzed by the Northeast Recycling Council’s (NERC's) Environmental Benefits Calculator, Pennsylvania saved 2.5 MMtCe or 9 MMtCO2e as a result of recycling approximately 4.9 MMt of materials in 2005. There is potential to reduce an additional 2.9 MMtCe or 11 MMtCO2e, assuming the recycling of an additional 4 MMt of Pennsylvania-generated recyclables identified as discarded in landfills and incinerators by the Statewide Municipal Waste Composition Study (April 2003).

More than 5.4 MMtCe or 20 MMtCO2e could be avoided annually if all recyclable materials being disposed of were added to the materials currently recovered from the municipal waste stream through recycling programs in the Commonwealth. These materials include newspaper, corrugated cardboard, office paper, magazines, mixed paper, plastic bottles, film plastic, rigid plastic, glass, steel and aluminum cans, steel scrap, and other metals. Additional savings above and beyond this projection could be realized if comprehensive programs were developed for the collection and recycling of wood waste, textiles, and carpet.

Energy conserved from manufacturing products using recycled feedstock rather than virgin raw materials, or non-renewable resources, resulted in the savings of 98 trillion Btu of energy in 2005, enough to power over 941,000 Pennsylvania homes for one year or the equivalent of conserving 786 MMgal of gasoline.

Emission and energy credit accrued by the state's recycling efforts could be recognized as a tradable commodity that may help achieve the Commonwealth's sustainability goals.

PA DEP could target recycling programs to specifically begin or increase collecting those materials that provide the maximum GHG reductions. To further stimulate recycling opportunities, PA DEP could ultimately ban those materials from disposal or processing. Aluminum, steel, plastics, cardboard, and paper should be initially targeted, as these materials will yield the greatest reductions.

Act 101, the Municipal Waste, Planning Recycling and Waste Act Reduction of 1988, provides the foundation for recycling that has resulted in comprehensive environmental and economic benefits for Pennsylvania. The Act provides for a $2/ton recycling fee on waste disposed of or processed at municipal waste landfills and resource recovery facilities in the Commonwealth. The recycling fee generates approximately $47 million annually to a Recycling Fund administered by PA DEP. The Recycling Fund provides support to local governments for implementation of recycling programs. The recycling fee also supports the stimulation of markets for recyclable materials. DEP is focusing Act 101 funds on programs geared toward financial sustainability, including those that are targeting new materials that were previously disposed of. Increasing the amount of materials recycled will provide direct reduction in GHG emissions.

Pennsylvania’s recycling program provides annual economic benefits in excess of $23 billion and nearly 82,000 jobs (National Recycling Council, REI Study, 2001). The program also provides extensive environmental benefits. The 2.5 MMtCe eliminated in 2005 by recycling amounted to a savings of approximately 3% of all GHG emissions in the Commonwealth. Also, recycling conserved considerable natural resources. By recycling almost 1.2 million tons of steel cans, appliances, and similar materials in 2005, Pennsylvania industries saved almost 1.5 million tons of iron ore, 829,786 tons of coal, and 71,124 tons of limestone. Through recycling newspapers, phone books, office paper, cardboard, and mixed paper, the Commonwealth saved the equivalent of 78 million tree seedlings grown for 10 years. These trees would sequester CO2 from the atmosphere and store it in their wood.

Table 2-2 lists the baseline data that reflect the reduction of carbon equivalent since 2001.

Table 2-2. GHG Reduction Under Historical Recycling

| YEAR | GHG REDUCTION |
| --- | --- |
| 2001 | 2.1 MMtCe |
| 2002 | 1.7 MMtCe |
| 2003 | 2.1 MMtCe |
| 2004 | 1.9 MMtCe |
| 2005 | 2.5 MMtCe |

Historically, data reported to PA DEP demonstrates an annual modest increase in the tonnage of materials recycled. In 1989, the first full year of Act 101 recycling reporting, approximately 378,000 standard tons of materials were recycled. Since then, the program has grown to nearly 4.9 million tons of materials recycled in 2005 (Table 2-3). These annual increases provide a proven track record of quantifiable environmental and economic benefits.

Table 2-3. Historical Disposal and Recycling Data

| Year | Population | Disposal (tons) | Per Capita Disposal/Day (tons) | Recycling (tons) |
| --- | --- | --- | --- | --- |
| 2000 | 12,281,054 | 9,324,468 | 0.76 | 3,791,433 |
| 2001 | 12,281,054 | 9,477,159 | 0.77 | 3,941,949 |
| 2002 | 12,281,054 | 9,613,250 | 0.78 | 3,927,048 |
| 2003 | 12,281,054 | 10,201,821 | 0.83 | 4,448,937 |
| 2004 | 12,281,054 | 10,373,136 | 0.84 | 4,747,332 |
| 2005 | 12,440,621 | 10,181,392 | 0.82 | 4,865,923 |

Pennsylvania’s recycling data were analyzed in the NERC Environmental Benefits Calculator. The raw 2005 data inputs used for the analysis are displayed in Attachment 1. Attachment 2 shows GHG reductions estimated by the calculator for 2005. Attachment 3 shows GHG reductions based on the recycling of recyclable materials that were identified as disposed of in the Statewide Waste Characterization Study (April 2003). Attachment 4 is the NERC Environmental Benefits Calculator in spreadsheet form, including five worksheets reflecting 2005 PA recycling data, showing a total reduction of 10.3 MMtCO2e. This reduction is based on the 2005 level of recycling in PA, compared to 100% disposal of recyclables.

The goal of 18 MMtCO2e represents 86% of the state’s total recycling potential of 20 MMtCO2e. This has been determined to be a feasible goal. Baseline reductions have been subtracted to reveal the additional reductions gained by this measure (10.3 MMtCO2e).

Data Sources/Assumptions/Methods for GHG:

Baseline Recycling Composition Data Source: PA DEP. 2005. “Pennsylvania Recovered Material Composition Study.” Available on-line at: http://www.dep.state.pa.us/dep/deputate/airwaste/wm/RECYCLE/document/Rec_Mat_Comp.pdf

Baseline Landfill Waste Composition Source: PA DEP. 2003. “Statewide Municipal Waste Composition Study.” Section 4. Available on-line at: http://www.dep.state.pa.us/dep/deputate/airwaste/wm/RECYCLE/Waste_Comp/Study.htm.

Data Sources/Assumptions/Methods for Costs:

The overall cost to the Commonwealth needed to increase recycling to achieve the increased GHG reductions could be funded partly through the Recycling Fund, provided it is reauthorized by the General Assembly. The Commonwealth should realize an overall economic benefit from avoided waste disposal cost, increased numbers of jobs from an increased recycling industry, taxes from new business, and some increased revenues from the sales of the new materials being recycled.

The Center for Climate Strategies (CCS) utilized an evaluation of a material recovery facility (MRF) located in Lycoming County to provide estimates of capital costs, O&M costs, and potential revenues associated with an increase in recycling volumes. The average landfill tip fee was provided in an article from PennFuture, which cited the Solid Waste Digest as the primary source. The estimate for additional collection cost due to increased recycling comes from an EPA Web page describing the difference in collection costs between low and high diversion rates, adjusted to represent the number of households in Pennsylvania. Assumptions and methods will be documented in further detail, following the presentation of the waste management scenario projections and GHG emissions reduction quantification.

Waste Management Scenario Projections

[NOTE: THE SECTION BELOW DESCRIBES THE WASTE MANAGEMENT FORECAST BASED ON SCENARIO 3A (SEE ATTACHMENT 5), WHICH WAS SELECTED BY THE SUBCOMMITTEE]

Waste disposal data on the PA DEP Web site display the amount of waste deposited at PA landfills and waste-to-energy/resource recovery facilities (hereafter referred to as WTE). These data also provide information on the origin of waste disposed of, allowing for the identification of imported waste deposited at landfill and WTE facilities. CCS utilized these disposal data for 2000 through 2005, in conjunction with the recycling total from Table 2-3, to develop the waste management business-as-usual (BAU) projection. The amount of MSW exported from PA (600,000 tons) was reported in an article in Biocycle magazine.

Table 2-4 displays the waste management baseline that serves as the basis for the waste management scenario projections. The “MSW In-State Generation” total includes all in-state MSW deposited in PA landfills and WTE facilities that originated in PA, MSW exported from PA, and MSW recycled. The “In-State MSW Disposed of in Landfills” is the sum of the “In-State MSW Disposed of in PA Landfills” and “Reported MSW Exported.” The baseline diversion rate was calculated by dividing the tonnage of MSW recycled by the in-state MSW generation. To maintain consistency with other work plans in Pennsylvania, the Industry and Waste Subcommittee utilizes 2000 as the baseline year for waste management in Pennsylvania. According to available disposal and recycling data, the recycling rate in 2000 was 28.2%. This baseline recycling rate was applied to actual disposal data for 2006 to provide a starting point for the waste management BAU projection.

Table 2-4. Pennsylvania Baseline Waste Management

| Item | Year 2006 |
| --- | --- |
| MSW In-State Generation (tons) | 15,199,459 |
| Total MSW Disposed in PA Landfills (tons) | 14,805,019 |
| Imported MSW Disposed of in PA Landfills (tons) | 6,773,180 |
| In-state MSW Disposed of in PA Landfills (tons) | 8,031,839 |
| Reported MSW Exported (tons, assumed landfilled) | 601,706 |
| In-State MSW Disposed of in Landfills (tons) | 8,633,545 |
| Total MSW Combusted in PA WTE Facilities (tons) | 2,752,084 |
| Imported MSW Disposed of in PA WTE Facilities (tons) | 479,643 |
| In-state MSW Combusted PA WTE Facilities (tons) | 2,272,442 |
| Total In-State MSW Disposal (LF + WTE, tons) | 10,905,987 |
| MSW Diverted (tons) | 4,293,472 |

The waste management baseline scenario for 2006 was utilized to project the BAU and Policy (implementation goal of 42.4% recycling rate) scenarios through 2025. The growth in waste generation (disposal + diversion) was assumed to follow the average annual growth in per-capita generation from the 2000–2008 data described above (0.52%). The BAU waste management projection was generated by increasing the “In-State MSW Generation” annually by multiplying the projected population by the average annual per-capita generation growth rate of 0.52%, and assuming a constant recycling rate of 28.2% of in-state generation. Additional recycling in each year is assumed to reduce in-state waste landfilled, so waste disposed of at WTE facilities increases constantly at 0.52%. The results of the BAU projection are displayed in Table 2-5.

Table 2-6 displays the implementation of the work plan goal through 2025, including the incremental change in the recycling rate throughout the project period. The “Target Recycling Rate” from Table 2-6 was multiplied by the “MSW In-State Generation” from each year in Table 2-5 to yield the total tons recycled under the Policy scenario, shown in Table 2-7. It was assumed that all incremental recycling will offset “In-state MSW Disposed of in PA Landfills.”

Table 2-5. BAU Pennsylvania Waste Management, 2005–2025

| Item | 2005 | 2010 | 2012 | 2015 | 2020 | 2025 |
| --- | --- | --- | --- | --- | --- | --- |
| MSW In-State Generation (tons) | 15,630,089 | 14,450,125 | 14,655,662 | 14,969,013 | 15,444,567 | 15,858,076 |
| Total MSW Disposed of in PA Landfills (tons) | 15,385,112 | 12,568,151 | 12,934,198 | 13,503,354 | 14,508,146 | 15,587,705 |
| Imported MSW Disposed of in PA Landfills (tons) | 7,515,388 | 5,024,535 | 5,280,806 | 5,682,571 | 6,435,047 | 7,297,708 |
| In-state MSW Disposed of in PA Landfills (tons) | 7,869,725 | 7,543,616 | 7,653,392 | 7,820,783 | 8,073,100 | 8,289,998 |
| Reported MSW Exported (tons, assumed landfilled) | 600,000 | 609,782 | 615,980 | 625,395 | 641,407 | 657,829 |
| In-State MSW Disposed of in Landfills (tons) | 8,469,725 | 8,153,398 | 8,269,372 | 8,446,178 | 8,714,507 | 8,947,827 |
| Total MSW Combusted in PA WTE Facilities (tons) | 2,728,123 | 2,841,537 | 2,870,418 | 2,914,291 | 2,988,907 | 3,065,433 |
| Imported MSW Disposed of in PA WTE Facilities (tons) | 433,681 | 626,615 | 623,991 | 619,832 | 621,555 | 634,699 |
| In-state MSW Combusted in PA WTE Facilities (tons) | 2,294,442 | 2,214,923 | 2,246,428 | 2,294,458 | 2,367,351 | 2,430,734 |
| Total In-State MSW Disposal (LF + WTE, tons) | 10,764,166 | 10,368,321 | 10,515,799 | 10,740,636 | 11,081,858 | 11,378,561 |
| MSW Diverted (tons) | 4,865,923 | 4,081,804 | 4,139,863 | 4,228,377 | 4,362,709 | 4,479,515 |

Table 2-6. Implementation of Targets, 2010–2025

| Goal Implementation | 2010 | 2012 | 2015 | 2020 | 2025 |
| --- | --- | --- | --- | --- | --- |
| Percent Implementation | 7% | 20% | 50% | 80% | 100% |
| Target Recycling Rate | 29.2% | 31.1% | 35.3% | 39.5% | 42.4% |
| Incremental Increase in Recycling Rate | 0.9% | 2.8% | 7.1% | 11.3% | 14.1% |

GHG Emissions Reduction Analysis

CCS utilized the NERC Environmental Benefits Calculator (EBC) to estimate the net GHG benefit of incremental MSW diversion, described by Table 2-6. This model presents both a life-cycle GHG benefit and a direct landfill GHG benefit for diversion, as opposed to disposal of waste in landfills. The EBC is informed by the EPA WAste Reduction Model (WARM), but only requires the user to input material-specific tonnage of MSWTE diverted, whereas WARM requires composition detail for landfill disposal and combustion of each waste material, in addition to the composition of diverted MSW.

Table 2-7. Policy Pennsylvania Waste Management, 2005–2025

| Item | 2005 | 2010 | 2012 | 2015 | 2020 | 2025 |
| --- | --- | --- | --- | --- | --- | --- |
| MSW In-State Generation (tons) | 15,630,089 | 14,450,125 | 14,655,662 | 14,969,013 | 15,444,567 | 15,858,076 |
| In-State MSW Disposed of in Landfills (tons) | 8,469,725 | 8,017,338 | 7,855,385 | 7,389,084 | 6,969,423 | 6,708,069 |
| In-state MSW Combusted in PA WTE Facilities (tons) | 2,294,442 | 2,214,923 | 2,246,428 | 2,294,458 | 2,367,351 | 2,430,734 |
| MSW Diverted (tons) | 4,865,923 | 4,217,864 | 4,553,849 | 5,285,471 | 6,107,793 | 6,719,273 |
| Incremental MSW Diverted (tons) | - | 136,060 | 413,986 | 1,057,094 | 1,745,084 | 2,239,758 |

CCS utilized the recycling composition provided in Attachments 1 and 3 by PA DEP. The material categories for Attachment 1 were regrouped, as necessary, in order to place all diverted waste into one of the categories accepted by the EBC. The composition based on Attachment 1 is considered to be the BAU diversion composition (Table 2-8). Table 2-8 also displays the Policy diversion composition. This column was derived by adding the additional diversion for each material from Attachment 3 to the BAU diversion composition derived from Attachment 1.

Table 2-8. Material-Specific MSW Diversion Composition—BAU and “Policy”

| Material Type | BAU Recycling Composition (% of Diversion) | Policy Recycling Composition (% of Diversion) |
| --- | --- | --- |
| Aluminum Cans | 0.4% | 0.8% |
| Steel Cans | 0.4% | 1.4% |
| Glass | 1.5% | 0.0% |
| HDPE | 0.2% | 0.9% |
| LDPE | 0.0% | 0.0% |
| PET | 0.2% | 1.1% |
| Corrugated Cardboard | 18.2% | 18.9% |
| Magazines/Third-Class Mail | 0.6% | 3.3% |
| Newspaper | 6.2% | 7.9% |
| Office Paper | 1.9% | 5.1% |
| Phonebooks | 0.0% | 0.0% |
| Textbooks | 0.0% | 0.0% |
| Whole Computers | 0.1% | 0.0% |
| Food Scraps | 1.7% | 0.9% |
| Yard Trimmings | 14.9% | 7.9% |
| Grass | 0.0% | 0.0% |
| Leaves | 0.0% | 0.0% |
| Branches | 0.0% | 0.0% |
| Ferrous Scrap Metal | 14.8% | 11.1% |
| Aluminum Scrap Metal | 0.0% | 0.5% |
| Copper Wire | 0.0% | 0.0% |
| Tires | 0.0% | 0.0% |
| Construction & Demolition | 0.0% | 0.0% |
| Carpet | 0.0% | 0.0% |
| Dimensional Lumber | 5.4% | 2.9% |
| Medium-density Fiberboard | 0.0% | 0.0% |
| Clay Bricks | 0.0% | 0.0% |
| Aggregate | 0.0% | 0.0% |
| Fly Ash | 0.0% | 0.0% |
| Mixed Paper, Broad Definition | 6.1% | 8.3% |
| Mixed Metals | 12.6% | 7.0% |
| Mixed Plastics | 1.3% | 11.4% |
| Mixed Recyclables | 13.5% | 10.7% |
| Mixed Organics | 0.0% | 0.0% |
| Other Recyclables | 0.0% | 0.0% |

The BAU and Policy recovered materials composition from Table 2-8 for each material type were multiplied by the BAU and Policy waste diversion from Tables 2-5 and 2-7, respectively. This calculation yielded the inputs for the NERC EBC. CCS ran the EBC for the years 2015, 2020, and 2025, inputting the material-specific waste diversion, as well as the total in-state waste landfill disposal and WTE combustion for that year. The EBC was used twice for each year—once for the BAU diversion and once for the Policy diversion. The difference between the two results yielded the net GHG reduction.

As previously stated, the EBC provides the net landfill GHG reduction, as well as the total life-cycle GHG reduction. The landfill benefit takes into account the reduction in carbon sequestered in landfills, as well as the reduction in energy-producing LFG due to reduced waste disposal. Therefore, it is possible that the incremental GHG reduction at landfills from increased waste diversion will be very small, or possibly negative.

Table 2-9 displays a summary of the incremental waste diversion, life-cycle GHG reduction, and direct landfill GHG reduction. In total, this work plan would result in an additional 36 million tons diverted through 2025, with a cumulative life-cycle and direct landfill GHG reduction of 65.1 and 3.11 MMtCO2e, respectively.

Table 2-9. Incremental MSW Diversion GHG Benefit

| Year | Incremental Diversion (tons) | Life-cycle GHG Reduction (MMtCO2e) | Direct Landfill GHG Reduction (MMtCO2e) |
| --- | --- | --- | --- |
| 2009 | - | - | - |
| 2010 | 136,060 | 0.47 | 0.04 |
| 2011 | 274,049 | 0.94 | 0.08 |
| 2012 | 413,986 | 1.42 | 0.13 |
| 2013 | 625,376 | 2.15 | 0.19 |
| 2014 | 839,736 | 2.89 | 0.26 |
| 2015 | 1,057,094 | 3.63 | 0.32 |
| 2016 | 1,191,378 | 3.72 | 0.17 |
| 2017 | 1,327,304 | 4.14 | 0.19 |
| 2018 | 1,464,887 | 4.57 | 0.21 |
| 2019 | 1,604,142 | 5.00 | 0.23 |
| 2020 | 1,745,084 | 5.44 | 0.25 |
| 2021 | 1,842,046 | 5.54 | 0.24 |
| 2022 | 1,939,987 | 5.84 | 0.22 |
| 2023 | 2,038,915 | 6.13 | 0.21 |
| 2024 | 2,138,835 | 6.43 | 0.20 |
| 2025 | 2,239,758 | 6.74 | 0.18 |
| Total | 20,878,638 | 65.1 | 3.11 |
| Total (2009-2020) | 34.4 | 2.07 |

Cost-Effectiveness Analysis: The evaluation of the reference case MRF facility in Lycoming County stated capital costs of $8.7 million and annual O&M costs of $407,532. This facility processes about 12,000 tons of recyclables per year. Revenue from recycled material at this facility in 2004 was $702,550. These figures were multiplied by a factor of 1.11545 to convert the financials from 2004 to 2007 dollars.

The additional collection cost from the EPA collection cost fact sheet was $2.25 per household. The number of households in PA from the 2000 census was multiplied by the 2000–2008 population growth to estimate the number of households in 2008 (4,843,881).

The landfill tipping fee ($61/ton, 2007$) assumed for this analysis is the average PA gate rate for waste disposal.

The costs associated with the additional recycling targeted by this work plan include annualized capital costs, annual O&M costs, and additional collection costs. The capital costs were determined by dividing the capital cost (in 2007$) of the reference MRF facility by the annual tons processed to determine a per-ton capital cost. This factor is multiplied by the additional tonnage recycled in each year and an annualizing factor, then is added to the annualized capital cost from previous years to capture the assumption that the recycling program will ramp up over time. The annual O&M costs were estimated by dividing the reference MRF O&M cost (in 2007$) by the annual tonnage received at that facility, multiplying that factor by the incremental tonnage recycled in each year as a result of the work plan target. Finally, the additional collection costs for each year were determined by multiplying the per-household collection cost by the 2008 number of households, then multiplying that number by the implementation rate (first row of Table 2-6).

The cost savings associated with additional recycling are assumed to include revenue from recycled materials and the avoided solid waste landfill tip fee. The MRF facility revenue was estimated by multiplying half of the 2004 per-ton revenue from the reference MRF facility by the incremental recycling tonnage for each year due to the work plan target. The avoided solid waste landfill tip fee in each year was found by multiplying the 2007 average PA gate rate of $61/ton by the incremental recycling for each year.

The net program cost, when discounted at a 5% rate from 2007, is a net savings of $848 million (net present value [NPV]) through the project period (2009–2025). The cost-effectiveness is 
–$8/tCO2e over this same period. The cost savings over the standardized planning period (2009–2020) is –$451 million (NPV), with a cost-effectiveness of –$8/tCO2e. See Table 2-10 for a detailed tabulation of results.

Table 2-10. Incremental MSW Diversion Cost-Effectiveness

| Year | Incremental Recycling (tons) | Annualized Capital Cost ($MM) | Annual O&M Cost ($MM) | Additional Collection Cost ($MM) | Materials Revenue ($MM) | Avoided Landfill Tip Fee ($MM) | Net Program Cost ($MM) | Discounted Cost ($MM) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2009 | - | $0.0 | $0.0 | $0.0 | $0.0 | $0.0 | $0.0 | $0.0 |
| 2010 | 235,561 | $18.4 | $8.9 | $0.7 | $7.7 | $14.4 | $5.9 | $5.1 |
| 2011 | 474,461 | $18.6 | $18.0 | $1.5 | $15.5 | $28.9 | -$6.4 | -$5.3 |
| 2012 | 716,734 | $18.9 | $27.2 | $2.2 | $23.4 | $43.7 | -$18.9 | -$14.8 |
| 2013 | 1,082,714 | $28.5 | $41.0 | $3.3 | $35.4 | $66.0 | -$28.6 | -$21.3 |
| 2014 | 1,453,835 | $28.9 | $55.1 | $4.4 | $47.5 | $88.7 | -$47.8 | -$34.0 |
| 2015 | 1,830,146 | $29.3 | $69.3 | $5.4 | $59.8 | $111.6 | -$67.3 | -$45.6 |
| 2016 | 2,062,631 | $18.1 | $78.1 | $6.1 | $67.4 | $125.8 | -$90.8 | -$58.5 |
| 2017 | 2,297,960 | $18.3 | $87.1 | $6.8 | $75.0 | $140.2 | -$103.1 | -$63.3 |
| 2018 | 2,536,157 | $18.6 | $96.1 | $7.4 | $82.8 | $154.7 | -$115.5 | -$67.5 |
| 2019 | 2,777,249 | $18.8 | $105.2 | $8.1 | $90.7 | $169.4 | -$128.0 | -$71.3 |
| 2020 | 3,021,262 | $19.0 | $114.5 | $8.7 | $98.7 | $184.3 | -$140.8 | -$74.7 |
| 2021 | 3,189,134 | $13.1 | $120.8 | $9.2 | $104.1 | $194.5 | -$155.6 | -$78.6 |
| 2022 | 3,358,699 | $13.2 | $127.2 | $9.6 | $109.7 | $204.9 | -$164.5 | -$79.1 |
| 2023 | 3,529,971 | $13.3 | $133.7 | $10.0 | $115.3 | $215.3 | -$173.5 | -$79.5 |
| 2024 | 3,702,964 | $13.5 | $140.3 | $10.5 | $120.9 | $225.9 | -$182.6 | -$79.7 |
| 2025 | 3,877,691 | $13.6 | $146.9 | $10.9 | $126.6 | $236.5 | -$191.7 | -$79.7 |
| Total | 36,147,170 | $302 | $1,369 | $105 | $1,180 | $2,205 | -$1,609 | -$848 |
|  |  |  |  |  | Total (2009-2020) | -$451 |

Implementation Steps:

- Ensure that the state government is taking a leadership role and maximizing recycling efforts. These efforts will be initiated with a new comprehensive management directive that will ensure all Commonwealth agencies, boards and commissions are implementing recycling and waste reduction programs, as well as purchasing environmentally preferable products.

- Encourage county governments to report recycling activities within their jurisdiction, as required by Act 101. To facilitate more timely and improved reporting PA DEP will implement or procure a new or modified reporting system to capture much of the recycling data that currently goes unreported.

- Municipal Government Recycling Programs—Assist in working to amend Act 101 to require recycling programs for municipalities with a lesser density than currently stated in the Act, and with smaller populations than the 5,000 in the current Act. PA DEP should consider proposing the new limits. Seek ways to encourage all municipal recycling programs to include all plastic and paper types in a list that should be developed by PA DEP. This would logically include all types of plastic and paper that have a market potential and/or sorting convenience to home owners—e.g., generally co-mingled materials that do not required confusing requirements for acceptable versus unacceptable materials.

- Public Recycling Availability—PA DEP should consider establishing rules on density and availability of recycling containers for all public areas in which waste disposal receptacles are placed. This should be in the form of guidelines for municipal recycling programs and state governmental agencies. Appropriate language can be incorporated into the Act 101 amendments.

- Funding through Act 101—Continue to financially support and reward recycling programs, as is currently available through Act 101 fees and grant programs.

- Conduct a comprehensive review of all the current legislation to identify areas where legislation creates obstacles or impediments to the management and beneficial use of waste material.

- Develop a strategy to focus on expanding recycling programs to:

  - Support and grow recycling industries.

  - Eliminate barriers that impede the use of waste for energy production.

  - Support the growth of private-sector recycling programs by leveling the playing field between government-supported and private-sector programs.

  - Ensure financial support to protect past investments in recycling programs.

  - Promote new private-sector investments and protect past private-sector investments in LFGTE projects and similar programs.

  - Ensure adequate funding to facilitate a sophisticated and robust statewide recycling program for all Commonwealth citizens.

- Assist in developing a single legislative package for consideration that folds all previously enacted legislation under one comprehensive package. The resulting package should include assisting in recycling at the source of generation, encouraging market development, and limiting disposal of recyclable materials at the end.

Potential Overlap:

- Increased Capture and Use of Landfill Methane

- Waste-to-Energy MSW

An overlap may exist between the WTE MSW work plan and the Statewide Recycling Initiative work plan. However, for both work plans it is assumed that waste that is either diverted or combusted reduces MSW solely from landfills. The result is no overlap between the Waste-2 and Waste-6 work plans, as the incremental GHG reduction for each would not change, depending on the implementation of the respective work plans.

Other Considerations and Notes:

Attachment 1: Pa. Materials Recycled, 2005

| MATERIAL | DEP Code(s) | Breakout | TONS |
| --- | --- | --- | --- |
| FOOD WASTE | FW1 |  | 66,481.70 |
| GLASS |  |  |  |
| GLASS: CLEAR | GL1 | 15,577.80 |  |
| GLASS: MIXED | GL2 | 21,866.30 |  |
| GLASS: GREEN | GL3 | 6,311.40 |  |
| GLASS: BROWN | GL4 | 6,681.50 |  |
| GLASS: PLATE | GL5 | 5,153.20 |  |
| GLASS: OTHER | GL6 | 1,929.30 |  |
| Subtotal Glass |  |  | 57,519.50 |
| BATTERY: LEAD-ACID | B01 |  | 22,169.90 |
| METALS |  |  |  |
| ALUMINUM CANS | AA1 | 17,590.00 |  |
| FERROUS | F01 | 580,142.10 |  |
| STEEL & BIMETALLIC (TIN) CANS | F02 | 13,935.90 |  |
| WHITE GOODS | F03 | 56,383.30 |  |
| MIXED METALS | MM1 | 174,797.40 |  |
| MIXED CANS | MX2 | 2,547.00 |  |
| NON FERROUS | N01 | 48,413.40 |  |
| COPPER | N02 | 4,524.60 |  |
| BRASS | N03 | 2,349.60 |  |
| LEAD | N04 | 167.5 |  |
| STAINLESS STEEL | N05 | 203,794.40 |  |
| NICKEL | N10 | 48.7 |  |
| WIRE/CABLE | W01 | 1,455.30 |  |
| Subtotal Metals |  |  | 1,106,149.20 |
| PAPER |  |  |  |
| PAPER: CARDBOARD | C01 | 713,552.00 |  |
| PAPER: BROWN BAGS & SACKS | C02 | 3,749.60 |  |
| PAPER: MAGAZINE | PA1 | 24,682.80 |  |
| PAPER: NEWSPRINT | PA2 | 244,252.40 |  |
| PAPER: MIX | PA3 | 230,483.50 |  |
| PAPER: OFFICE PAPER | PA4 | 76,303.80 |  |
| PAPER: COMPUTER | PA5 | 3,807.70 |  |
| PAPER: PHONE BOOKS | PA6 | 1,242.50 |  |
| Subtotal Papers |  |  | 1,298,074.30 |
| PLASTICS |  |  |  |
| DRUM PLASTIC | DR1 | 791.2 |  |
| PLASTIC: PET | PL1 | 6,754.60 |  |
| PLASTIC: HDPE | PL2 | 6,955.40 |  |
| PLASTIC: PVC (POLYVINYL/CHLORIDE) | PL3 | 15,206.50 |  |
| PLASTIC: LPDE (LOW DENSITY POLYETHYLENE) | PL4 | 2,598.90 |  |
| PLASTIC: PP (POLYPROPLENE) | PL5 | 3,236.20 |  |
| PLASTIC: PS (POLYSTYRENE) | PL6 | 1850.2 |  |
| PLASTIC: MIXED | PL7 | 16,225.60 |  |
| PLASTIC: FILM | PL8 | 5,747.40 |  |
| PLASTIC: OTHER | PL9 | 4,594.90 |  |
| Subtotal Plastics |  |  | 63,960.90 |
| SINGLE STREAM | SS1 |  | 43,645.80 |
| TEXTILES | M03 |  | 25,182.70 |
| TIRES | M01 |  | 55,416.50 |
| WOOD | WW1 |  | 213,284.90 |
| YARD TRIMMAGE | Y03 |  | 585,681.50 |
| OTHER RECYCLABLES |  |  |  |
| CIRCUIT BOARDS | CB1 | 61.6 |  |
| CONSUMER ELECTRONICS | CRT | 2,900.00 |  |
| FLUORESCENT TUBES | FL1 | 261 |  |
| HOUSEHOLD HAZARDOUS WASTE | HHW | 1,353.90 |  |
| MATTRESSES | MT1 | 116.6 |  |
| ANTIFREEZE | O02 | 1,342.20 |  |
| OIL FILTERS | OL3 | 798.9 |  |
| COMMINGLED MATERIALS | XXX | 228,699.80 |  |
| Subtotal Other Recyclables |  |  | 235,534.00 |
| 904 excess |  |  | 25,929.00 |
| Tire excess |  |  | 72,770.00 |
| ISRI excess |  |  | 51,795.00 |
| Lancaster County (RE-Trac) | INCORPORATED |  |  |
| TOTAL STANDARD |  |  | 3,923,594.90 |
| TOTAL NON-STANDARD |  |  | 942,328.10 |
| GRAND TOTAL |  |  | 4,865,923.00 |

Attachment 2: Reductions in Greenhouse Gas Emissions as a Result of 2005 Recycling

| Materials | Reporting Year 2005 | Greenhouse Gas Emissions Associated with Recycling- Metric Tons Carbon Equivalent (MTCE) | Greenhouse Gas Emissions if Recyclables Had Been Disposed (MTCE) | Net Greenhouse Gas Emissions from Recycling as Compared to Disposal (MTCE) |
| --- | --- | --- | --- | --- |
| Aluminum Cans | 33,619 | -124,418 | 381 | -124,799 |
| Steel Cans | 44,590 | -21,817 | -2,494 | -19,323 |
| Glass | 201,097 | -15,239 | 2,194 | -17,433 |
| HDPE | 40,115 | -15,230 | 1,923 | -17,152 |
| LDPE | 2,599 | -1,201 | 125 | -1,326 |
| PET | 39,736 | -16,667 | 2,161 | -18,828 |
| Corrugated Cardboard | 714,526 | -606,295 | 46,378 | -652,673 |
| Magazines/Third-class Mail | 25,935 | -21,718 | -2,313 | -19,405 |
| Newspaper | 276,048 | -210,163 | -63,883 | -146,280 |
| Office Paper | 76,652 | -59,629 | 32,309 | -91,939 |
| Phonebooks | 1,721 | -1,246 | -398 | -848 |
| Textbooks | 0 | 0 | 0 | 0 |
| Whole Computers | 0 | 0 | 0 | 0 |
| Food Scraps | 66,482 | -3,600 | 10,599 | -14,199 |
| Yard Trimmings | 585,682 | -31,717 | -35,002 | 3,286 |
| Grass | 0 | 0 | 0 | 0 |
| Leaves | 0 | 0 | 0 | 0 |
| Branches | 213,285 | -11,550 | -25,957 | 14,407 |
| Ferrous Scrap Metal | 650,458 | -318,251 | -36,376 | -281,875 |
| Aluminum Scrap Metal | 31,681 | -117,246 | 359 | -117,605 |
| Copper Wire | 0 | 0 | 0 | 0 |
| Tires | 128,187 | -63,783 | 2,101 | -65,884 |
| Construction & Demolition | 688,211 | Not Available (NA) | NA | NA |
| Carpet | 0 | 0 | 0 | 0 |
| Dimensional Lumber | 0 | 0 | 0 | 0 |
| Medium-density Fiberboard | 0 | 0 | 0 | 0 |
| Clay Bricks | 0 | NA | NA | NA |
| Aggregate | 0 | 0 | 0 | 0 |
| Fly Ash | 0 | 0 | 0 | 0 |
| Mixed Paper, Broad Definition | 244,234 | -235,593 | 12,891 | -248,484 |
| Mixed Metals | 490,360 | -703,102 | -17,722 | -685,380 |
| Mixed Plastics | 47,652 | -19,418 | 2,407 | -21,825 |
| Mixed Recyclables | 0 | 0 | 0 | 0 |
| Mixed Organics | 0 | 0 | 0 | 0 |
| Other Recyclables | 263,279 | NA | NA | NA |
| Total as a Result of Recycling | 4,866,149 | -2,597,884 | -70,318 | -2,527,566 |

Attachment 3: Potential GHG Reductions if Recyclable Materials Disposed of Were Recycled

|  | Potential Tons Recyclable | Greenhouse Gas Emissions Associated with Recycling (MTCE) |
| --- | --- | --- |
| Materials | (MSW Composition Study, April 2003) |  |
| Aluminum Cans | 48,844 | -180,763 |
| Steel Cans | 102,532 | -50,166 |
| Glass | 234,629 | -17,780 |
| HDPE | 68,082 | -25,848 |
| LDPE | 0 | 0 |
| PET | 87,601 | -36,743 |
| Corrugated Cardboard | 785,032 | -666,121 |
| Magazines/Third-class Mail | 251,027 | -210,208 |
| Newspaper | 389,263 | -296,357 |
| Office Paper | 341,975 | -266,029 |
| Phonebooks | 0 | 0 |
| Textbooks | 0 | 0 |
| Whole Computers | 0 | 0 |
| Food Scraps | 0 | 0 |
| Yard Trimmings | 0 | 0 |
| Grass | 0 | 0 |
| Leaves | 0 | 0 |
| Branches | 0 | 0 |
| Ferrous Scrap Metal | 282,131 | -138,039 |
| Aluminum Scrap Metal | 43,057 | -159,347 |
| Copper Wire | 0 | 0 |
| Tires | 0 | 0 |
| Construction & Demolition | 0 | NA |
| Carpet | 0 | 0 |
| Dimensional Lumber | 0 | 0 |
| Medium-density Fiberboard | 0 | 0 |
| Clay Bricks | 0 | NA |
| Aggregate | 0 | 0 |
| Fly Ash | 0 | 0 |
| Mixed Paper, Broad Definition | 433,821 | -418,473 |
| Mixed Metals | 32,138 | -46,081 |
| Mixed Plastics | 906,653 | -369,457 |
| Mixed Recyclables | 0 | 0 |
| Mixed Organics | 0 | 0 |
| Other Recyclables | 0 | NA |
| Total as a Result of Recycling | 4,006,785 | -2,881,412 |

Attachment 4: NERC Environmental Benefits Calculator, 2005 Pa. Recycling Data

Attachment 5: Waste Management Projection Scenarios

PA DEP provided CCS historical disposal data for 1990–2008. These data show the amount of waste disposed of at each facility in Pennsylvania, as well as the origin of that waste. CCS used these data, in addition to the recycling data provided in Table 2-3. The methods used to develop these scenarios are similar to those used to develop the Waste Management Projection (highlighted above), except for the application of the average annual growth (AAG) in per-capita generation as the growth factor for waste generation.

Scenario 3a was selected by the Industry and Waste Subcommittee during a public teleconference that took place on May 6, 2009. This scenario was used to quantify GHG reduction and cost-effectiveness.

Note for Scenario 1: The AAG in the diversion rate from 2000 through 2005 was used to simulate an increase in the BAU diversion rate. Under this scenario, the BAU diversion rate in 2025 would be 46.6%.

| Scenario 1 - BAU Growth in Diversion Rate (AAG 2000-2005) |
| --- |
| Scenario 1a - 2000-2008 AAG in per-capita generation | Baseline Diversion Rate | 31.1% |  |  |  |
|  | AAG Diversion Rate (2000-2005) | 2.0% |  |  |  |
|  | AAG Per-Capita Generation (2000-2008) | 1.4% |  |  |  |
|  |  | 2005 | 2010 | 2015 | 2025 |
|  | Total MSW Generation (tons) | 15,630,089 | 15,784,007 | 17,128,905 | 19,914,458 |
|  | BAU In-State MSW Landfilled (tons) | 8,469,725 | 8,137,042 | 8,336,915 | 8,355,735 |
|  | BAU MSW Diverted (tons) | 4,865,923 | 5,436,486 | 6,527,214 | 9,288,834 |
|  | Incremental MSW Diversion (tons) | - | 192,112 | 1,249,859 | 1,206,085 |
| Scenario 1b - 2000-2005 AAG in per-capita generation | Baseline Diversion Rate | 31.1% |  |  |  |
|  | AAG Diversion Rate (2000-2005) | 2.0% |  |  |  |
|  | AAG Per-Capita Generation (2000-2005) | 3.1% |  |  |  |
|  |  | 2005 | 2010 | 2015 | 2025 |
|  | Total MSW Generation (tons) | 15,630,089 | 16,292,711 | 19,140,177 | 26,077,464 |
|  | BAU In-State MSW Landfilled (tons) | 8,469,725 | 8,399,291 | 9,315,834 | 10,941,617 |
|  | BAU MSW Diverted (tons) | 4,865,923 | 5,611,699 | 7,293,638 | 12,163,486 |
|  | Incremental MSW Diversion (tons) | - | 198,304 | 1,396,618 | 1,579,337 |
| Scenario 1c - 2003-2008 AAG in per-capita generation | Baseline Diversion Rate | 31.1% |  |  |  |
|  | AAG Diversion Rate (2000-2005) | 2.0% |  |  |  |
|  | AAG Per-Capita Generation (2000-2008) | 0.1% |  |  |  |
|  |  | 2005 | 2010 | 2015 | 2025 |
|  | Total MSW Generation (tons) | 15,630,089 | 15,369,086 | 15,604,049 | 15,879,252 |
|  | BAU In-State MSW Landfilled (tons) | 8,469,725 | 7,923,140 | 7,594,743 | 6,662,638 |
|  | BAU MSW Diverted (tons) | 4,865,923 | 5,293,575 | 5,946,146 | 7,406,666 |
|  | Incremental MSW Diversion (tons) | - | 187,062 | 1,138,594 | 961,700 |

| Scenario 2 - 2005 Baseline Recycling Rate |
| --- |
| Scenario 2a - 2000-2008 AAG in per-capita generation | Baseline Diversion Rate | 31.1% |  |  |  |
|  | AAG Per-Capita Generation (2000-2008) | 1.1% |  |  |  |
|  |  | 2005 | 2010 | 2015 | 2025 |
|  | Total MSW Generation (tons) | 15,630,089 | 15,218,941 | 16,197,327 | 18,112,373 |
|  | BAU In-State MSW Landfilled (tons) | 8,469,725 | 8,242,019 | 8,771,877 | 9,808,995 |
|  | BAU MSW Diverted (tons) | 4,865,923 | 4,737,925 | 5,042,514 | 5,638,702 |
|  | Incremental MSW Diversion (tons) | - | 218,830 | 1,746,739 | 3,906,519 |
| Scenario 2b - 2000-2005 AAG in per-capita generation | Baseline Diversion Rate | 31.1% |  |  |  |
|  | AAG Per-Capita Generation (2000-2008) | 3.1% |  |  |  |
|  |  | 2005 | 2010 | 2015 | 2025 |
|  | Total MSW Generation (tons) | 15,630,089 | 15,832,224 | 18,599,211 | 25,340,425 |
|  | BAU In-State MSW Landfilled (tons) | 8,469,725 | 8,574,150 | 10,072,648 | 13,723,442 |
|  | BAU MSW Diverted (tons) | 4,865,923 | 4,928,851 | 5,790,263 | 7,888,922 |
|  | Incremental MSW Diversion (tons) | - | 227,649 | 2,005,760 | 5,465,482 |
| Scenario 2c - 2003-2008 AAG in per-capita generation | Baseline Diversion Rate | 31.1% |  |  |  |
|  | AAG Per-Capita Generation (2000-2008) | -0.5% |  |  |  |
|  |  | 2005 | 2010 | 2015 | 2025 |
|  | Total MSW Generation (tons) | 15,630,089 | 14,765,643 | 14,570,723 | 14,007,246 |
|  | BAU In-State MSW Landfilled (tons) | 8,469,725 | 7,996,529 | 7,890,968 | 7,585,809 |
|  | BAU MSW Diverted (tons) | 4,865,923 | 4,596,806 | 4,536,124 | 4,360,703 |
|  | Incremental MSW Diversion (tons) | - | 212,313 | 1,571,324 | 3,021,115 |

| Scenario 3 - 2000 Baseline Recycling Rate |
| --- |
| Scenario 3a - 2000-2008 AAG in per-capita generation | Baseline Diversion Rate | 28.2% |  |  |  |
|  | AAG Per-Capita Generation (2000-2008) | 0.5% |  |  |  |
|  |  | 2005 | 2010 | 2015 | 2025 |
|  | Total MSW Generation (tons) | 15,630,089 | 14,450,125 | 14,969,013 | 15,858,076 |
|  | BAU In-State MSW Landfilled (tons) | 8,469,725 | 8,153,398 | 8,446,178 | 8,947,827 |
|  | BAU MSW Diverted (tons) | 4,865,923 | 4,081,804 | 4,228,377 | 4,479,515 |
|  | Incremental MSW Diversion (tons) | - | 235,561 | 1,830,146 | 3,877,691 |
| Scenario 3b - 2000-2005 AAG in per-capita generation | Baseline Diversion Rate | 28.2% |  |  |  |
|  | AAG Per-Capita Generation (2000-2008) | 3.1% |  |  |  |
|  |  | 2005 | 2010 | 2015 | 2025 |
|  | Total MSW Generation (tons) | 15,630,089 | 15,195,816 | 17,851,578 | 24,321,816 |
|  | BAU In-State MSW Landfilled (tons) | 8,469,725 | 8,574,150 | 10,072,648 | 13,723,442 |
|  | BAU MSW Diverted (tons) | 4,865,923 | 4,292,443 | 5,042,630 | 6,870,313 |
|  | Incremental MSW Diversion (tons) | - | 247,717 | 2,182,576 | 5,947,284 |
| Scenario 3c - 2003-2008 AAG in per-capita generation | Baseline Diversion Rate | 28.2% |  |  |  |
|  | AAG Per-Capita Generation (2000-2008) | -1.2% |  |  |  |
|  |  | 2005 | 2010 | 2015 | 2025 |
|  | Total MSW Generation (tons) | 15,630,089 | 13,949,375 | 13,230,742 | 11,750,525 |
|  | BAU In-State MSW Landfilled (tons) | 8,469,725 | 7,870,853 | 7,465,369 | 6,630,165 |
|  | BAU MSW Diverted (tons) | 4,865,923 | 3,940,354 | 3,737,358 | 3,319,233 |
|  | Incremental MSW Diversion (tons) | - | 227,398 | 1,617,621 | 2,873,293 |

Waste-3. Reduced Transportation of Waste-Solid Waste Management Initiative

Lead Staff Contact: Mike Texter (717) 783-6006

Initiative Summary: The Solid Waste Management Initiative focuses on reduced transportation of waste.

Goals: The following goals were non-quantified, with a recommendation to review in 3 years:

- Reduction in vehicle miles traveled through improvement in local waste pickup efficiency.

- Improved technology (such as improved trucks or hybrids) for waste pickup and transfer.

- Reduced-consumption transportation mode (such as rail) for transport from transfer facilities to landfills.

Implementation Period: Not applicable.

Parties Affected/Implementing Parties: DEP

Data Sources/Assumptions/Methods for GHG: Not applicable.

Data Sources/Assumptions/Methods for Costs: Not applicable.

Potential Overlap: Not applicable.

Other Considerations/Notes:

In 2006, the transportation of waste from the Allentown/Bethlehem/Easton area, New Jersey, New York, and Philadelphia to disposal facilities in western Pennsylvania consumed 39.2 million gallons of fuel.

Excessive waste disposal capacity and low tipping fees in western Pennsylvania encourage the long-distance transportation of waste. The Waste Futures initiative will identify legislative, regulatory and other actions DEP can take to reduce excess waste disposal capacity.

Waste-4. Improved Efficiency at Wastewater Treatment Facilities

Lead Staff Contact: Nicki Kasi (717) 772-4053

Initiative Summary: Improving efficiency at wastewater treatment facilities through outreach programs based on sustainable infrastructure principles.

Goals: Assist 50% more treatment plants per year to improve efficiency (a 50% improvement over the current 6–8 treatment plants)

Implementation Period: 3–4 additional treatment plants per year from 2010 through 2020

Parties Affected/Implementing Parties: DEP, Outreach Assistance Provider Program (OAPP), wastewater system owners and operators.

Implementation Steps:

- DEP—Increase personnel assigned to OAPP wastewater treatment plant outreach by 50%.

- Provide grant funding for wastewater plant upgrades.

- Improve ease of permitting for wastewater plant upgrades.

Data sources/Assumptions/Methods for GHG:

Based on past program performance, treatment facilities visited by this program tend to treat around 1–2 million gallons of water per day. Calculations on GHG savings are as follows:

- 2,500 Kilowatt-hours (kWh)/MMgal treated x 1.5 MMgal/day facility = 3,750 kWh/day

- 3,750 kWh x 365 days = 1,368,750 kWh/yr

Savings at these facilities is estimated at 10%, so:

- 1,368,750 kWh/yr x 0.10 = 136,875 kWh/yr savings per facility

Converting to CO2 emissions:

136,875 kWh/yr x 7.18 x 10-4 tCO2/kWh= 98.3 tCO2/yr per facility

Table 4-1 summarizes the GHG savings possible from implementing a 50% increase in treatment plant upgrades. By upgrading an average of 3–4 additional facilities per year, a total of 0.022 MMtCO2e can be saved.

Table 4-1. GHG Savings and Costs of Treatment Plant Upgrades

| Year | Average Additional Treatment Plants Improved | Savings per Facility (metric tons CO2e/ year) | Total Savings Above BAU (metric tons CO2e/year) | Annualized Capital Costs ($) | Cost Savings to Plants ($) | Cost of Additional Personnel | NPV of Net Costs (2007$) | Cost- Effec-tiveness ($/tCO2e) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2010 | 3.5 | 98.3 | 344 | 1,686 | -$175,000 | 42,500 | -$37,416 |  |
| 2011 | 3.5 | 98.3 | 688 | 3,372 | -$262,500 | 42,500 | -$106,234 |  |
| 2012 | 3.5 | 98.3 | 1,032 | 5,058 | -$350,000 | 42,500 | -$168,413 |  |
| 2013 | 3.5 | 98.3 | 1,376 | 6,744 | -$437,500 | 42,500 | -$224,429 |  |
| 2014 | 3.5 | 98.3 | 1,720 | 8,430 | -$525,000 | 42,500 | -$274,728 |  |
| 2015 | 3.5 | 98.3 | 2,064 | 10,116 | -$612,500 | 42,500 | -$319,728 |  |
| 2016 | 3.5 | 98.3 | 2,408 | 11,802 | -$700,000 | 42,500 | -$359,819 |  |
| 2017 | 3.5 | 98.3 | 2,752 | 13,488 | -$787,500 | 42,500 | -$395,368 |  |
| 2018 | 3.5 | 98.3 | 3,096 | 15,174 | -$875,000 | 42,500 | -$426,714 |  |
| 2019 | 3.5 | 98.3 | 3,441 | 16,860 | -$962,500 | 42,500 | -$454,179 |  |
| 2020 | 3.5 | 98.3 | 3,785 | 18,546 | -$1,050,000 | 42,500 | -$478,060 |  |
|  |  | TOTAL | 22,707 |  |  |  | -$3,245,088 | -$143 |

Data Sources/Assumptions/Methods for Costs:

The cost of implementation of treatment plant upgrades is estimated at $5,000 per plant, and upgrades result in an average cost savings of $25,000 per plant per year. Upgrades were annualized over 15 years at a 5% interest rate. The cost to DEP to hire additional personnel necessary to increase outreach efforts is estimated at $35,000–$50,000. The total cost savings over the policy period is $3.2 million discounted to 2007 dollars, as summarized in Table 4-1.

Notes/Other Considerations:

The DEP Office of Water Management proposes several methods to improve efficiency in order to maintain sustainable infrastructure (SI) within wastewater treatment systems. The efficient use of energy is crucial for sustaining infrastructure and national security. Electrical energy rate cap expirations set for 2010 further exacerbate this issue.

Wastewater treatment plants typically are the largest consumer of electricity on most municipal bills, often consuming more than one-third of the energy consumed for all municipal services. In many instances, opportunities exist to reduce energy consumption at these facilities. To assist treatment plants in improving efficiency, DEP provides outreach to these facilities, teaching system operators how to use the system in the most efficient manner for treatment and suggesting ways to reduce the amount of energy required to operate the facility.

Three basic types of treatment plants are in use today: activated sludge, fixed film, and lagoon systems. Of the many treatment facilities in Pennsylvania, approximately 70% are activated sludge facilities. These facilities inject diffused air into an aeration basin to sustain a biological growth in order to treat the wastewater. The aeration basins that these facilities require are the largest consumer of electricity in wastewater treatment systems. Opportunities exist to improve efficiency in many of these facilities throughout the state.

OAPP uses part-time wage payroll instructors who are certified operators or specialists in a given field. These instructors provide on-site technical, managerial, and financial assistance to wastewater system owners and operators. The program responds to system needs identified by DEP regional staff, local government associations, or system personnel. On-site assistance and training are provided through a combination of video, classroom, and Web-based training and one-on-one assistance to address specific system problems. In the coming fiscal year, OAPP plans to accomplish the following:

- Continue on-site technical assistance for facilities requesting assistance with energy efficiency. The average activated sludge wastewater treatment plant consumes 6,000 kWh/MMgal of wastewater treated. At approximately $0.08/kWh, the energy consumption is estimated at $500/MMgal treated. Using energy audits under the auspices of OAPP, DEP proposes to assist 6–8 wastewater systems in reducing energy consumption in FY 2008–2009, with a focus on assisting at least one in each DEP region. On average, these audits will result in an estimated annual energy savings of 10%–15% in the cost of kWh per treatment plant. It must be kept in mind that due to the relatively low cost of electricity in the past, the preference for wastewater treatment has been aerobic treatment processes. This will no longer be the most cost-effective solution once the expected sharp increases in costs per kWh take place. Therefore, a further focus of this outreach effort will be to encourage and re-educate the owners and operators of wastewater treatment systems on the benefits of more energy-efficient and effective wastewater treatment processes related to anaerobic treatment.

- Continue collaboration with DEP Central and Regional staff in providing training opportunities for operators in conjunction with various associations.

- Integrate the principles of SI in all technical assistance provided by OAPP. This would include providing training with regard to all aspects of SI.

- Distribute the DVD on energy efficiency and other tools for SI.

- In conjunction with the Pennsylvania Water Environment Association, another special Nutrient Reduction Technology conference is scheduled for this fall in the Scranton area on September 10–12, 2009. This year’s conference will include energy efficiency, improvements to water quality, and other SI principles .

- Enhance the operator information center web site "Technical Corner" as it relates to SI, energy efficiency, and other operational issues.

The DEP Wastewater Outreach Program has provided assistance in energy efficiency since 1993. Unfortunately, in the 1990s energy costs were not high enough to cause a significant amount of interest. While the program had several success stories in the past, many people simply were not tuned into the idea of energy efficiency. In one case, the program saved a municipality over $100,000 annually (in an approximately 6 MMgal/day system). By today's standards, this type of savings would be greatly magnified. With the pending expiration of electrical energy rate caps and the spiraling cost of oil, people are now starting to pay attention and ask questions.

Below are examples of our past accomplishments:

- On-site technical assistance to Ridgeway Borough on energy efficiency and process control utilized the process of denitrification to save energy and chemical costs. This process utilizes the nitrate that is produced in the process of nitrification for facultative organism respiration. This results in improved water quality by reducing total nitrogen released to the receiving stream and saves money. With an investment of $500, Ridgeway was able to document savings of $31,000 annually in energy and chemical costs, in addition to improving the quality of its effluent.

- On-site energy efficiency technical assistance was provided to the City of Warren. In this system older sparge ring diffusers were used for mixing and aeration. By changing the cycles of mixing and aeration, the system could realize a savings of several thousand dollars per month. This project is still underway.

- DEP Central and Regional office staff collaborated to produce a continuing education training program titled "Flush Away High Energy Costs." In conjunction with PA Rural Water, this training session was piloted in the northwestern region and was well received by operators throughout the region. This session provides operators with the tools they need to reduce energy costs within their systems, while maintaining or improving water quality.

- In 1996, an energy efficiency in wastewater treatment systems video was produced jointly by DEP and the Maryland Center for Environmental Training. In the past year, this video was upgraded and digitized to a DVD format so it can be widely distributed.

- A training session was held in the State College area for DEP Central and Regional Office staff on energy efficiency in water/wastewater systems. This session followed a format similar to the "Flush Away High Energy Costs" operator training session. This session will help regional staff to further spread the word about energy efficiency.

- A special conference on total nutrient reduction was held in the Lancaster area last fall. This sold-out event provided operators and managers with tools needed to improve reduction of nutrients and increase efficiency.

- Assistance was provided to program staff involved in a pilot project with Montgomery County Community College to create a certificate program focusing on water and wastewater treatment. Based on the input provided, the pilot program will be modified to include basics of SI with an emphasis on energy efficiency, as well as effective process control.

All treatments plants produce excess solids, often referred to as sludge or biosolids. These excess solids have to be treated before their ultimate disposal. There are two basic types of treatment for these solids: aerobic digestion and anaerobic digestion. Anaerobic treatment tends to be more energy neutral or even produces energy, as the methane produced through this process can be used as a fuel. Unfortunately, this technology is not used in many instances in Pennsylvania, due to past problems with the operation, mostly due to problems in handling the gases produced in the treatment process. Technology in this arena has improved in recent years, making the management of these systems safer and more efficient. PA DEP currently has a pilot project in the works that will use anaerobic treatment and, depending on the outcome of this project, expects that other facilities may consider this option moving forward.

In the past fiscal year, DEP had several projects in this arena. These projects are closely tied into the overall goal of SI. In many cases, treatment systems have operated in a fashion set forth by previous generations, where energy consumption was not a large concern. Taking a moment and asking why we operate in this fashion can lead to significant opportunities for reduced energy costs and improved water quality. By today's standard, any treatment facility that is required to nitrify should also consider denitrification, as it can lead to reduced operating costs, lower sludge production, and improved water quality.

The savings realized by energy-efficient measures could easily be used to fund improved water quality. In fact, in cases where a facility starts using denitrification for the beneficial uptake of nitric acid, there would be a recovery of 60% of the cost of nitrification and improved water quality at the same time. Cost savings are certain, and the savings could escalate as energy costs continue to rise.

It is a goal for systems to be self-sustaining in the water/wastewater industry. The single largest cost for a wastewater system is the cost of aeration. Fine bubble aeration could reduce those costs by 50%. This money could be incorporated into sustainable infrastructure.

Potential Overlap:

Waste-to-Energy Digesters (for use of biosolids)

Waste-5. Waste-to-Energy Digesters

Strategy Name: Waste-to-Energy Digesters

Lead Staff Contact: Kim Hoover (717-772-5161)

Summary: This initiative encourages an expansion of regional digesters that can offer larger-scale and higher technology treatment.

Goals: Install four 1–4-megawatt (MW) digesters by 2020.

Implementation Period: This work plan targets four additional digesters by 2020, capable of utilizing a mixture of feedstock from organic MSW, organic residual waste, manure, and biosolids. It is assumed that these digesters come on line in 2012, 2014, 2016, and 2018.

Parties Affected/Implementing Parties: DEP, counties and municipalities, digester owners and operators, businesses, food companies.

Background Discussion on Anaerobic Digestion:

Thermophilic anaerobic digestion is the preferred strategy for future digestion facility planning, rather than the common mesophilic technologies that predominate on U.S. farms and wastewater treatment plants. Technologies common in Europe provide for mixed feedstocks, yield more gas, and are more efficient than manure-only digesters. The effluent (digestate) is closely monitored and can yield precision-agriculture soil amendment with a guaranteed nitrogen-phosphorus-potassium analysis for fertilizer application. Depending on the exact technology/vendor selected for these digesters, about 50% of the input is manure, and the remainder is some combination of food residues, crop residues, yard wastes, organic fraction of MSW, or sewage sludge. The European model for centralized digestion relies on processes that digest waste that has a moisture content of less than 25%. Utilizing drier feedstock creates a higher biogas yield and allows for a more stable digestion process that requires less mixing and disposal of wastewater.

Based on data provided by DEP on residual waste availability, it appears that York and Adams counties are potential locations for digestion facilities. These data, in addition to the availability of manure and organic MSW in PA, suggest that there would be ample feedstock to support four additional anaerobic digesters, each requiring 25,000 tons of waste feedstock per year. For a digester project to reach its full environmental and economic potential, a constant feedstock supply is required.

In the regional (centralized) model,

- New feedstocks for digesters include food waste and yard waste, as well as conventional manure and sludge.

- WTE digesters produce electrical power, along with high-grade solid and liquid end products.

- The business community can participate as both user and investor.

- Food companies would have an outlet for food waste.

- The concept expands upon local on-farm digesters that produce power for farm use and treated solid and liquid fertilizers.

Two known vendors of anaerobic digesters are Waste-to-Energy Solutions and BioFerm Energy Systems. Waste-to-Energy Solutions is a licensed vendor in PA and sells Niras Danish digesters. BioFerm Energy Systems is a German company that has recently expanded operations to North America.

CCS consulted with a representative of BioFerm Energy Systems and received information from this consultation to provide a reference case for the analysis of this work plan. The BioFerm system utilizes a dry fermentation technology, optimal for feedstocks with less than 25% moisture content. The minimum methane content of the resulting biogas is 55%, although higher levels have been realized. The elimination of most liquid from the digester input eliminates the need for mixing of the input. Therefore, dry fermentation anaerobic digestion facilities use much less energy (5% of electricity and 3% of heat generated by the digestion process) than traditional digesters. BioFerm Energy Systems has completed construction on 27 digesters worldwide, with many more in development. A byproduct of all anaerobic digestion is a nutrient-rich digestate that, after processing, may be used as an organic soil amendment. If markets for electricity and direct heat are not available for a given anaerobic digestion facility, it is possible to process the biogas into a liquid vehicle fuel substitute for compressed natural gas. Further information on BioFerm’s dry fermentation process is available on its Web site.

Data sources/Assumptions/Methods for GHG: The reference case digestion facility converts 25,000 tons per year in 8 fermentation chambers into 5.4 MMkWh electricity and almost 22 MMBtu of direct heat through the dry fermentation anaerobic digestion process. In addition, 17,543 tons of marketable compost is produced as a result of the process. The methane displacement as a result of the combustion of the digestion biogas is nearly 21 tCO2e/yr. The assumed GHG reduction from offset grid electricity is based on annual emission factor projections from the Electricity Generation Subcommittee (displayed in Table 5-1). A natural gas emission factor of 0.05369 tCO2e/MMBtu was used to estimate the GHG reduction from offset direct heat (the emissions factor from Residential/Commercial Subcommittee assumptions).

Data Sources/Assumptions/Methods for Costs: The assumed capital cost for a reference case dry fermentation anaerobic digestion facility is $5.5 million. O&M costs include a front loader ($4,550 per year), compost processing cost ($15 per ton compost), maintenance cost ($4,000 per fermentation chamber per year), and facility operation (1 full-time-equivalent position per year: $50,000). Revenues received by the facility include the value of compost ($30.00/ton) and the value of electricity ($0.05/kWh) and direct heat produced ($3.00/MMBtu).

GHG Emissions Reduction Analysis: The GHG reduction is estimated by computing the sum of the methane displacement, offset grid electricity, and avoided natural gas combustion for direct heat. The methane displacement is found by multiplying the number of digesters on line by the annual methane displacement value. The electricity generated per year in a single digester is multiplied by the projected grid-based electricity emission factor for each year and the number of digesters on line in each year to yield the GHG reduction from offset electricity generation. The GHG reduction from avoided natural gas combustion for direct heat is found by multiplying the direct heat produced per digester by the natural gas emission factor and the number of facilities on line in each year. The resulting cumulative GHG reduction for 2009–2020 is 0.6 MMtCO2e (see Table 5-1).

Table 5-1. Anaerobic Digestion GHG Reduction

| Year | Number of Facilities | GHG Reduction: Methane Displacement (MMtCO2e) | Projected Grid-Based Electricity Generation (tCO2e/MWh) | GHG Reduction: Offset Grid Electricity (MMtCO2e) | GHG Reduction: Offset Heat Generation - Assume Nat. Gas (MMtCO2e) | Total GHG Reduction (MMtCO2e) |
| --- | --- | --- | --- | --- | --- | --- |
| 2009 | 0 | - | 0.539 | - | - | - |
| 2010 | 0 | - | 0.539 | - | - | - |
| 2011 | 0 | - | 0.539 | - | - | - |
| 2012 | 1 | 0.02 | 0.539 | 0.003 | 0.001 | 0.02 |
| 2013 | 1 | 0.02 | 0.539 | 0.003 | 0.001 | 0.02 |
| 2014 | 2 | 0.04 | 0.538 | 0.006 | 0.002 | 0.05 |
| 2015 | 2 | 0.04 | 0.538 | 0.006 | 0.002 | 0.05 |
| 2016 | 3 | 0.06 | 0.537 | 0.009 | 0.004 | 0.07 |
| 2017 | 3 | 0.06 | 0.536 | 0.009 | 0.004 | 0.07 |
| 2018 | 4 | 0.08 | 0.535 | 0.012 | 0.005 | 0.10 |
| 2019 | 4 | 0.08 | 0.534 | 0.012 | 0.005 | 0.10 |
| 2020 | 4 | 0.08 | 0.533 | 0.012 | 0.005 | 0.10 |
| Total (2009-2020) | 0.50 |  | 0.07 | 0.03 | 0.60 |

Additional GHG reduction potential includes reduced transport of solid waste to landfills and the downstream benefit of applying compost as a soil amendment. These benefits have not been included in this quantification. The transportation benefit would require additional assumptions regarding the relative distance between the waste source and the disposal facilities (digester versus landfill) and the efficiency of trucks used. The downstream soil amendment benefit would require additional research regarding the amount of fossil fuel-based fertilizer offset and the GHG emission profile of the production and use of the traditional fertilizer.

Cost-Effectiveness Analysis: The project costs include capital cost and O&M costs highlighted in the Data Sources for Costs section. The annualized capital cost is found by multiplying the assumed capital cost by the number of facilities on line and an annualization factor. The O&M costs are found for each of the four O&M cost elements using the following calculations, with the sum of the products being the total annual O&M cost:

- Multiply the cost of the front loader by the number of facilities on line in each year.

- Multiply the compost processing cost by the per-facility quantity of compost produced and the number of facilities on line in each year.

- Multiply the maintenance cost per fermentation chamber by the number of fermentation chambers per facility (8) and the number of facilities on line in each year.

- Multiply the facility operation cost by the number of facilities on line in each year.

The revenues are calculated by taking the sum of the following products:

- Multiply the value of compost by the tons of compost produced and the number of facilities on line in each year.

- Multiply the value of electricity by the amount of electricity generated per facility and the number of facilities on line in each year.

- Multiply the value of direct heat by the amount of direct heat generated per facility and the number of facilities on line in each year.

The cost analysis produces an estimated cost of $0.70 million ($2007, NPV) for the project period 2009–2020. The cost-effectiveness over this time period is equal to $1.2 $/tCO2e. The results of the cost-effectiveness analysis are presented in Table 5-2.

Table 5-2. Anaerobic Digestion Cost-Effectiveness

| Year | Number of Facilities | Annualized Capital Cost ($MM) | Annual O&M Cost ($MM) | Annual Revenue ($MM) | Net Project Cost ($MM) | Discounted Project Cost ($MM) |
| --- | --- | --- | --- | --- | --- | --- |
| 2009 | 0 | $0.00 | $0.00 | $0.00 | $0.00 | $0.00 |
| 2010 | 0 | $0.00 | $0.00 | $0.00 | $0.00 | $0.00 |
| 2011 | 0 | $0.00 | $0.00 | $0.00 | $0.00 | $0.00 |
| 2012 | 1 | $0.53 | $0.38 | $0.86 | $0.05 | $0.04 |
| 2013 | 1 | $0.53 | $0.38 | $0.86 | $0.05 | $0.04 |
| 2014 | 2 | $1.06 | $0.76 | $1.73 | $0.09 | $0.07 |
| 2015 | 2 | $1.06 | $0.76 | $1.73 | $0.09 | $0.06 |
| 2016 | 3 | $1.59 | $1.14 | $2.59 | $0.14 | $0.09 |
| 2017 | 3 | $1.59 | $1.14 | $2.59 | $0.14 | $0.09 |
| 2018 | 4 | $2.12 | $1.53 | $3.46 | $0.19 | $0.11 |
| 2019 | 4 | $2.12 | $1.53 | $3.46 | $0.19 | $0.11 |
| 2020 | 4 | $2.12 | $1.53 | $3.46 | $0.19 | $0.10 |
| Total (2009-2020) | $0.70 |

Implementation Steps:

Centralized mixed-feedstock anaerobic digestion would be more viable, given the following incentive mechanisms:

- Allowance of renewable energy credits for carbon offset trading.

- Provision of renewable energy grants and loans from federal, state, and municipal funds.

- Purchasing agreements with utilities for electricity and direct heat provided by digestion facilities.

- Streamlining of the permitting process to allow location within 30 miles of a reliable feedstock source.

Potential Overlap:

- Increased Capture and Use of Landfill Methane

- Improved Efficiency at Wastewater Treatment

Waste-6. Waste-to-Energy MSW

Strategy Name: Waste-to-Energy Municipal Solid Waste

Lead Staff Contact: Kim Hoover (717-772-5161)

Summary: This initiative encourages more WTE projects and waste volume in the energy mix.

Goals: Increase WTE derived from MSW by 40% by 2030.

Re-evaluate the use of alternative fuels in 3 years.

Implementation Period: 20% increase by 2020, 40% by 2030

Parties Affected/Implementing Parties: DEP, power stations, private and public WTE facilities.

Background Discussion on Waste-to-Energy MSW: In 2006, Pennsylvania saved approximately 2.3 MMtCO2e as a result of recovering energy from 2.92 million tons of municipal and residual waste. The Commonwealth can reduce additional emissions by recovering energy from additional Pennsylvania municipal and residual wastes from metropolitan areas with sufficient waste generation to justify a WTE facility. These metropolitan areas include Allegheny, Berks, Chester, Lackawanna, Lehigh, Luzerne, Montgomery, Northampton, and Philadelphia counties.

The burning of solid waste reduces GHGs from avoided landfill emissions and the displacement of traditional fossil fuel energy sources, despite the fact that the operation of WTE facilities and the burning of waste also produce GHG emissions.

The recent Oneida-Herkimer Supreme Court Decision should encourage regional solid waste authorities to revisit the role of WTE as a waste management option. As remaining landfill capacity is exhausted in Bucks, Chester, Lehigh, Montgomery, and Northampton counties, there will be additional incentives for these regions to invest in WTE capacity. DEP will work with these counties to update their solid waste management plans to include WTE facilities. Concurrently, DEP will also work on legislative and regulatory changes to reduce or ban the disposal of certain types of materials. Subsequent efforts will focus on Allegheny, Berks, Lackawanna, and Luzerne counties as their remaining landfill capacity is exhausted.

DEP has been doing extensive work in an effort to include more WTE projects and volume in the energy mix. It is shown, using an EPA life-cycle measurement tool, that WTE has environmental and GHG performance superior to landfilling (with recycling and gas usage) over the complete materials management life cycle—including 30% up-front recycling, reprocessing, mining, power generation (fossil fuel avoidance), and other factors. Comparing power generation (viewing the combustion cycle only) to coal shows WTE emitting about one-third of the GHGs of a coal plant.

Consideration of using waste (as refuse-derived fuel) in standard power stations, especially waste coal circulating fluidized beds, is also considered as a good way to make use of existing capital and gain the environmental advantages from WTE. These projects would meet all current environmental standards. The subcommittee has already mentioned various methods to promote WTE—including additions/modifications to the Alternative Energy Portfolio Standard, taxes, and other financial incentives—to the various participants. That a significant amount of energy is present in the waste currently being landfilled is understood. This is usually thought of as electricity or heat, but research is underway to convert trash to liquid fuel. As such, 20–40 million barrels of liquid fuel (diesel) could be created annually from the waste the state landfills once that technology becomes viable.

Data sources/Assumptions/Methods for GHG: The information used to develop the waste management projections for the Statewide Recycling Initiative Work Plan was also used to establish the baseline MSW WTE combustion for the State of Pennsylvania (2,613,109 tons in 2000, including 534,850 tons imported of MSW). The GHG reduction was calculated by adding the incremental WTE combustion to the “Tons Sent to Incinerators” data input for the NERC CEB calculator. This is the same model used to quantify the GHG reduction for the Statewide Recycling Initiative Work Plan, and was chosen to quantify this work plan also to maintain consistency.

Data Sources/Assumptions/Methods for Costs: The assumptions for the cost elements of this work plan are $250,000/ton MSW combusted per day for capital cost and $40/ton MSW combusted per day for O&M cost. These numbers convert to $684.93/ton/year for capital cost and $0.11/ton/year for O&M cost. The revenue assumptions include the difference between the WTE and landfill tipping fees ($65/ton for WTE, $61/ton for landfills) and an estimated electricity price of $0.05/kWh.

GHG Emissions Reduction Analysis: As indicated in the Data Sources section, the waste management projection used for the Statewide Recycling Initiative Work Plan is also used for the quantification of this work plan. The WTE targets (20% in 2020, 40% in 2030) are multiplied by the 2000 baseline WTE combustion to project the future WTE combustion under this work plan. The BAU scenario WTE combustion projections are subtracted from the target WTE combustion totals to yield the incremental WTE combustion. The NERC model was used to estimate the GHG reductions of this work plan. The model was run twice each for the years 2015, 2020, and 2025. One run estimates the BAU GHG reduction, while the second estimates the GHG reduction from the WTE combustion target. The difference between the two results is the incremental GHG reduction. As the MSW management projection only goes through 2025, GHG emissions are estimated through 2025. The incremental GHG reduction through the entire target period (2009–2025) is 2.80 MMtCO2e. The incremental GHG reduction for the subcommittee’s analysis period (2009–2020) is 1.42 MMtCO2e. Table 6-1 displays these results.

Table 6-1. Incremental GHG Reduction from WTE-MSW Combustion

| Year | BAU WTE Combustion (tons) | Policy WTE Combustion (tons) | Incremental WTE Combustion (tons) | GHG Reduction (WP ESF) (MMtCO2e) |
| --- | --- | --- | --- | --- |
| 2009 | 2,193,983 | 2,193,983 | - | - |
| 2010 | 2,214,923 | 2,279,596 | 64,674 | 0.02 |
| 2011 | 2,230,624 | 2,365,210 | 134,586 | 0.04 |
| 2012 | 2,246,428 | 2,450,823 | 204,396 | 0.06 |
| 2013 | 2,262,334 | 2,536,437 | 274,103 | 0.09 |
| 2014 | 2,278,344 | 2,622,050 | 343,706 | 0.11 |
| 2015 | 2,294,458 | 2,707,664 | 413,206 | 0.13 |
| 2016 | 2,308,862 | 2,793,277 | 484,416 | 0.15 |
| 2017 | 2,323,352 | 2,878,891 | 555,539 | 0.17 |
| 2018 | 2,337,930 | 2,964,504 | 626,574 | 0.19 |
| 2019 | 2,352,597 | 3,050,118 | 697,521 | 0.22 |
| 2020 | 2,367,351 | 3,135,731 | 768,380 | 0.24 |
| 2021 | 2,379,895 | 3,187,993 | 808,099 | 0.25 |
| 2022 | 2,392,504 | 3,240,256 | 847,751 | 0.26 |
| 2023 | 2,405,180 | 3,292,518 | 887,337 | 0.28 |
| 2024 | 2,417,924 | 3,344,780 | 926,856 | 0.29 |
| 2025 | 2,430,734 | 3,397,042 | 966,308 | 0.30 |
| 2026 | 2,443,056 | 3,449,304 | 1,006,249 | - |
| 2027 | 2,455,440 | 3,501,566 | 1,046,127 | - |
| 2028 | 2,467,886 | 3,553,829 | 1,085,942 | - |
| 2029 | 2,480,396 | 3,606,091 | 1,125,695 | - |
| 2030 | 2,492,969 | 3,658,353 | 1,165,384 | - |
|  |  |  | Total (2009-2020) | 1.42 |
|  |  |  | Total (2009-2025) | 2.80 |

Additional GHG reduction potential includes reduced transport of solid waste to landfills. This benefit has not been included in this quantification. It would require additional assumptions regarding the relative distance between the waste source and the disposal facilities (WTE facility versus landfill) and the efficiency of trucks used.

Cost-Effectiveness Analysis: The costs associated with the additional WTE MSW combustion targeted by this work plan include annualized capital costs and annual O&M costs. The capital costs are determined by multiplying the capital cost for WTE combustion by the annual tons combusted and an annualizing factor. Then, the annualized capital costs for each year are added to the annualized capital costs from previous years to capture the assumption that WTE MSW combustion will ramp up over time. After 2025, the capital costs for 2010 expire. Therefore, in 2025, the annualized capital cost for the year 15 years prior are subtracted from the 2025 cost. This process is repeated for 2025 through 2030). The annual O&M costs are estimated by multiplying the per-ton O&M cost by the annual tonnage combusted in each year as a result of the work plan target.

The annual cost savings related to offset landfill tipping fees are calculated by multiplying the difference between the landfill and WTE tip fees by the incremental WTE combustion for each year. The revenue generated from generated electricity is calculated by multiplying the assumed price of electricity by the incremental WTE combustion for that year. The result is a cost savings of $40 million (NPV, 2007$) through 2020. The cost-effectiveness over the period 2009–2020 is –$28/tCO2e. The results are displayed in Table 6-2.

Table 6-2. Cost-effectiveness of Incremental WTE MSW Combustion

| Year | Incremental WTE Combustion (tons) | Annualized Capital Cost ($MM) | O&M Cost ($MM) | Additional Tip Fee ($MM) ($MM) | Revenue from Produced Electricity ($MM) | Net Project Cost ($MM) | Discounted Cost ($MM) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2009 | - | $0.0 | $0.00 | $0.00 | $0.00 | $0.0 | $0.0 |
| 2010 | 64,674 | $4.3 | $0.01 | $0.26 | $1.94 | $2.6 | $2.2 |
| 2011 | 134,586 | $4.6 | $0.01 | $0.54 | $4.04 | $1.1 | $0.9 |
| 2012 | 204,396 | $4.6 | $0.02 | $0.82 | $6.13 | -$0.7 | -$0.5 |
| 2013 | 274,103 | $4.6 | $0.03 | $1.10 | $8.22 | -$2.5 | -$1.9 |
| 2014 | 343,706 | $4.6 | $0.04 | $1.37 | $10.31 | -$4.3 | -$3.1 |
| 2015 | 413,206 | $4.6 | $0.05 | $1.65 | $12.40 | -$6.1 | -$4.1 |
| 2016 | 484,416 | $4.7 | $0.05 | $1.94 | $14.53 | -$7.8 | -$5.1 |
| 2017 | 555,539 | $4.7 | $0.06 | $2.22 | $16.67 | -$9.7 | -$5.9 |
| 2018 | 626,574 | $4.7 | $0.07 | $2.51 | $18.80 | -$11.5 | -$6.7 |
| 2019 | 697,521 | $4.7 | $0.08 | $2.79 | $20.93 | -$13.4 | -$7.4 |
| 2020 | 768,380 | $4.7 | $0.08 | $3.07 | $23.05 | -$15.2 | -$8.1 |
| 2021 | 808,099 | $2.6 | $0.09 | $3.23 | $24.24 | -$18.3 | -$9.2 |
| 2022 | 847,751 | $2.6 | $0.09 | $3.39 | $25.43 | -$19.3 | -$9.3 |
| 2023 | 887,337 | $2.6 | $0.10 | $3.55 | $26.62 | -$20.4 | -$9.3 |
| 2024 | 926,856 | $2.6 | $0.10 | $3.71 | $27.81 | -$21.4 | -$9.3 |
| 2025 | 966,308 | $2.6 | $0.11 | $3.87 | $28.99 | -$22.4 | -$9.3 |
| 2026 | 1,006,249 | $2.6 | $0.11 | $4.02 | $30.2 | -$23.4 | -$9.3 |
| 2027 | 1,046,127 | $2.6 | $0.11 | $4.18 | $31.4 | -$24.5 | -$9.2 |
| 2028 | 1,085,942 | $2.6 | $0.12 | $4.34 | $32.6 | -$25.5 | -$9.1 |
| 2029 | 1,125,695 | $2.6 | $0.12 | $4.50 | $33.8 | -$26.5 | -$9.1 |
|  | Total (2009-2020) | $51 | $0.5 | $18.3 | $137.0 | -$67.5 | -$40 |
|  | Total (2009-2025) | $64 | $1.0 | $36.0 | $270.1 | -$169.3 | -$86 |
|  | Total (2009-2030) | $77 | $1.6 | $57.7 | $433.0 | -$296.8 | -$132 |

Implementation Steps:

Incentives for WTE MSW projects include:

  - Make it easier to flow waste to privately owned facilities.

  - Include WTE in state renewable energy standards.

  - Make WTE a Tier I renewable source under the renewable energy portfolio standard.

From 2009 to 2011, WTE facilities will be supported by funds already committed to the solid waste program via the Recycling Fund. These funds will not divert dollars from the expanded recycling initiative because they come from a dedicated funding stream that is separate from recycling funding. In 2015, it is assumed that significant market potential will have been created for WTE facilities that will cause counties and private industry to invest in construction to increase WTE capacity. This market potential is a result of potential profitability from the sale of electricity generated, funds earned through collection of tipping fees, and savings from avoided landfill construction costs. DEP should work with PA counties to update their solid waste management plans to include WTE facilities. Concurrently, DEP should also work on legislative and regulatory changes to reduce or ban the disposal of certain types of materials.

Long-term actions include regulatory changes to further reduce obstacles to the use of waste as an energy source. The Waste Futures initiative will identify legislative, regulatory, and other actions DEP can take to reduce excess waste disposal capacity.

Potential Overlap:

- Increased Capture and Use of Landfill Methane

- Statewide Recycling Initiative—Reduced Transportation of Waste

- Solid Waste Initiative

- Fuels for Schools Work Plan

- AEPS Tier I (@8%, 15%, 20%) Work Plans

An overlap may exist between the WTE MSW work plan and the Statewide Recycling Initiative work plan. However, for both work plans, it is assumed that waste that is either diverted or combusted reduces MSW solely from landfills. Thus, there would not be an overlap between Waste-2 and Waste-6, as the incremental GHG reduction for each would not change depending on the implementation of the respective work plans.

# Footnotes

SCS Engineers, Current MSW Industry Position and State-of-the-Practice on LFG Collection Efficiency, Methane Oxidation, and Carbon Sequestration in Landfills (prepared for Solid Waste Industry for Climate Solutions, Version 2.2, January 2009) (“SWICS January 2009”)

scfm: Standard cubic feet per minute. To convert costs from $/scfm to $/MMBtu, divide by 262.8 [500 Btu/scfm X 525,600 minutes/year / 1,000,000]. Thus, $260/scfm becomes $0.99/mmBtu,

USEPA’s Landfill Methane Outreach Program (LMOP) LFG Energy Project Development Handbook (http://www.epa.gov/lmop/res/handbook.htm), (“LMOP Project Handbook”), Table 4-2

Ibid, $53/foot X 5,280 ft/mile = $280,000/mile

Data provided in original Work Plan. Not included in quantification, as it is assumed that the capital cost includes retrofits to burners and boilers.

EPA’s LMOP Project Handbook, op cit.

USEPA’s Landfill Gas Emissions Model—LandGEM, version 3.02. (http://www.epa.gov/ttn/catc/dir1/landgem-v302.xls). Methane Generation Rate k = 0.04 year-1, Potential Methane Generation Capacity Lo = 100 m3/Mg.

Emissions of Greenhouse Gases in the United States 2007, U.S. Department of Energy, Office of Integrated Analysis and Forecasting, Energy Information Administration (DOE/EIA-0573(2007), December 2008), page 28, Table 19.

Based on the EPA LandGEM model using estimates of MSW placed in Pennsylvania landfills between 1960 and the present, assuming 20% oxidation of uncollected methane and 100% destruction efficiency of collected methane.

EPA LMOP Benefits Calculator using 43,200 MMscf/year / 365 days/year, or 118.36 MMscf/day (http://www.epa.gov/lmop/res/lfge_benefitscalc.xls)

Heat content of methane from http://www.epa.gov/lmop/res/converter.htm; heat content of other fuels from http://www.eia.doe.gov/kids/energyfacts/science/energy_calculator.html, accessed May 2009.

Personal communication – Mike McLaughlin (SCS Engineers) to Brad Strode (CCS) via e-mail on June 2, 2009.

RW Beck. 2004. “Lycoming County Material Recovery Facility Evaluation.” Available through PA DEP at: http://www.dep.state.pa.us/dep/deputate/airwaste/wm/recycle/document/MRF_Lycoming.pdf.

PennFuture. 2007. “Critical PA Environmental Program Issues: Waste Disposal and Other Fees in Pennsylvania.” Primary source cited as, “Solid Waste Digest, Year 17, Report No. 1. 2007.” Available at: http://www.pennfuture.org/UserFiles/Tipping%20Fee%20Fact%20Sheet.pdf.

US EPA. 2009. “Wastes-Resource Conservation-Tools for Local Government Recycling Programs-Collection Costs.” Available at: http://www.epa.gov/osw/conserve/tools/localgov/economics/collection.htm.

U.S. Census Bureau. “State & County QuickFacts—Pennsylvania.” Available at: http://quickfacts.census.gov/qfd/states/42000.html.

PA DEP. “Municipal Waste Disposal Information.” Data available for 1988 through 2008. Available at: http://www.depweb.state.pa.us/landrecwaste/cwp/view.asp?A=1238&Q=464453.

Lrsova, Ljupka et al. 2008. “The State of Garbage in America – 16th Nationwide Survey of MSW Management in the U.S.” Biocycle. December 2008. Available for a limited time without subscription at www.biocycle.net.

The term “diversion” is used to identify all waste that does not end up at a landfill or incineration facility as a result of source reduction, recycling, or composting. For the purposes of this Work Plan, diversion is equal to the sum of recycling and composting. It is generally assumed that all food and yard waste is diverted to compost facilities, while all other diverted waste materials are recycled.

The Industry and Waste Subcommittee and members of the public have noted that there is currently no additional planned capacity for WTE in Pennsylvania. For the purposes of this analysis, it is assumed that limitations in capacity will reduce the WTE management of imported waste.

The Environmental Benefits Calculator and associated documentation may be found at http://www.nerc.org/documents/environmental_benefits_calculator.html.

Attachment 1 is informed by data from the PA Recovered Materials Composition Report: http://www.dep.state.pa.us/dep/deputate/airwaste/wm/RECYCLE/document/Rec_Mat_Comp.pdf.

For some of the material types accepted by the EBC, there was not enough information from the available data sources to provide a composition estimate. The unrepresented diversion was included in such categories as “Mixed Plastics”, “Mixed Metals”, or “Mixed Recyclables.”

O&M costs include labor, materials and supplies, general operating expenses, and maintenance and repairs.

Standardized factor provided by Hal Nelson of CCS via e-mail on May 11, 2009. Original source was Table 10.1 at http://www.gpoaccess.gov/usbudget/fy09/pdf/hist.pdf.

From Solid Waste Digest, as cited by PennFuture.

CCS used the Capital Recovery Factor method of animalization, assuming an 5% interest rate and 15 year loan period.

Based on recent experience of recycling markets, CCS chose to assume that the value of recycled material would be half as much as in 2004. This factor was applied in an attempt to provide a conservatively low estimate for the revenue potential of additional recycling.

Based on 2006 county waste disposal information posted on DEP website.

Electricity usage was determined by surveying twelve wastewater treatment plants in Pennsylvania and plotting electricity usage against the size of facility. This information was provided by Jim Elliott, Gannett Fleming, Inc. to Rachel Anderson, CCS via email, June 2009.

Kilowatt-hour conversion from http://www.epa.gov/grnpower/pubs/calcmeth.htm,accessed May 2009.

Thomas Brown, PA DEP; communicated via email to Rachel Anderson, CCS, May 2009.

Thomas Brown, PA DEP; personal communication to Kim Hoover, DEP, June 2009.

http://www.niras.com/Services/Energy.aspx

http://www.bioferm-es.com/us/

Personal Communication – Leah Simmet (BioFerm Energy Systems) to Brad Strode (CCS) via telephone and e-mail on May 18 and May 19, 2009.

http://www.bioferm-es.com/us/wp-content/uploads/2009/03/bioferm-dry-fermentation.pdf

Information regarding energy and compost outputs, as well as methane offset was provided by BioFerm Energy Systems. BioFerm asserts that these values are based on the AVERAGE results of dry fermentation anaerobic digestion systems. Actual yields may differ depending on feedstock mix, facility location, and other factors.

Based on discussion with BioFerm, but not a PA-specific value. CCS suggests refining assumption for compost value.

Consistent with electricity value used in Waste-to-Energy MSW Work Plan, provided by Dave Vollero.

Consistent with heat value used in Landfill Methane Displacement of Fossil Fuels Work Plan, provided by Mike McLaughlin.

CCS used the Capital Recovery Factor method of animalization, assuming an 5% interest rate and 15 year loan period.

As presented by Brian Bahor, Covanta Energy at the May 10, 2007  Solid Waste Advisory Committee Meeting; meeting materials can be found at http://www.dep.state.pa.us//dep/subject/advcoun/solidwst/swac2007.htm

under the link “Waste as an Alternative Fuel”

http://www.depweb.state.pa.us/landrecwaste/cwp/view.asp?A=1216&Q=488974

link is at “2006 Residual Waste Biennial Report Data” (Excel spreadsheet – 2006_rw.xls).

5.3 million tons is probably combustible portion of the total 19.4 million tons of residual waste (“2006 PA RW” tab of spreadsheet). Additional 4.1 MMTCO2-e is 0.788 times 5.2 million tons residual waste (same multiplier as that used by Covanta).

“Application of the U.S. Decision Support Tool for Materials and Waste Management,” by Susan Thorneloe, Keith Weitz, and Jenna Jambeck, 2006. .Thorneloe, from EPA, and Weitz, from RTI, have written numerous works on waste and WTE, going back into the 1990’s. These can be found at http://www.wte.org/docs/Thorneloe2006.pdf. This report and others may also be accessed through the IWSA site on greenhouse gases. http://www.wte.org/environment/greenhouse_gas.html.

All information provided by Dave Vollero to Brad Strode via e-mail on June 2, 2009, with the exception of the landfill tipping fee, which was cited by the PennFuture article mentioned in the Statewide Recycling Initiative Work Plan.

CCS used the Capital Recovery Factor method of animalization, assuming an 5% interest rate and 15- year loan period.