Residential and Commercial Subcommittee

Summary of Work Plans Recommended for Quantification

The Res/Com Subcommittee is in process of discussing consolidation and quantification parameters for workplans. The following tables reflect current discussion points. Table 1 shows the 11 workplans for quantification – these represent consolidation of 30 workplans (see Table 2 for consolidation cross-reference). Note that two workplans in Table 2 are under discussion as potential stand-alone workplans. Workplans that are being discussed as “non-quantifiable” are shown in Table 3. Workplans being excluded due to overlap, lack of definition, or expectation that resulting emission reductions are relatively low are shown in Table 4.

Table 1: Workplans for Quantification (some workplans still under discussion)

| Work Plan # / Grouping | Work Plan Name | Notes | Quantification Parameters Completed |
| --- | --- | --- | --- |
| RC-1 | High Performance Buildings |  | Goals and implementation period chosen (see page 5), other assumptions need review |
| RC-2 | Integrated Keystone Home Performance (KHP) |  |  |
| RC-3 | Leadership for State/Local and School Buildings |  |  |
| RC-4 | Lighting |  | Not yet |
| RC-5 | Appliance Standards |  | Not yet |
| RC-6 | Distributed Energy – Geothermal Heating and Cooling | Workplans for technologies that generate electricity moved to energy supply (CHP, Building integrated renewables). Res/Com subcommittee considering setting targets for renewable generation from buildings. | Not yet |
| RC-7 | Demand Side Management (DSM) – Gas |  | Not yet |
| RC-8 | Water Conservation | Including industrial sector | Not yet |
| RC-9 | Department of General Services (DGS) – Initiative to Reduce Energy Use by State Government | Subcommittee has not yet discussed, may be covered by other workplans | Not yet |
| RC-10 | B5 Bioheat Initiative |  | Not yet |
| RC-11 | Utility Incentives for Demand-Side Management | Workplan moved to Energy Supply |  |

Table 2: Reference for Workplans Consolidated into Table 1

| Work Plan # / Grouping | Work Plan Name | Notes |
| --- | --- | --- |
| RC-1 | High Performance Buildings |  |
|  | GHG 2030 Challenge |  |
|  | High Performance Building Codes (New Construction |  |
|  | Energy Audits for Commercial Real Estate Transfers |  |
|  | Building Performance Labels That Reflect Actual Utility Usage |  |
|  | Energy Audits for Residential Real Estate Transfers |  |
|  | Energy Improvement Mortgages |  |
|  | PA Encourages Commissioning and Retro-commissioning | To be considered for individual quantification |
|  | Re-Roof Pennsylvania | To be considered for individual quantification |
|  | PA Home Climate Champion Collaborative |  |
| RC-2 | Integrated Keystone Home Performance (KHP) |  |
| RC-3 | Leadership for State/Local and School Buildings |  |
|  | Benchmarking All Existing Commonwealth-Owned Facilities |  |
|  | High Performance Building Standards for Existing Commonwealth of PA Buildings |  |
|  | High Performance Pennsylvania Buildings |  |
|  | Benchmarking All Existing PA Public PreK-12 Schools, AVTSs (Area Vocational Technical Schools) & CTCs (Career Technical Centers) |  |
|  | PASSHE Energy Consumption Reduction |  |
| RC-4 | Lighting |  |
|  | Re-Light Pennsylvania |  |
|  | Expand Energy Efficiency Funds |  |
|  | Increase Lighting Efficiency Standards |  |
| RC-5 | Appliance Standards |  |
|  | Federal Appliance Standards |  |
|  | Appliance Standards |  |
|  | Turn it Off PA! Campaign | ?? Possible inclusion, needs workplan |
| RC-6 | Distributed Energy – Geothermal heating and cooling |  |
|  | Renewable Heating and Cooling with Geothermal Infrastructure |  |
|  | Promote Combined Heat and Power | Workplan moved to Energy Supply |
|  | PA Promotes Building-Integrated Photovoltaics (BIPV), Solar Thermal, Micro Hydro, and Micro Wind | Workplan moved to Energy Supply |
|  | Solar Rights Initiative | Workplan moved to Energy Supply |
| RC-7 | Demand Side Management (DSM) – Gas |  |
| RC-8 | Water Conservation | Subcommittee has not discussed yet |
| RC-9 | Department of General Services (DGS) – Initiative to Reduce Energy Use by State Government | Subcommittee has not discussed yet |
| RC-10 | B5 Bioheat Initiative |  |
| RC-11 | Utility Incentives for Demand-Side Management | Workplan moved to Energy Supply |

Table 3: Workplans under discussion as “Non-Quantifiable” – to be included as recommendations without quantification of GHG reductions and costs

Work Plan

Green Strings

PA values embodied energy in building materials, including historic structures

Sustainability education programs

Educate Consumers on the Value of Energy Efficient Homes and Businesses

Training for building operators

Promoting Green Campus Initiative

Climate Change Collaborative Clearinghouse

Adaptive building reuse

Table 4: Workplans suggested for exclusion

| Work Plan | Rationale for excluding from quantification |
| --- | --- |
| Require high-performance buildings for schools and other State-funded projects | No workplan Covered by other workplans |
| Energy Recovery from air exhaust | Potential reductions are too small to warrant quantification |
| Pennsylvania State System of Higher Education (PASSHE) Green Energy | Potential reductions are too small to warrant quantification |
| Fuels for Schools | Moved to agriculture subcommittee |
| Building Codes and Standards | Overlaps with other workplans |
| Four day work week | Not quantifiable – move to transportation with telecommuting reword to flex week |
| Promote geo-thermal (geo-exchange) heating and cooling | Repeated workplan |
| Home ‘MPG’ labels | Not quantifiable, overlap with other workplans |

# High Performance Buildings

New Buildings Goals and standards

|  |  | 2010 | 2020 | 2030 |
| --- | --- | --- | --- | --- |
| New Commercial (private) | Overall goal (relative to 2007 building) | 60% fossil fuel reduction | 80% fossil fuel reduction | 100% fossil fuel reduction |
|  | Performance standard | LEED Silver ENERGY STAR 75 | LEED Silver ENERGY STAR 85 | ?? |
|  | Fraction of buildings that meet standard | 100% of new buildings | 100% of new buildings | 100% of new buildings |
|  | Deployment of renewable energy | To be determined | To be determined | To be determined |
| New Commercial (Commonwealth owned or operated) | Overall goal (relative to 2007 building) | 60% fossil fuel reduction | 80% fossil fuel reduction | 100% fossil fuel reduction |
|  | Performance standard | LEED Silver ENERGY STAR 85 | LEED Silver ENERGY STAR 85 | ?? |
|  | Fraction of buildings that meet standard | 100% of new buildings | 100% of new buildings | 100% of new buildings |
|  | Deployment of renewable energy | To be determined | To be determined | To be determined |
| New Commercial (Schools) | Overall goal (relative to 2007 building) | 60% fossil fuel reduction | 80% fossil fuel reduction | 100% fossil fuel reduction |
|  | Performance standard | LEED Silver ENERGY STAR 85 | LEED Silver ENERGY STAR 85 | ?? |
|  | Fraction of buildings that meet standard | 100% of new buildings | 100% of new buildings | 100% of new buildings |
|  | Deployment of renewable energy | To be determined | To be determined | To be determined |
| New Residential | Overall goal (relative to 2007 building) | 60% fossil fuel reduction | 80% fossil fuel reduction | 100% fossil fuel reduction |
|  | Performance standard | HERS 50 | HERS 40 | HERS 30 |
|  | Fraction of buildings that meet standard | 100% of new buildings | 100% of new buildings | 100% of new buildings |
|  | Deployment of renewable energy | To be determined | To be determined | To be determined |

Notes: Overall goals reflect 2030 GHG goals

Looking for input from subcommittee on Performance standards that will help set policies to achieve the Overall goals

Fraction of buildings that meet standard is currently set to 100% to reflect a mandate policy (rather than incentives that would likely reach a smaller fraction of buildings)

Existing Buildings Goals and standards

|  |  | 2010 | 2020 | 2030 |
| --- | --- | --- | --- | --- |
| Existing Commercial (private) | Overall goal (relative to 2007 building) | 50% fossil fuel reduction | 50% fossil fuel reduction | 50% fossil fuel reduction |
|  | Performance standard | ENERGY STAR 75 | LEED EB Silver ENERGY STAR 75 | LEED EB Silver ENERGY STAR 75 |
|  | Fraction of buildings that meet standard | 20% of existing buildings | 50% of existing buildings | 100% of existing buildings |
|  | Deployment of renewable energy | To be determined | To be determined | To be determined |
| Existing Commercial (Commonwealth owned or operated) | Overall goal (relative to 2007 building) | 60% fossil fuel reduction | 80% fossil fuel reduction | 100% fossil fuel reduction |
|  | Performance standard | ENERGY STAR 75 | LEED EB Silver ENERGY STAR 75 | LEED EB Silver ENERGY STAR 75 |
|  | Fraction of buildings that meet standard | 20% of existing buildings | 50% of existing buildings | 100% of existing buildings |
|  | Deployment of renewable energy | To be determined | To be determined | To be determined |
| Existing Commercial (Schools) | Overall goal (relative to 2007 building) | 60% fossil fuel reduction | 80% fossil fuel reduction | 100% fossil fuel reduction |
|  | Performance standard | ENERGY STAR 75 | LEED EB Silver ENERGY STAR 75 | LEED EB Silver ENERGY STAR 75 |
|  | Fraction of buildings that meet standard | 20% of existing buildings | 50% of existing buildings | 100% of existing buildings |
|  | Deployment of renewable energy | To be determined | To be determined | To be determined |
| Existing Residential | Overall goal (relative to 2007 building) | 60% fossil fuel reduction | 80% fossil fuel reduction | 100% fossil fuel reduction |
|  | Performance standard | HERS 50 | HERS 50 | HERS 50 |
|  | Fraction of buildings that meet standard | 20% of existing buildings | 50% of existing buildings | 100% of existing buildings |
|  | Deployment of renewable energy | To be determined | To be determined | To be determined |

Notes: Overall goals reflect 2030 GHG goals

Looking for input from subcommittee on Performance standards that will help set policies to achieve the Overall goals

Fraction of buildings that meet standard is currently set to 100% to reflect a mandate policy (rather than incentives that would likely reach a smaller fraction of buildings)

GHG 2030 Challenge

Strategy Name: 2030 Challenge

All new buildings, developments and major renovations shall be designed to meet a fossil fuel, GHG-emitting, energy consumption performance standard of 50% of the regional (or country) average for that building type.

At a minimum, an equal amount of existing building area shall be renovated annually to meet a fossil fuel, GHG-emitting, energy consumption performance standard of 50% of the regional (or country) average for that building type.

The fossil fuel reduction standard for all new buildings shall be increased to:

60% in 2010
70% in 2015
80% in 2020
90% in 2025

Carbon-neutral in 2030 (using no fossil fuel GHG emitting energy to operate).

These targets may be accomplished by implementing innovative sustainable design strategies, generating on-site renewable power and/or purchasing (20% maximum) renewable energy and/or certified renewable energy credits.

This challenge has been adopted by, among others, the US Conference of Mayors, the USGBC, the State of New Mexico, the cities of Chicago, Santa Fe, Albuquerque, Sarasota, Plano, and Seattle.

Lead Staff Contact:

GGGC - Maureen Guttman, AIA   717.772.8946

Other Involved Agencies:

All

Primary: DGS (State owned buildings)

Revenue (Tax credits)

Possible New Measure(s): (See workplans below)

“High-Performance PA Buildings” – All Commonwealth owned or funded construction projects must meet a performance level equivalent to a minimum of LEED Silver plus an Energy Star rating of 85. (See HB 45, SB 672)

“High-Performance Tax Credits” – Tax credits for private sector construction projects that meet a performance level equivalent to a minimum of LEED Silver plus an Energy Star rating of 85. (See HB 46, SB 673)

“Green Strings” – All Commonwealth funding programs, whether grants, loans, tax credits, tax incentives, etc. will have at least a minimal expectation of energy/resource conservation results attached.

“Energy Audits at Real Estate Transfer” – Energy audit required as part of “seller’s disclosure” information in a residential sales transaction.

“Keystone Home Performance” – Retooling of Keystone HELP program to offer greater degree of assistance (much lower loan rates) to homeowners implementing energy-saving measures based on whole-house energy audit.  (See also PHFA’s “Keystone Renovate and Repair” program, and Maine Home Performance Program)

“Illuminating Education” – Current GGGC/OETD program to distribute CFL lamps to middle school students in PA as part of overall energy curriculum program.

“LEED for Homes” – Require that all new homes bear an Energy Star rating (15% more energy efficient than code-compliant construction). Increase required efficiency requirement every 5 years all new homes are carbon-neutral.

High Performance Building Codes (New Construction)

Strategy Name:  High Performance Building Codes

Lead Staff Contact:  GGGC - Maureen Guttman, AIA   717.772.8946

Summary: Requires that all new construction in Pennsylvania achieve a minimum of LEED certification by incorporating green building requirements in the statewide building code (UCC).

Other Involved Agencies:

DGS, Labor & Industry, DCED

Existing Measures:  No LEED or high-performance requirements exist in PA.  EPACT 2005 tax credits for certain Energy Star measures do exist.

Possible New Measure(s):

Incorporate green building requirements in the statewide building code (UCC).

  - This could be a phased-in approach that begins in the first years with Energy Star standards, and expands to cover high-performance standards for energy, water, storm water, materials, etc.  Ultimate goal will be zero-carbon buildings throughout the Commonwealth.

  - UCC improvements will need to include a much higher level of administration and enforcement than what currently exists.  Statewide emphasis on training must occur.

  - New construction will not be permitted if plans/subsequent building are not LEED certified

Potential GHG Reduction: The building sector (residential, commercial, industrial, institutional) accounts for approximately 48% of energy consumption and carbon emissions.  Significant cuts in this sector will dramatically reduce the amount of GHG emissions from the use of fossil fuels to produce electricity, and burning of oil and gas for heating, etc.

A minimal requirement that all new construction achieves an Energy Star rating will translate into approximately 15% less energy consumed than current code-compliant buildings.

As requirements increase over time, GHG savings will also increase.

Economic Cost:  No direct cost to the Commonwealth.  Possible need to invest in training and education.

Implementation Steps:

Support integrity of UCC as it gets negotiated in the General Assembly.

Propose modifications to UCC to increase energy standards for all new construction.

Provide/oversee training and education on how new standards will be achieved.

Potential Overlap:

Reduced Load Growth, HB 2200, Alternative Energy Investment Act, AEPS Tier I @ 8%, 15% and 20%, Work Plans

Demand Side Management – Natural Gas Work Plan

Energy Audits Work Plan

High Performance Building Construction Tax Credits

Summary:  Tax credits for private sector construction projects that meet a performance level equivalent to a minimum of LEED Silver plus an Energy Star rating of 85.

Lead Staff Contact:   GGGC - Maureen Guttman, AIA   717.772.8946

Other Involved Agencies: DGS, Revenue

Existing Measures:  No LEED or high-performance requirements exist in PA. EPACT 2005 tax credits for certain Energy Star measures do exist.  The Alternative Energy Investment Act included $25 million for a grant program to support high-performance green buildings, however there is still a need to provide further incentives.

Possible New Measure(s):  Tax credits for private sector construction projects that meet a performance level equivalent to a minimum of LEED Silver plus an Energy Star rating of 85.  Several current legislative proposals based on this objective are being considered (See HB 46, SB 673).

Potential GHG Reduction:  Qualified private-sector construction would consume at least 25% less energy (approximately 25% less GHG emissions) than current building projects.

Economic Cost:  Tax credits would represent a decrease in revenue to the Commonwealth.

Implementation Steps:

Support legislative proposals (with possible amendments to achieve greater savings) and determine high-performance rating system to be used (LEED, Green Globes, other).

Potential Overlap:

Reduced Load Growth, HB 2200, Alternative Energy Investment Act, AEPS Tier I @ 8%, 15% and 20%, Work Plans

Demand Side Management – Natural Gas Work Plan

Energy Audits Work Plan

Energy Audits for Commercial Real Estate Transfers

Strategy Name: Energy audits for commercial real estate transfers

Lead Staff Contact: Maureen Guttman (717-783-8411)

Summary:  This initiative requires energy information to be included in a “seller’s disclosure” for commercial real estate transfers.  Alternatively, an Energy Star portfolio manager energy use index would be required.  The “seller’s disclosure” consists of a property disclosure statement; the seller is currently not obligated by the statute to make any specific investigation.  A third party verified energy audit should be an additional document and not part of “seller’s disclosure.”

Other Involved Agencies:

Possible New Measure(s):

Potential GHG Reduction:  No quantifiable reductions.

Economic Cost:  $ million savings

Implementation Steps:

Potential Overlap:

Building Performance Labels That Reflect Actual Utility Usage

Work plan needed

Energy Audits for Residential Real Estate Transfers

Lead Staff Contact:  Jeffrey Olsen (717-705-0374)

Summary: Require energy information be included among list of items in a “Sellers Disclosure” during residential real estate transfers.  The “Sellers Disclosure” in Pennsylvania consists of a property disclosure statement. The seller is not obligated by the statute to make any specific investigation or inquiry in an effort to complete the property disclosure statement. Any third party verified home energy audit should not be part of a “Sellers Disclosure” but rather a stand alone additional required document.

Other Agencies Involved:  Department of State’s State Real Estate Commission; Public Utility Commission; Pennsylvania Housing Finance Agency.

Possible New Measures: Currently residential energy audits are available for homeowners looking to identify energy efficiency and areas where investment into increased efficiency may lead to significant cost savings. In addition, a properly conducted audit can indicate upgrades, which would also qualify the homeowner for substantial energy tax credits and/or deductions. It’s important to note that tax breaks are part of legislative programs, which have defined periods that may disappear in future years.

Companies with the appropriate expertise should conduct energy audits. While the requirements for determining expertise exist as guidelines for reputable companies, third party verified requirements are ill defined and span a broad spectrum of energy efficiency. Chapter 75 of the Pennsylvania Home Inspection Law states that an inspection company must be a not for profit franchise, have membership in more than 10 states, require inspectors not to become fully accredited unless they have performed or participated in more than 100 home inspections, and must pass a recognized accredited examination. It also requires members to comply with a code of conduct and attend continuing professional education classes.

The closest thing to requirements for third party verified audits can be found through some co-ops and networks such as the Residential Energy Services Network, which provides standardized home energy ratings commensurate with home energy efficiency. Mandating energy audits or inspections for all real estate transactions would require better defined parameters for energy ratings and a more definitive final rating score. Presently it is doubtful that enough companies currently exist to provide the number of audits that this program would require.

Projected GHG Reduction: The major factors that affect utilities bills in residential homes are insulation, windows, air leaks, heating and cooling systems, water heaters and major appliances. Sealing air leaks in most homes can result in over 28% of your audits overall estimated annual energy savings for upgrades. Additionally, adding programmable thermostats, ceiling insulation and replacing an antiquated water heater can save as much as 50%.

Ideally, a typical home of 2,200 square feet, built in the 1960’s with an overall volume of 17,600 cubic foot volume and assuming natural gas heat and the price of electricity at .081/kwh and implementing all of the anticipated energy efficient upgrades will save approximately $118 / month in energy bills.

For comparison, a row house occupying 1542 square feet and a volume of 15420 cubic feet built in 1907 and heated with natural gas under similar utility costs, as the first example would result in a monthly-anticipated savings of $68.00.

Additionally, these upgrades would result in greenhouse gas reductions on the average of 11 tons per year for the first example and 2 tons for the second example. According to the Pennsylvania Association of Realtors there were 170,000 real estate transactions in Pennsylvania in 2007 involving single-family residences.  If audits had been required as a condition of sale on each transaction and assuming that each buyer will follow the recommendations of the audit to at least at a minimum seal air leaks, 28% of the audits overall estimated annual energy savings would be realized. Further assuming an average 6.5 tons of greenhouse gases reduced annually per fully implemented audit (maximum 11 tons and minimum 2 tons) would have resulted in an average annual greenhouse gas reduction of 309,400 tons. (6.5 tons x 170,000 audits x .28).    309,400 metric tons the first year*

These figures are derived from sample home energy audits conducted by CMC Energy Services and reported as part of their Home Energy Tune-uP Report. (cmcenergy.com)

Estimated Costs: Immediate benefits are seen through reduced homeowner costs, which may allow more people to afford to buy homes. The Environmental Protection Agency has confirmed that more energy efficient housing can result in as much as 6.8% more potential buyers qualifying for mortgages. And with respect to increased market value, the Appraisal Journal recently documented that the value of a home increases $25.00 for every $1.00 decrease in energy costs.

Most audits, including phase I and II environmental studies are required by the lender as a means of avoiding liability. With some exceptions such as termite and radon inspections, the cost of audits rests with the buyer. Because an energy audit would significantly benefit the buyer, this audit would probably be their responsibility. Because the audits would probably not indicate situations that would be unhealthy or structurally unsafe, there would not be any regulatory obligation for the seller to pay for the fixes. The cost for a residential energy audit starts at around $400.00 for an average family dwelling and increases dramatically with the size of the house. Audits for as much as $2,000 to $3,000 would not be uncommon and depending on the original efficiency of the home, may not provide enough energy savings opportunities for the buyer to be cost efficient. While the intent of the audit is to identify areas where efficiency upgrades can save money, many potential buyers might use them as a measuring device to avoid certain homes that are more energy inefficient. This could result in reduced sales to older homes in older neighborhoods.

Implementation Strategy:

As no legal requirement for audits is currently mandated in Pennsylvania, the Residential Real Estate Transfer Law must be amended. This would require legislative action.

Additionally the mortgage industry must recognize a standardized home rating system and adjust the current mortgage profile to include value realized as a result of increased energy efficiency.

  - Energy audits coupled with Energy Mortgages could increase the number of families qualified for mortgages. Energy Mortgages credit a home’s efficiency rating into the loan by proportionately increasing the value of the home. In order to have a Pennsylvania policy of requiring lenders to provide Energy Mortgages it’s necessary to adopt a standardized home rating system like the one adopted by the Residential Energy Services Network (RESNET). Home energy ratings provide a standard measurement of a home’s energy efficiency. Ratings can be used for both new and existing homes. An effective rating system will include all information necessary for a lender to judge the worthiness of a home to meet the criteria for an Energy Mortgage. The program is already established through the mortgage industry and the National Association of State Energy Officials however the program is not that widespread with only 19 accredited providers in Pennsylvania.

  - Basing a mortgage on the home efficiency rating allows the buyer to borrow more on the basis that the monthly utility bills will be proportionally less. In cases where the home is in need of energy efficient upgrades an Energy Improvement Mortgage could help finance the upgrades in an existing home by allowing the owner to use a portion of the mortgage payment to pay for the cost of the upgrades.

Potential Overlap:

Reduced Load Growth, HB 2200, Alternative Energy Investment Act, AEPS Tier I @ 8%, 15% and 20%, Work Plans

Keystone Home Performance Work Plan

Demand Side Management – Natural Gas Work Plan

Energy Improvement Mortgages

Strategy Name: Energy improvement mortgages

Lead Staff Contact: Maureen Guttman (717-783-8411)

Summary:  This initiative develops energy improvement mortgages (EIM) or energy efficient (EE) mortgages and promotes these products in PA.

Other Involved Agencies: PA Housing and Finance Authority and Fannie Mae

Possible New Measure(s):

Potential GHG Reduction:  No quantifiable reductions.

Economic Cost:  $ million savings

Implementation Steps:

Potential Overlap:

PA Encourages Commissioning and Retro-commissioning

Strategy Name: PA Encourages Commissioning and Retro-commissioning

Lead Staff Contact:  Valerie Hearn, Business Development Specialist, Green Building Alliance, Pittsburgh, PA; 412.431.0709 or valerieh@gbapgh.org

Summary:  Promote the common practice of performing commissioning and retro-commissioning processes on newly constructed, renovated, and existing buildings for the purpose of ensuring optimal performance of building systems.

Other Involved Agencies:  ASHRAE; Leadership in Energy and Environmental Design (LEED®) Certification; BOMA; IFMA; EPA

Possible New Measure(s):  Promote the common practice of performing commissioning processes on newly constructed and/or renovated buildings for the purpose of ensuring optimal performance of building systems.

Building project teams are currently familiar with ASHRAE standards which cite building commissioning as good practice. (Guideline 0-2005)

Potential GHG Reduction:   Unknown at this time; can be determined from identifying problem areas in MEP systems, appropriately addressing them, and reducing energy use.

Economic Cost:  In an effort to deter costs associated with such activities, the state could subsidize those costs or provide tax incentives.

Implementation Steps:  This program may be implemented through stricter municipal/state building codes.  Certain tax incentives and/or credits may also be assigned to assist in full implementation.

Several mainstream certification standards also promote the practice of performing building commissioning making the activity seem more attractive.

An example of such a program is the California Governor’s Green building Executive Order and AB 32 which calls for all California state buildings greater than 50,000 sq. ft. be retro-commissioned by June 30, 2013 and re-commissioned every five years.  Nearly 25 RCx are at or near completion.  The energy efficiency measures implemented through this program to date have a verified electricity savings of approximately 10%.  Projected electricity savings for measures yet to be implemented is approximately 15%.  Projected natural gas savings is 16%.

Potential Overlap:

PASSHE Energy Consumption Reduction

Benchmarking all Commonwealth Buildings by 2010; meet Energy Star 75 rating by 2020

High Performance Pennsylvania Building Standards

High Performance Building Standards for Existing Commonwealth of PA Buildings

High Performance Building Construction Tax Credits

Re-Roof Pennsylvania

Strategy Name: Re-Roof PA

Lead Staff Contact: Maureen Guttman (717-783-8411)

Summary:  This initiative mandates standards of thermal resistance for all new roofing projects.

Other Involved Agencies:

Possible New Measure(s):

High reflectivity should be mandatory for all commercial buildings to minimize cooling loads.

Thermal resistance standards (R/U factors) should be raised to minimize both cooling and heating loads.

Green roofs should be promoted with incentives for benefits to cooling, carbon sequestration and storm water management.

Skylights for daylighting should be mandatory for roof replacements in buildings sized less than four stories with deep sections that result in windowless spaces for occupants.

Shading or insulation from renewable energy systems as secondary goals should be explored.

Potential GHG Reduction:

Economic Cost:  $ million savings

Implementation Steps:

Potential Overlap:

PA Home Climate Champion Collaborative

Strategy Name: Pennsylvania Home Climate Champion Collaborative (PHCCC)

Lead Staff Contact: Vivian Loftness or Maureen Guttman (717-783-8411)

Summary:  This initiative establishes a PHCCC project with the goal of 100,000 low energy homes.

Other Involved Agencies:

Possible New Measure(s):

The Pennsylvania Home Climate Champion Collaborative provides vision, clarity and access to human and physical resources so that 100,000 homes will achieve substantial (greater than 60%) energy reductions while maintaining or improving indoor air quality, resilience to storms and power outages, adaptability, comfort, and affordability between now and 2025.  Five % of these demonstration projects should achieve PassivHaus energy independence goals of 90% energy reduction with 10% met by renewable energy.

Potential GHG Reduction:

Economic Cost:  $ million savings

Implementation Steps:

Potential Overlap:

# Integrated Keystone Home Performance (KHP)

Integrated Keystone Home Performance (KHP)

Lead Staff Contact: Dennis Maloskey, GGGC (717-787-8378)

Summary:  This initiative ties existing funding programs together to incentivize energy audits, improve energy efficiency and increase the environmental benefits of these programs, which target existing residential buildings.

Other Involved Agencies: PA Treasury, PHFA, US EPA / DOE, PUC, DCED

Existing Measures:

PA Treasury: Keystone HELP Program offers reduced-interest unsecured loans for Pennsylvania residents to purchase energy efficient equipment, such as HVAC, windows, hot water heaters, etc.

PHFA: Keystone Renovate & Repair Loan Program (R&R) can be used to pay for repairs and improvements that increase the basic livability of the home, including additions and construction, that makes the home safer, more energy efficient, or more accessible to people with disabilities or people who are elderly.

U.S. EPA and U.S. DOE: Home Performance with ENERGY STAR program, a model program which uses a comprehensive, whole-house approach to improving energy efficiency and comfort at home, while helping to protect the environment.

PUC: As part of the Alternative Energy Portfolio Standard, PA utilities are required to explore energy efficiency measures prior to applying for capacity increases.

DCED: Currently runs PA’s WAP (Weatherization Assistance Program) and has contractors, auditors, and program administration in place.

PA Home Energy: A NPO-sponsored residential energy audit and performance evaluation program serving WPP utility customers.

ECA (Unnamed Program): Start-up program, similar to PA Home Energy serving Philadelphia and Pittsburgh metro areas.

Alternative Energy Investment Act: $92.5 million from this Act for residential and commercial energy efficiency activities and other initiatives.  A portion of this money will be integrated into the Keystone HELP Program and the PHFA.

Possible New Measure(s):  Offer Commonwealth residential sector an incentive for implementing whole-house performance, provide consumer and contractor education, create jobs, spur marketplace development, and significantly improve PA’s existing housing stock while reducing energy consumption and associated greenhouse gas emissions. Propose blending all existing programs and efforts, and applying for federal loan guarantees and special project funding, and seeking partnerships with utilities and others (manufacturers, contractors, NPO’s, etc…).

“Blending” could occur by working with the federal government and other PA agencies (and possibly utilities), with the intention of voluntarily partnering with the DEP to integrate these existing grant programs.

Projected 2025 Reduction (Million Metric Tons of CO2 Equivalents):

Projected emission reductions should be in the range of 20% to 30% from current levels. This program could save over 6.02 MMTCO2e by 2025 if implemented in all 5,250,000 PA housing units (approximately 308,824 homes per year).  Assumptions for this calculation include: a 30 year useful life of all building upgrades, achieving 100% implementation over a 17 year period, and counting reductions realized by weatherization actions taken by people on their own, independent of funding from this program.  These actions would be spurred by increased energy prices, and heightened awareness and education of the energy saving potential of home energy efficiency actions.

Economic Cost:  All these programs currently exist.  No new funding streams are anticipated in the short-term.  Cost savings resulting from decreased utility bills are likely to occur within the first year.

Additional funding (federal grants, sponsoring partners, state programs, etc..) and costs (program administration, staffing, etc..) would need to be further defined and established.

Implementation Steps:

Propose adding “green strings” to existing PA programs, adding DOE Title XVII loan guarantees and thereby reducing interest rates by ~0.5%.

Negotiate new contract with AFCFirst, PA Treasury, PHFA, and DCED based on a “home performance” funding model.

Possibly engage utility companies and others on ways to plug into the program, such as providing energy conservation packets to homeowners, or providing grants to train home performance contractors and/or grants to purchase home diagnostic equipment.

Additional implementation steps would need to be further defined and established.

Need to provide:

  - Customer assistance to identify which measures to deploy in order to optimize energy savings,

  - Certified building science professionals trained to properly identify and install the most cost effective energy-savings measures,

  - Quality assurance and control,

  - Funding for taking a whole-house approach,

  - Finance rates that truly provide incentives to consumers.

Potential Overlap:

Energy Audit Work Plan

Reduced Load Growth, Alternative Energy Investment Act, HB 2200, AEPS Tier I (@ 8%, 15%, 20%) Work Plans

Demand Side Management – Natural Gas Work Plan

# Leadership for State/Local and School Buildings

Benchmarking All Existing Commonwealth-Owned Facilities.

Lead Staff Contact:  	D. Maloskey / GGGC 787-8378

M. Hand / OETD 787-9377

Initiative Summary:  Require U.S. EPA Energy Star Portfolio Manager benchmarking for all Commonwealth of Pennsylvania (CWoPA) owned and leased facilities by 2009.  Establish a goal of minimum Energy Star rating of 75 for all CWoPA buildings by the year 2020.

Other Involved Agencies: DGS, PUC, All Commonwealth Agencies

Possible New Measure(s): Implement Energy Star benchmarking for all CWoPA buildings by 2009.  Meet at least an Energy Star score of 75 for all new and existing buildings by year 2020.

Projected GHG Reduction (Million Metric Tons of CO2 Equivalents):

Projected emission reductions should be in the range of 20% to 30% from current levels.

Economic Cost:  No added cost for benchmarking. If using the existing Guaranteed Energy Savings Act (GESA )/Energy Service Company (ESCO) contract process, a 2% to 4% increase in construction cost could be anticipated to allow for documentation and processing fees associated with obtaining Energy Star certification.  If CWoPA were to implement an in-house ESCO process, both processing and documentation costs could be significantly reduced.  Future operation costs would also offset initial capitol investment.

Implementation Steps: This program is currently underway due to a $500,000 grant with the U.S. Department of Energy.  The Department of General Services is building a benchmarking database and will be utilizing existing contract capacity with the Penn State Facilities Engineering Institute to begin the auditing/benchmarking process.   Other implementation steps could include:

- Develop Energy Star strategy work group, DGS, OETD and GGGC

- Revise facility manager job descriptions and train staff to incorporate benchmarking into their standard operating procedures.

- Revise GESA / ESCO language to incorporate Energy Star performance-based requirements.

- Mandate all FY 2009-2010 and future GESA / ESCO projects adopt the Energy Star performance-based requirements.

- Continue working with U.S. EPA to streamline work process and minimize costs associated with implementing Energy Star performance requirements into building operational procedures.

- PUC to develop and mandate all PA utilities conform to a uniform billing structure and format to allow automated billing data entry into Energy Star Portfolio Manager database.

- Develop / hire in-house staff to run program or educate existing qualified ESCOs on new requirements.

Potential Overlap:

Department of General Services

High Performance Building Standards for Existing Commonwealth Buildings

Other Commonwealth Government Initiatives

High Performance Building Standards for Existing Commonwealth of PA Buildings.

Lead Staff Contact:  	D. Maloskey / GGGC 787-8378

M. Guttman / GGGC 772-8948

Initiative Summary:  Require the equivalent to USGBC LEED-EB, Green Globes or other high performance building standards and U.S. EPA Energy Star ratings for all Commonwealth of Pennsylvania (CWoPA) owned and leased facilities.  Establish a goal of minimum LEED-EB Silver certification and an Energy Star rating of 75 for all CWoPA buildings by the year 2010.

Other Involved Agencies: DGS, All Commonwealth Agencies

Possible New Measure(s): Implement the equivalent to LEED-EB, Green Gloabes, etc., certification for ongoing operation and maintenance and Energy Star ratings for all Commonwealth buildings.  Meet at least the equivalent to LEED-EB Silver certification and an Energy Star score of 75 for all existing buildings by year 2020.

Projected GHG Reduction (Million Metric Tons of CO2 Equivalents):

Projected emission reductions should be in the range of 20% to 30% from current levels.

Economic Cost:  If using the existing Guaranteed Energy Savings Act (GESA) / Energy Service Company (ESCO) contract process, a 3% to 5% increase in construction costs could be anticipated to allow for documentation and processing fees associated with obtaining the equivalent to LEED and Energy Star certification.  If CWoPA were to implement an in-house ESCO process, both processing and documentation costs could be significantly reduced.  Future operation costs would also offset initial capital investments.

Implementation Steps:

- Continue LEED strategy work group, DGS and Governor’s Green Government Council (GGGC)

- Revise GESA / ESCO language to incorporate the equivalent to LEED-EB and Energy Star performance-based requirements.

- Complete the two (2) pilot projects (Governor’s Residence and RCSOB) – and mandate implementation of the policies developed in these pilot projects for ALL CWoPA facilities.

- Mandate all FY 2009-2010 and future GESA / ESCO projects adopt the equivalent of LEED-EB and Energy Star performance-based requirements.

- Continue working with USGBC and U.S. EPA to streamline work process and minimize costs associated with implementing LEED and Energy Star principles and performance requirements into building operational procedures.

- Develop / hire in-house staff to run program or educate existing qualified ESCOs on new requirements.

Potential Overlap:

Department of General Service

Most Electricity Sector Initiatives

Building Benchmarking

High Performance Pennsylvania Buildings

Lead Staff Contact:   GGGC - Maureen Guttman, AIA   717.772.8946

Summary: All Commonwealth owned or funded construction projects must meet a performance level equivalent to a minimum of LEED Silver plus an Energy Star rating of 85. (See HB 45, SB 672)

Other Involved Agencies:	DGS, DCED

Possible New Measure(s):  No LEED or equivalent high-performance building standard requirements exist.  The Dept. of Education offers additional reimbursement for school construction projects meeting LEED or Green Globe standards.  Several current legislative proposals based on this objective are being considered.

Potential GHG Reduction: All new state-funded construction would consume at least 25% less energy (approximately 25% less GHG emissions) than current building projects.

Economic Cost:  None, but may result in fewer capital projects being realized due to slightly increased capital costs.  If long-term operating and maintenance budgets can be borrowed from, overall cost impact should be negligible.

Implementation Steps:

Support legislative proposals, with possible amendments to achieve greater savings. Examples, special session House Bill 4 of 2008

Determine high-performance rating system to be used (LEED, Green Globes, other).

Modify DGS Architect/Engineer RFP/contract to require a higher standard of competency for design professionals performing state-funded design work.

Secure an agreement with developer of rating system (i.e. USGBC) for acceptance of portfolio standards for the state, reducing costs to register, certify and commission the projects.

Potential Overlap:

Department of General Services, Benchmarking State Buildings, Other Commonwealth Government reduction initiatives

Benchmarking All Existing PA Public PreK-12 Schools, AVTSs (Area Vocational Technical Schools) & CTCs (Career Technical Centers).

Lead Staff Contact: 		D. Maloskey / GGGC 787-8378

M. Hand / OETD 787-9377

Initiative Summary:  Implement Energy Star benchmarking for all public school buildings by 2010.  Meet at least an Energy Star score of 75 for all new and existing buildings by year 2020.

Other Involved Agencies: PDE, DGS, PUC

Possible New Measure(s): Require U.S. EPA Energy Star Portfolio Manager benchmarking for all Commonwealth of Pennsylvania (CWoPA) publicly owned and leased educational facilities by 2010.  Establish a goal of minimum Energy Star rating of 75 for all public school buildings by the year 2020.

Projected GHG Reduction (Million Metric Tons of CO2 Equivalents):

Projected emission reductions should be in the range of 20% to 30% from current levels.

Economic Cost:  No added cost for benchmarking. If using the existing GESA / ESCO contract process, a 2% to 4% increase in construction cost could be anticipated to allow for documentation and processing fees associated with obtaining Energy Star certification.  If CWoPA were to implement an in-house ESCO process, both processing and documentation costs could be significantly reduced.  Future operation costs would also offset initial capitol investment.

Implementation Steps:  The GGGC will continue to work with the PA School Board Officials and their newly formed Green Committee to develop this initiative.  Other implementation steps could include:

- Develop Energy Star strategy work group, PDE, DGS, OETD, PUC and GGGC

- Develop language for facility manager job descriptions and train staff to incorporate benchmarking into their standard operating procedures.

- Revise GESA / ESCO language to incorporate Energy Star performance-based requirements.

- Mandate all FY 2009 and future GESA / ESCO projects adopt the Energy Star performance-based requirements.

- Continue working with U.S. EPA to streamline work process and minimize costs associated with implementing Energy Star performance requirements into building operational procedures.

- PUC to develop and mandate all PA utilities conform to a uniform billing structure and format to allow automated billing data entry into Energy Star Portfolio Manager database (based upon California Assembly Bill 1103).

- Advocate and increase participation in the Build Green Schools initiative and the Green Schools Pledge.

Potential Overlap:

Department of General Service

High Performance Building Standards for Commonwealth facilities

Other State Government reduction initiatives

PASSHE Energy Consumption Reduction

Lead Staff Contact: 	Steven Dupes (717) 720-4118

Initiative Summary: In October of 2004, the Pennsylvania State System of Higher Education (PASSHE) established an internal goal to reduce energy consumption by 1.5% annually measured by an Energy Utilization Index (BTU consumed/SF of conditioned space).

Other Involved Agencies: None directly involved. DGS is involved with some of the initiatives to reduce consumption.

Possible New Measure(s): Since the benchmark year of 2003, the Universities have reduced their Energy Utilization Index by 12.3%, amounting to a cumulative $7.9 million of avoided energy costs since 2003.

Continue emphasis on existing efforts to reduce energy consumption through full implementation and seek new energy saving initiatives to meet or exceed the 1.5% annual EUI reduction goal.  The following are some of the tools available to achieve this goal:

Guaranteed Energy Saving Program

Energy manager staffing

Aggressive building operating system control

Behavioral changes

LEED and Energy Star efforts

Projected GHG Reduction (Million Metric Tons of CO2 Equivalents):

Guaranteed Energy Saving Program - 0.04MMTCO2e

Energy manager initiatives – 0.005MMTCO2e

Aggressive building operating system control - 0.005MMTCO2e

Behavioral changes - 0.02MMTCO2e

LEED and Energy Star efforts - 0.01MMTCO2e

Total Reduction: 0.8 MMTCO2e

Economic Cost:

Guaranteed Energy Saving Program.  Self funded, projected to be paid for by utility dollar savings.

Energy manager initiatives. Generally this position is self funded from initiatives implemented.  Estimated cost of the position with benefits is about $100,000 per university, or $1.4M total.

Aggressive building operating system control. Up to one-half of energy manager’s time can be spent in analyzing and manipulating building operating system controls to minimize energy usage.

Behavioral changes. To lead a campaign to effectively modify behaviors, outside consultants would most likely be required.  Estimated cost of these services is about $50K per year per campus. It is expected that energy savings generated by the changed behavior should cover the cost of the consultant services.

LEED and Energy Star efforts. Cost varies by project certification level. University use of LEED project standards is increasing.  Cost of these initiatives appears to range from about 5% to 15% of the total cost of construction.  Based on the typical annual construction program, this equates to a cost of $5 M to $15 M in initial construction costs; however, these costs should be recovered over the life of the project in reduced energy costs.

Implementation Steps:

Continue implementation of Guaranteed Energy Saving Act (GESA) projects.

- Currently, one university has completed a GESA project, three universities have projects in construction, and the remaining ten universities and the Dixon University Center are in the process of conducting investment grade audits.

- The GESA projects are expected to reduce energy consumption by about 20% for PASSHE.  This equates to about $10 million in annual energy savings through implementing energy compensation measures, including upgrades to lighting systems, heating and air conditioning systems, utility distribution systems and building system controls.

Increase utilization of campus Energy Managers.

- About one half of the PASSHE universities have established positions for energy managers. These positions are typically funded out of energy consumption and unit cost savings achieved through the work of the energy manager.

- Energy managers utilize the building control systems to aggressively manage the heating, ventilation and air conditioning systems (and sometimes lighting) to minimize energy consumption while maintaining an environment conducive to the university’s mission.

- Energy managers are also instrumental in managing and successfully implementing university GESA projects.

Aggressive building operating system control. Up to one-half of an energy managers time can be spent in analyzing and manipulating building operating system controls to minimize energy usage.

Behavioral changes. To effectively modify the behavior of the building occupants requires:  analysis of building level energy consumption, surveying occupants to identify behaviors and motivators, and developing a plan to modify behaviors and educate where the occupants are motivated to participate. This process must be repeated and adjusted continuously to ensure momentum is not lost through the significant turnover of students.

LEED and Energy Star efforts.

- Continue to evaluate projects on a case by case basis for application of LEED and/or Energy Star standards.

- Attempt to increase funding available for capital projects to avoid the initial cost limitations of projects over the preferred project life cycle cost.

Potential Overlap:

Department of General Services

Most Electricity Sector initiatives

# Lighting

Re-Light Pennsylvania

Strategy Name: Re-Light Pennsylvania

Lead Staff Contact: Maureen Guttman (717-783-8411)

Summary:  This initiative is a critical building technology that accelerates replacement of less efficient outdoor and indoor lighting systems, including maximizing use of daylighting in indoor settings.  It applies to residential and commercial buildings as well as parks, street lights and parking facilities.

Other Involved Agencies:

Possible New Measure(s):

Potential GHG Reduction:

Economic Cost:  $ million savings

Implementation Steps:

Potential Overlap:

Expand Energy Efficiency Funds

Strategy Name: Expand energy efficiency funding

Lead Staff Contact: Maureen Guttman (717-783-8411)

Summary:  This initiative would institute public benefit funds for investment in residential, commercial and industrial energy efficiency and renewable energy programs through third-party administrators.

Other Involved Agencies: PA Utilities Commission

Possible New Measure(s):

Potential GHG Reduction:

Economic Cost:  $ million savings

Implementation Steps:

Potential Overlap:

Increase Lighting Efficiency Standards

Strategy Name: Increase lighting efficiency standards

Lead Staff Contact: Maureen Guttman (717-783-8411)

Summary:  This initiative would adopt legislation to prescribe a minimum level of operating efficiency for lighting devices by specified dates.  The goal of the legislation is to phase out less efficient lighting devices (i.e. incandescent bulbs) with lighting devices that meet a minimum standard in lumens per watt.

Other Involved Agencies: Department of General Services

Possible New Measure(s):

Potential GHG Reduction:

Economic Cost:  $ million savings

Implementation Steps:

Potential Overlap:

# Appliance Standards

Federal Appliance Standards

Lead Staff Contact: Libby Dodson (717) 772-8907

Initiative Summary:  Emissions reductions realized from the minimum energy efficiency appliance standards established by the 2005 and 2007 federal energy bills.

Other Involved Agencies: N/A

Possible New Measure(s): N/A

Projected 2025 Reduction (Million Metric Tons of CO2 Equivalents): According to ACEEE data, the appliance standards established by the 2005 EPAct will translate into emissions reductions of 1.76 MMTCO2e in 2025.  These reductions are related to energy efficiency improvements for the following categories of appliances: bottle-type water dispensers, compact audio products, DVD players and recorders, metal halide lamp fixtures, portable electric spas (hot tubs), residential furnaces and boilers, single-voltage external AC to DC power supplies, state-regulated incandescent reflector lamps, and walk-in refrigerators and freezers.

Additional reductions will be realized through the implementation of the enhanced energy efficiency standards established in the Energy Independence and Security Act of 2007.  The emissions reductions associated with these new standards are being calculated by ACEEE, and should be made available by the end of 2008.

Economic Cost:	N/A

Implementation Steps:  	N/A

Potential Overlap:

Reduced Load Growth, HB 2200, Alternative Energy Investment Act, AEPS Tier I @ 8%, 15% and 20%, Work Plans

Demand Side Management – Natural Gas Work Plan

Appliance Standards

Strategy Name: Appliance standards

Lead Staff Contact: Maureen Guttman (717-783-8411)

Summary:  This initiative establishes efficiency standards for appliances and lighting devices that are not addressed by the federal government.

Other Involved Agencies:

Possible New Measure(s):

The efficiency standards apply to all appliances or lighting devices that are commercially available and have measurable energy savings potential, including the following:

Dry-type transformers

Refrigerators and freezers

Exit signs

Traffic signals

Touchier lamps

Large air conditioning units greater than 20 tons

Unit heaters

Clothes washers

Potential GHG Reduction:

Economic Cost:  $ million savings

Implementation Steps:

Potential Overlap:

# Distributed Energy

Renewable Heating and Cooling with Geothermal Infrastructure

Strategy Name: Renewable Heating and Cooling with Geothermal Infrastructure

Lead Staff Contact: Vivian Loftness, 412-268-1539

Summary: Pennsylvania’s rich water resources are not used to any extent as a strategic approach to reducing energy consumption and carbon emissions.  Water, however, is a superb energy carrier and, in geothermal heating and cooling, allows us to tap the renewable energy stored in the earth just below frost line.  According to the US Department of Energy, geothermal heating and cooling can save 30-60% over conventional combustion-based heating and electric chillers or air conditioners and can reduce carbon emissions by a similar amount.

All of the historic towns and cities in the Commonwealth were founded on top of and adjacent to water resources.  Development of community-based (district) geothermal infrastructure (e.g., Warren PA municipal geothermal system) will support economic redevelopment while simultaneously reducing energy consumption and lowering carbon emissions.  Where district systems are not feasible, geothermal outfitting or retrofitting of individual buildings will provide similar benefits, for the near term and for a sustainable future.

Other Involved Agencies:

Department of Community & Economic Development

Possible New Measure(s):

- Map/identify potential sources of water: unused old wells that would still be productive, water-filled mine tunnels, surface water, recycled gray water, sewage treatment plant effluent, retention basin storm water, harvested rainwater, and water from a subsurface aquifer

  - Consider ways in which overload on existing stormwater network might be eased by district HVAC loops

  - Consider ways in which co-located process water within a community might be integrated into district water loop system

    - Develop/assist in developing community water resource database/diagrams

- Loan/matching program for community-based infrastructure

- Formation of regional/community electronic cooperatives to support infrastructure development (based on current USDA program that supports rural electric cooperatives for installation of geothermal systems).

Potential GHG Reductions: [Had only electricity conversion factor for carbon emissions at hand, so these estimates are based only on the fraction of heating and cooling energy assumed to be electricity and are therefore very conservative. All assumptions stated]

If 10% of conventional systems could be displaced/converted to geothermal heating and cooling, estimated carbon emissions reduction (based on 2006 energy consumption data from EIA State Energy Data System), would conservatively be:

Commercial Sector: 794,250 tons CO2/year

Residential Sector: 89,335 tons CO2/year

Additional conversion/displacement in subsequent years would be additive.

Assumptions for commercial savings:

Based on the 2006 EIA State Energy Data System, annual energy consumption in Pennsylvania’s commercial sectors is 687.8 trillion BTUs or 201,525,400 MWH (source energy).  Heating and cooling represent approximately 35% of that consumption (70.5 million MWH), and it is provided by a variety of fuels with a mix of carbon emissions coefficients.  For this calculation, one-half of that amount was assumed to be electricity (35.3 MWH) and the carbon emissions were calculated for that portion only since the US average conversion rate for electricity production is known.  Assuming that geothermal heating and cooling could replace 10% of the current technology, saving 45% of the associated heating and cooling electricity consumption (0.45 x 3.53 MWH) and that there are 0.5 tons of carbon emissions per MWH of heating and cooling electricity, then 794,250 tons CO2/year could conservatively be saved with this strategy.

Assumptions for residential savings:

Based on the 2006 EIA State Energy Data System, annual energy consumption in Pennsylvania’s residential buildings sectors is 912.6 trillion BTUs or 267,391,800 MWH (source energy)  .  Approximately 45-50% of that consumption is energy for heating and cooling (120.3 million MWH) and it represents a variety of fuels, with a mix of carbon emissions coefficients.   For this calculation, only one-third of that amount was assumed to be electricity (39.7 million MWH) and the carbon emissions were calculated for that portion only since the average conversion rate for electricity production is known.

Assuming that geothermal heating and cooling could replace 10% of the current technology, saving 45% of the associated heating and cooling electricity consumption (0.45 x 3.97 MWH) and that there are 0.5 tons of carbon emissions per MWH of heating and cooling electricity, then 89,325 tons CO2/year could conservatively be saved with this strategy.

Economic Cost:

Implementation Steps:

Potential Overlap:

DCED Renewable Energy Program: Geothermal and Wind Projects (Jan. 2009)

Potential Complimentarity: Potential integration with DOE/Oak Ridge National Laboratory’s interest in extending/funding infrastructure for geothermal heating and cooling.  December 2008 report available at

Promote Combined Heat and Power

Note: Moved to Energy Supply

Strategy Name: Promote combined heat and power (CHP)

Lead Staff Contact: Maureen Guttman (717-783-8411)

Summary:  This initiative encourages CHP systems to reduce fossil fuel use and GHG emissions.  Reductions are achieved through the improved efficiency of CHP systems, relative to separate heat and power technologies, and by avoiding transmission and distribution losses associated with moving power from central generation stations to distant locations where electricity is used.

Other Involved Agencies:

Possible New Measure(s):

Promote use of natural gas-fired CHP.

Promote use of biomass-fired CHP.

Create or expand markets for CHP units by incentives designed to promote implementation for residential, commercial and industrial users.

Promote CHP technologies through provisions for tax benefits, attractive financing, utility rebates and other incentives.

Remove barriers to CHP development, such as utility rate structures that allow discounted electric rates to compete with CHP.  Also, interconnection standards should be designed to facilitate economical and efficient CHP connection to the grid.

Consider the economic and environmental benefits of CHP as a resource in each electric utility’s Integrated Resource Plan.  Potential measures include training and certification of installers and contractors; net metering and other pricing arrangements; clear and consistent interconnection standards; and creation and support for biomass fuel markets.

Potential GHG Reduction:

Economic Cost:  $ million savings

Implementation Steps:

Potential Overlap:

PA Promotes Building-Integrated Photovoltaics (BIPV), Solar Thermal, Micro Hydro, and Micro Wind

Note: Moved to Energy Supply

Strategy Name:  PA Promotes Building-Integrated Photovoltaics (BIPV), Solar Thermal, Micro Hydro, and Micro Wind

Submitting Organization Contact:  	Jenna Cramer, Program Specialist, Green Building Alliance, Pittsburgh, PA, (412) 431-0709 x6005 or jennac@gbapgh.org

Summary:  Promotion of building-integrated photovoltaics, solar thermal, micro hydro, and micro wind in order to reduce greenhouse gas emissions from conventional fuel sources, improve efficiency of electricity delivery, lower utility bills, and drive local economic development.

Other Involved Agencies:  Department of Energy, Environmental Protection Agency, PA Department of Environmental Protection, The Pennsylvania Public Utility Commission, Solar Energy Industries Association, Department of Community and Economic Development, local utilities, labor unions

Possible New Measure(s):  Encourage widespread adoption of building-integrated photovoltaics, solar thermal, micro hydro, and micro wind in order to reduce greenhouse gas emissions from conventional energy sources, improve efficiency of electricity delivery, lower utility bills, and drive local economic development.

These renewable energy systems can generate electricity, provide hot water, as well as heat, cool, and light buildings, thus reducing energy costs and emissions from conventional fuel sources.  When buildings are able to generate power on-site or locally, it produces and delivers energy more efficiently and reduces the demand on larger electricity grids.

The design, installation, and maintenance of these renewable energy systems will require a new workforce of trained professionals, thus creating green jobs. The local economy can also benefit from continued research and development of renewable energy technologies, as well as the manufacturing, service, and sale of associated products.

Potential GHG Reduction: 	According to the U.S. Green Building Council, buildings account for 48% of all GHG emissions and 39% of carbon dioxide emissions in the United States.  Generating power on-site from renewable resources reduces the use of conventional fuel sources for generating electricity, heating water, and heating, cooling and lighting buildings, thus reducing GHG emissions.  The quantity of GHG reduction will depend on the scale at which the program is implemented.

Economic Cost:  The upfront cost of installation of these renewable energy systems can be offset with financial incentives from the government.  The long-term financial incentive for buildings to generate their own energy is reduced utility costs.  There is also a cost associated with implementing training programs for the new workforce.  The growth of green jobs and possible manufacturing and sale of products can generate revenue for the local economy.

Implementation Steps:  Implementation of this program would include state and municipal legislation coupled with financial incentives.  Examples include the following:

Strategically analyze the Commonwealth’s buildings to determine viable candidates for installation of renewable energy generation systems based on the current energy efficiency of the buildings

Regulatory policies, such as requiring utilities to purchase excess energy produced

Financial incentives to reduce first cost

Financing, including low interest rates and preferred loan programs

Consumer and workforce education programs for system installation and maintenance

Incentives for development of local renewable energy industry infrastructure

Potential Overlap / Synergies:

Reglaze PA: Window/Skylight Upgrades: High Thermal, Solar, and Optical Performance

PA Renewables; Incentivize Remove ‘Grid’ Barriers

PA enables Smart Grid/Micro Grid Infrastructure

PA values embodied energy in building materials, including historic structures

Turn it off PA campaign: unnecessary heating, cooling, lighting

Shade PA: Cool Buildings and Cool Communities

Weatherize PA: Air Tightness & Insulation: Reduce enclosure heat loss/heat gain

PA institutes water and energy budgets

Solar Rights Initiative

Note: Moved to Energy Supply

Strategy Name: Solar Rights Initiative

Lead Staff Contact: Maureen Guttman (717.772.8946)

Initiative Summary:  In order to enable and facilitate energy efficiency and renewable energy generation, the Commonwealth will prohibit Homeowners Associations (HOA) or municipalities from preventing outdoor clothes drying or installation of solar panels.

Other Involved Agencies: L&I

Possible New Measure(s): The Commonwealth supports legislation modeled after Florida’s Solar Rights Law  (Section 163.04, Florida Statute).  Inter alia, this statute prohibits the adoption of an ordinance by a governing body, which prohibits or has the effect of prohibiting the installation of solar collectors, clotheslines, or other energy devices based on renewable resources.  Furthermore, it states that no deed restrictions, covenants, or similar binding agreements running with the land shall prohibit or have the effect of prohibiting solar collectors, clotheslines, or other energy devices based on renewable resources from being installed on buildings erected on the lots or parcels covered by the deed restrictions, covenants, or binding agreements.

Projected 2025 Reduction (Million Metric Tons of CO2 Equivalents): Not Quantified

Economic Cost: No Cost to the Commonwealth

Implementation Steps:

Develop a piece of legislation

Proceed through the rulemaking process

# Demand Side Management (DSM) - Gas

Demand Side Management (DSM) - Gas

Lead Staff Contact: Mark Hand (717)787-9377

Summary:  Replacing or upgrading inefficient household appliance that utilize natural gas with more energy efficient models.

Other Involved Agencies: N/A

Possible New Measure(s): Average annual consumption of Natural Gas (NG) from 2000 through 2006:   				140,747 MMcf (million cu. ft.)

Total PA Electric Costumers = 		4,146,011

Total PA Customers using NG for heating =	2,062,693

Total PA Customers using NG for other = 	182,959

1. Air Sealing and Insulation (10-40% annual energy savings)

Pennsylvanians using NG for heating use about 600 therms per household.

Assumptions: By air sealing & insulation, consumers could probably easily save ¼ of this.  ½ of total heating-household may be able to participate.

150 Therms/heating-household X 1,031,347 households= 154,701,975 Therms X 100,000 Btus/1,000,000 Btus = 15,470,198 million Btus X 117.08 lbsCO2/million btu = 1,811,250,723 lbsCO2 /2,000 lbs = 905,625 tonsCO2 X .907= 821,402 metric tons of CO2= .82 MMTCO2e *

* This calculation is an underestimate of potential reductions because it only assumes winter heating savings from Natural Gas. There will also be summer air conditioning savings (not calculated in this assessment for NG).

2. Increase furnace and boiler efficiency from x to >95 AFUE .

Nationwide and in PA, about 50% of homes use NG for heating.

The minimum allowed AFUE rating for a non-condensing, fossil-fueled, warm-air furnace is 78%; the minimum rating for a fossil-fueled boiler is 80%; and the minimum rating for a gas-fueled steam boiler is 75%.

Although older furnace and boiler systems had efficiencies in the range of 56%-70%, modern conventional heating systems can achieve efficiencies as high as 97%, converting nearly all the fuel to useful heat for your home.  Energy efficiency upgrades and a new high-efficiency heating system can often cut your fuel bills and your furnace’s pollution output in half.  Upgrading your furnace or boiler from 56% to 90% efficiency in an average cold-climate house will save 1.5 tons of carbon dioxide emissions each year if you heat with gas, or 2.5 tons if you heat with oil.  (DOE, Energy Savers)

Therefore consumers could expect to see a range in energy savings from 15 to 50%  “heating season” improvements (depending on age and efficiency of equipment being replaced).  Using the same assumptions for #1 above (150 therms per household), this measure may expect to see similar or higher MMTCO2e results (for Natural Gas).  However, the CO2 advantage for “air sealing and insulating” is due to the additional electric savings from the summer air conditioning season.

= .82 MMTCO2e

3. Solar domestic hot water heaters

Heating water accounts for 14-25% of total household energy consumption. Solar water heaters can provide 85% of DHW needs.

The calculated avoided emissions below are a very rough approximation of savings for this measure.  Assumptions:

  - Approximately 130 Therms per household saved ¼ of the total households (heating & non-heating customers) may have adequate solar exposure for solar thermal applications.

0.25(2,062,693+182,959) = 561,413 households.

130 Therms/household X 561,413 households= 72,983,690 Therms X 100,000 Btus/1,000,000 Btus = 7,298,369 million Btus X 117.08 lbsCO2/million btu = 854,493,042 lbsCO2 /2,000 lbs = 427,247 tonsCO2 X .907= 387,513 metric tons of CO2= .39 MMTCO2e

4. Instantaneous hot water heaters with an Energy Factor > .80

For homes that use 41 gallons or less of hot water daily, demand water heaters can be 24% to 34% more energy efficient than conventional storage tank water heaters.

They can be 8% to 14% more energy efficient for homes that use a lot of hot water – around 86 gallons per day.  You can achieve even greater energy savings of 27% to 50% if you install a demand water heater at each hot water outlet.

Assumptions:

  - Approximately 150 therms per household for water heating. This measure may save 25% or 38 therms /household.

  - 1/2 of the total households (heating & non-heating customers) may be able to participate.  0.50(2,062,693+182,959) = 1,122,826 households.

38 Therms/ household X 1,122,826 households = 42,667,388 Therms X 100,000 Btus/1,000,000 Btus = 4,266,739 million Btus X 117.08 lbsCO2/million btu = 499,549778 lbsCO2 /2,000 lbs = 249,775 tonsCO2 X .907= 226,546 metric tons of CO2= .23 MMTCO2e

5. Use ENERGY STAR front-loading washing machines.

Most ENERGY STAR qualified washers extract more water from clothes during the spin cycle. This reduces the drying time and saves energy and wear and tear on your clothes.

ENERGY STAR qualified clothes washers clean clothes using 50% less energy than standard washers (including energy used in the washing process, including machine energy, water heating energy, and dryer energy).

Assumptions

  - Natural gas clothes dryers may use around 42 therms per year. Assume front loading washing machines will save 25% of the drying energy or 10.5 therms per household.

  - Assume ½ of total households may be able to participate, 0.50(2,062,693+182,959)= 1,122,826 households.

10.5 Therms/ household X 1,122,826 households= 11,789,673 Therms X 100,000 Btus/1,000,000 Btus = 1,178,967 million Btus X 117.08 lbsCO2/million btu = 138,033,491 lbsCO2 /2,000 lbs = 69,017 tonsCO2 X .907= 62,598 metric tons of CO2= .06 MMTCO2e

6. Pilot Lights

Standing pilot lights may use over 7 therms (700,000 btus) of gas per appliance, if left on year round.

Removing old appliances that have pilot lights on full time with appliances that have electronic (intermittent) ignitions could create savings.

Some people feel that standing pilot lights on appliances are gradually becoming the exception, instead of the rule, with new appliances on the market using electronic ignitions.  However, even though electronic ignition pilot lights are becoming increasingly common, without legislation, standing pilots may not disappear by 2025 because they are cheaper to manufacturer, and the appliance is sometimes viewed as solution to emergency heat when the electric goes out, because they do not need electric to start.

Assumptions:

  - Assume that 1/4 of the natural gas heating households has at least one appliance with a standing pilot light.

561,413 households X 7 therms = 3,929,891 therms X 100,000 Btus/1,000,000 Btus = 392,989 million Btus X 117.08 lbsCO2/million btu = 46,011,163 lbsCO2 /2,000 lbs = 23,005 tonsCO2 X .907= 20,866 metric tons of CO2= .02 MMTCO2e

Potential GHG Reduction:	2.34 MMTCO2e

The GHG calculated savings are based on limited data on PA residential gas consumption. Many estimations and assumptions were used and the GHG reduction results should be further validated for accuracy.

Cost:  Costs vary significantly between each recommended measure.  Some upfront costs are considerable, while others are nominal.  If a new energy efficient appliance were purchased to replace a broken appliance, the costs would have been incurred regardless of the energy efficiency decision.  In this scenario, depending on the product, a price premium may exist for increased efficiency appliances.  If an energy efficient appliance was bought to replace an inefficient, but still functioning appliance, the cost borne by the consumer will be greater.  In both scenarios, long-term costs savings from reduced utility bills are likely to occur.

Implementation Steps:

Market driven

Encourage natural gas utilities to engage in consumer education initiatives regarding these efficient technologies.

Potential opportunity for appliance efficiency legislation

Potential Overlap:

Reduced Load Growth Work Plan

HB 2200 Work Plan

Appliance Standards Work Plan

Alternative Energy Investment Act Work Plan

Others

# Water Conservation

Water Conservation

Strategy Name: Water Conservation

Lead Staff Contact: Maureen Guttman (717-783-8411)

Summary:  This initiative supports water conservation and yields energy savings.    To achieve 25% potable water conservation, enact new utility incentives, conservation credits, smart metering and education programs.  The energy impact of water use is estimated as 4% of all electricity consumption nationwide.

Other Involved Agencies:

Possible New Measure(s):

Potential GHG Reduction:

Economic Cost:  $ million savings

Implementation Steps:

Potential Overlap:

# Department of General Services (DGS) – Initiative to Reduce Energy Use by State Government

Need workplan

# B5 Bioheat Initiative

B5 Bioheat Initiative

Lead Staff Contact: Joe Sherrick (717-772-8944)

Summary:  This initiative aims to blend all heating oil sold in PA with a 5% blend of biodiesel.

Other Involved Agencies:  Department of Welfare

Possible New Measure(s): Replace five percent of heating oil with biodiesel.  Bioheat is the industry term for heating oil that is blended with biodiesel.  Heating oil is essentially the same as diesel with some difference in sulfur content and a colorant added to deter tax evasion through its potential use as a transportation fuel.  The use of Bioheat has been proven to reduce maintenance concerns and burns cleaner than conventional heating oil.  Significant, positive experience utilizing Bioheat exists.  Numerous customers throughout southcentral and southeastern PA have been using Bioheat in their furnaces and boilers for the past few years.  The state Department of General Services also has Bioheat on contract for state agencies.

Potential GHG Reduction: 			0.42 MMTCO2e

According to EIA data, as provided in the Petroleum Navigator, PA’s total annual heating oil consumption in 2007 was 929,363,000.  Using the same data source, a long-term (1983 through 2007) trend was established.  That trend reflects a 2.12% annual average decline for heating oil consumption in PA.  This same trend was applied to all years out to 2025.

A lifecycle analysis approach was used in comparing the GHG emissions of conventional heating oil versus Bioheat (5% biodiesel).  The same lifecycle standard for biodiesel, as specified in the federal renewable fuels standard, was incorporated in this analysis.  Implementing a requirement for all heating oil sold in PA to contain 5% biodiesel would: reduce GHG emissions by 0.42 MMTCO2e, further reduce our dependence on foreign oil by nearly 32 million gallons of heating oil and bolster the markets for PA-based biodiesel producers.  The attached tables reflect the data used in these calculations.

The State of Maryland recently enacted a three cents per gallon tax credit towards the purchase of all Bioheat that contains at least 5% biodiesel in every gallon of heating oil.  Such an incentive would address a cost premium, when and if one exists.  A similar incentive program could be considered in PA as a means to offset any potential premium.

Economic Cost:

Cost to DEP? – No direct costs; potential implementation costs if supporting legislation were passed

Cost to the Commonwealth? - No direct costs; potential implementation costs if supporting legislation were passed

Cost to regulated community or consumer?

  - According to the EIA’s 2001 Residential Energy Consumption Survey, the average annual home consumption of fuel oil is 469 gallons.  If any cost premium exists for the blending of biodiesel into heating oil it is estimated to be in the range of 0 – 5 cents per gallon or $0 - $23.45 more per year per household.  It’s also very possible that costs savings may be realized, particularly as petroleum prices increase.

Are there Federal funds available? N/A

Do these costs fund other programs? N/A

Are cost savings realized from this initiative?

  - Possible.  Cost savings may be realized as the price of petroleum increases.

Implementation Steps:  Representatives from the Northeast Regional Biomass Program, including PA, have been working in association with oil heat industry representatives to promote greater awareness and acceptance of Bioheat among both customers and distributors.  Further discussions should occur between the Departments of Public Welfare, the Office of Consumer Advocate and the DEP so that all are aware of potential economic considerations in implementing such an initiative.  Implementation would require legislative action.  Adequate injection blending facilities would need to be in place around the state to support this measure.

Potential Overlap:

Biofuels Investment and In-State Production Act

| Projected Heating Oil Consumption and Associated B5 Bioheat Requirements |  |  |
| --- | --- | --- |
| Year | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 |  |  |  |
| #2 Heating Oil | 929,363,000 | 909,673,787 | 890,401,704 | 871,537,914 | 853,073,766 | 835,000,795 |  |  |  |
| Biodiesel for B5 Bioheat | 46,468,150 | 45,483,689 | 44,520,085 | 43,576,896 | 42,653,688 | 41,750,040 |  |  |  |
| Year | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 |  | Lifecycle GHG Impact in 2025 |
| #2 Heating Oil | 817,310,712 | 799,995,406 | 783,046,937 | 766,457,534 | 750,219,588 | 734,325,655 |  |  |
| Biodiesel for B5 Bioheat | 40,865,536 | 39,999,770 | 39,152,347 | 38,322,877 | 37,510,979 | 36,716,283 |  | Fuel | MMTCO2e |
|  |  |  |  |  |  |  |  | Heating Oil | 8.26 |
| Year | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | B5 Bioheat | 7.84 |
| #2 Heating Oil | 718,768,446 | 703,540,828 | 688,635,818 | 674,046,581 | 659,766,427 | 645,788,808 | 632,107,315 | Delta | 0.42 |
| Biodiesel for B5 Bioheat | 35,938,422 | 35,177,041 | 34,431,791 | 33,702,329 | 32,988,321 | 32,289,440 | 31,605,366 |  |  |
| Baseline consumption data for PA is from EIA's Petroleum Navigator (see link below). |
| http://tonto.eia.doe.gov/dnav/pet/pet_cons_prim_dcu_SPA_a.htm |  |  |

| Diesel* Production GHG Lifecycle Assessment (LCA) (Includes Production-Related GHGs & Finished Fuel Carbon Content, Expressed as CO2e/Gallon) |
| --- |
|  | CO2 | CH4 | N2O | Total CO2e | Carbon Content (Lbs CO2/Gal.) | Total LCA (Lbs. CO2e/Gal.) |
| G/MMBTU | 20,142 | 109.1 | 0.343 |  |  |  |
| MMBTU per Gallon | 0.1284 | 0.1284 | 0.1284 |  |  |  |
| GWP | 1 | 23 | 296 |  |  |  |
| CO2e | 2586.23 | 322.19 | 13.04 | 6.44 | 22.38 | 28.82 |

`Biomass-Based Diesel' means renewable fuel that is biodiesel as defined in section 312(f) of the Energy Policy Act of 1992 (42 U.S.C. 13220(f)) and that has lifecycle greenhouse gas emissions, as determined by the Administrator, after notice and opportunity for comment, that are at least 50 percent less than the baseline lifecycle greenhouse gas emissions. Notwithstanding the preceding sentence, renewable fuel derived from co-processing biomass with a petroleum feedstock shall be advanced biofuel if it meets the requirements of subparagraph (B), but is not biomass-based diesel.

# Utility Incentives for Demand-Side Management

Utility Incentives for Demand-Side Management

Strategy Name:  Utility incentives for demand-side management

Lead Staff Contact:  Joseph Sherrick (717-705-0372)

Summary:   Amplify the future impacts of utility demand-side management programs by removing the financial disincentives to program success which are characteristic of traditional ratemaking practices, developing rate decoupling and related rate redesigns and/or positive performance incentives to spur higher levels of energy savings and GHG reductions.

Other Involved Agencies:  PUC, state legislature

Possible New Measure(s): This strategy builds upon the energy efficiency and conservation program   of Act 129 / House Bill 2200 which mandates the introduction of utility demand-side management (DSM) programs.  States which have the most successful energy efficiency programs, i.e., those which achieve superior rates of electric energy savings, tend on the whole to have adopted incentives for utilities.  An analysis of state-level data from across the nation indicates a pronounced relationship between the use of incentives and reductions in annual electricity sales.  States which were the most aggressive, employing both performance incentives as well as rate decoupling, achieved savings rates 3.2-fold higher than the scale achieved in states with no DSM incentives (such as Pennsylvania). The following table illustrates this relationship.

Table 1

Relationship Between Reduced Statewide Electricity Sales

And Use of Utility DSM Incentives

| State Approach to Electric Efficiency Incentives | Average Incremental Savings in Electricity Use |
| --- | --- |
| No incentives | 0.19% |
| Performance incentives only | 0.34% |
| Rate decoupling only | 0.34% |
| Both performance incentives and decoupling | 0.60% |

Traditional ratemaking impedes full utilization of energy efficiency opportunities by eroding utility revenues as these programs are implemented. The linkage between efficiency, energy sales and utility financial margins arises from rate designs which make utility profits dependent upon sales volume, and which fail to provide returns on efficiency investments comparable to those realized by investments in traditional capacity.

Mechanisms for addressing the financial impacts to utilities include performance target incentives, shared savings incentives, and rate-of-return adders, as well as rate decoupling to address both lost margin recovery and the throughput incentive.  In-depth discussions of these issues and regulatory approaches can be found in the references cited at the end of this workplan.

The need to reformulate utility incentives and disincentives is gaining increasing scrutiny in states across the nation that are seeking more effective strategies for accelerating energy efficiency utilization. Each of the top performing states now use some form of incentives for DSM. This trend is on the rise.  Today, more than half the states (29) use some form of financial incentives for DSM.  As state investments in energy efficiency programs increase, the attention to appropriate price signals for DSM is likewise growing.

Potential GHG Reduction: 	5.89  MMTCO2 additional

These computations estimate net incremental impacts of instituting utility incentives and thus represent the increased effectiveness of DSM programs implemented within a framework that addresses existing barriers created by current ratemaking practices.

The following steps were used in calculating the emissions reduction:

For consistency with other work plans, this analysis is based upon the same forecast of statewide electrical sales used in the Reduced Load Growth and AEPS work plans, looking at a period beginning with 2009 and concluding with 2025.

Impacts from the addition of the utility incentives were calculated using the difference between the no incentives and the most aggressive performance incentives figures from Table 1.  This is a rate of reduction of statewide electrical sales of 0.41%.  This is the newly realized savings resulting from market actions taken within the reporting year and so represents new impacts from a single year’s incremental activity in the DSM programs.

The annualized energy impacts associated with incentives was then multiplied by the statewide CO2 emission factor (1,279 pounds of CO2 per MWh) calculated by DEP for electricity produced in PA (short tons were converted to MMT).

Assumptions:

Assumes the necessary enabling legislation is not passed until 2010, with implementation subsequently beginning in 2011.

Assumes the institution of both revenue decoupling and supplemental performance incentives for maximum effect.

Assumes three years to ramp up to full impact, and equal increments of improvement in each year from 2011 to 2013 when full-scale impact is assumed to reach 0.41% annually.

Additive impacts over the analysis timeframe.

This estimate of impacts assumes that Pennsylvania proceeds with both rate decoupling and positive performance incentives on a statewide basis.  Other approaches are possible, such as pursuing either decoupling or performance incentives singly. Implementation could also be initiated on a pilot basis, for example as legislated in the state of Minnesota, with a corresponding decrease in overall impacts.

Economic Cost:

Cost to DEP – None

Cost to the public - Net benefit to ratepayers and utilities alike.  The magnitude of benefits realized will vary with the incentives and programs adopted.

Implementation Steps:

Enabling legislation is needed

The PUC will need to determine the specific form of incentives to be used

Potential Overlap:

Reduced Load Growth

| PROJECTED IMPACTS OF DSM PROGRAM INCENTIVES |
| --- |
| Year | Elec Sales | Programmatic Impact | Incremental GHG Impact | Cumulative GHG Impacts | Cumulative GHG Impacts |
|  | (MWh) | (MWh) | (Tons CO2) | (Tons CO2) | (MMT CO2) |
| 2009 | 151,928,332 |  |  |  |  |
| 2010 | 154,334,271 |  |  |  |  |
| 2011 | 156,781,428 | 214,791 | 137,359 | 137,359 | 0.12 |
| 2012 | 159,270,547 | 434,809 | 278,060 | 415,419 | 0.38 |
| 2013 | 161,802,389 | 663,390 | 424,238 | 839,657 | 0.76 |
| 2014 | 164,377,726 | 673,949 | 430,990 | 1,270,647 | 1.15 |
| 2015 | 166,997,346 | 684,689 | 437,859 | 1,708,506 | 1.55 |
| 2016 | 169,662,052 | 695,614 | 444,845 | 2,153,351 | 1.95 |
| 2017 | 172,372,662 | 706,728 | 451,953 | 2,605,304 | 2.36 |
| 2018 | 175,130,010 | 718,033 | 459,182 | 3,064,486 | 2.78 |
| 2019 | 177,934,944 | 729,533 | 466,537 | 3,531,022 | 3.20 |
| 2020 | 180,788,329 | 741,232 | 474,018 | 4,005,040 | 3.63 |
| 2021 | 183,691,047 | 753,133 | 481,629 | 4,486,669 | 4.07 |
| 2022 | 186,643,996 | 765,240 | 489,371 | 4,976,040 | 4.51 |
| 2023 | 189,648,091 | 777,557 | 497,248 | 5,473,288 | 4.96 |
| 2024 | 192,704,264 | 790,087 | 505,261 | 5,978,549 | 5.42 |
| 2025 | 195,813,466 | 802,835 | 513,413 | 6,491,962 | 5.89 |
| Cumulative Impact | 47,137,299 | 42.75 |

SOURCES OF FURTHER INFORMATION

American Council for an Energy Efficient Economy, the 2008 State Energy Efficiency Scorecard, October 2008.

American Council for an Energy Efficient Economy, Aligning Utility Interests with Energy Efficiency Objectives: A Review of Recent Efforts at Decoupling and Performance Incentives, October 2006.

ICF International, Utility Performance Standards, Oversight, and Cost Recovery, Briefing for the Maryland Energy Administration, September 2007.

National Association of Regulatory Utility Commissioners, Decoupling for Electric & Gas Utilities: Frequently Asked Questions, September 2007.

Regulatory Assistance Project, Energy Efficiency Policy Toolkit, January 2007.

Regulatory Assistance Project, Overview of Utility Incentives, Presentation to the New Mexico Public Regulation Commission, July 2008.

Regulatory Assistance Project, Revenue Decoupling Standards and Criteria, Report to the Minnesota Public Utilities Commission, June 2008.

USEPA and USDOE, Aligning Utility Incentives with Investment in Energy Efficiency, A Resource of the National Action Plan for Energy Efficiency, November 2007.

# Footnotes

A zero-carbon house is a building where net carbon dioxide emissions resulting from all energy used in the dwelling are zero or better. This includes the energy consumed in the operation of the space heating/cooling and hot-water systems, ventilation, all internal lighting, cooking and all electrical appliances.

http://www.eia.doe.gov/emeu/states/hf.jsp?incfile=sep_sum/html/sum_btu_com.html

http://www.eia.doe.gov/emeu/states/hf.jsp?incfile=sep_sum/html/sum_btu_res.html

For simplicity’s sake, the term ‘incentives’ is used here to refer to both rate decoupling and positive performance incentive mechanisms. It does not include basic program cost recovery which is already allowed under Act 129.

The figures in this table were developed using the data on statewide electricity sales and electric utility incentives published in The 2008 State Energy Efficiency Scorecard, American Council for an Energy Efficient Economy, October 2008, pages 9-17.

Correspondence with national experts on this subject has suggested that this figure may be conservative.

See analysis provided in the Reduced Load Growth Work Plan for Potential GHG Reduction Measure, Nov. 21, 2008.