Improve the Transmission & Distribution System

Work Plan for Potential GHG Reduction Measure

Strategy Name: Reduce Electric Transmission & Distribution Losses

Lead Staff Contact:  Joe Sherrick (717-705-0372) & Scott Gebhardt (717-425-7860)

Summary:  This work plan analyzes the potential GHG reductions associated with reducing average electric transmission & distribution losses (“system losses”) by 1%.

Other Involved Agencies:  Pennsylvania Public Utility Commission

Possible New Measure(s):  All electricity transmission and distribution (T&D) systems have inherent energy losses associated with moving electricity through lines and equipment operations that are integral to the movement and delivery of the electricity.  Even though energy losses will inevitably occur, there are strategies available to minimize these losses.

The primary areas where improvements could be made to help reduce T&D losses are as follows:

- Improvements in transmission and distribution system equipment, materials and management.

- Demand side management and end-use consumer improvements.

- Expand use of clean distributed generation.

- Policy changes.

Possible actions in the identified primary areas for T&D improvements include:

- Improvements in transmission and distribution systems.

- Replace existing transformers with higher efficiency transformers*

- Improve the measurement, accounting and reporting of T&D losses

- Overloaded lines are less efficient- therefore add transmission lines to reduce losses

- Replace existing wires with higher capacity wires

- Improve communications on T&D systems

- Use high voltage DC transmission

- Use high temperature super conductors

* DOE published new energy conservation efficiency standards for distribution transformers on October 12, 2007.  These new standards will start in 2010.

- End-use consumer improvements

- Demand side management strategies implemented

- Energy efficiency improvements

- Load factor improvements

- Power factor improvements

Utility representatives offered the suggestion of reduced demand by the end user as the most cost effective way to reduce transmission losses.  As the transmission and distribution system becomes more congested especially at peak demand times the reduction of demand becomes more significant for reducing losses.

- Expand use of Clean Distributed Generation

- Combined Heat and Power (CHP) applications

- Energy recycling

- Micro grid expansion

- Small-scale or residential size clean energy generation

Projected GHG Reduction: 			0.8 MMTCO2e

The following steps were used in calculating the emissions reduction:

- Consumption and system loss data was obtained for each of the eight electric distribution companies (EDCs) in PA for years 2001 through 2006.  This data was obtained from the PUC’s Electric Power Annual Outlook reports.

- Average rates of consumption and system losses were calculated for each EDC under a business as usual (BAU) scenario.  Average growth rates in consumption ranged from 0.32% to 2.11%.  Average rates for systems losses, by EDC, ranged from 5.65% to 8.87%.

- Projections for BAU rates for consumption and system losses were made beginning with the last year of reported data to the PUC (2006).

- A similar set of projections was developed for system losses that assumes a 1% reduction from the BAU system loss rate.

- The sum total MWh from system losses for each scenario (BAU and 1% reduction) was then multiplied by a five-year (2000 through 2004) statewide average CO2 emission factor (1,279 pounds of CO2 per MWh) that is reflective of the generation fleet in PA.  The emissions rates were calculated from generation and emissions data reported to the U.S. DOE’s Energy Information Administration (EIA).

- Emissions were converted to million metric and the difference between the two scenarios was calculated.

A series of tables summarizing the estimated CO2 reductions potential of this initiative are included in this work plan immediately following “Potential Overlap.”

Economic Cost:  Industry and DOE representatives cautioned that life cycle cost analysis must be considered regarding improvements to the transmission and distribution systems.  The economics of improvements to the lines and other physical equipment may be capital cost prohibitive thus reduction in demand may be the most cost effective way to reduce losses.

Implementation Steps:

- Allow CHP generators to build private wires and micro-grids

- Provide a mechanism to fairly compensate distributed generation for power provided to the grid

Potential Overlap:

- Act 1, Act 129, Reduced Load Growth, Stabilized Load Growth, AEPS Tier I (8%, 15%, 20%) work plans

- All actions that increase or reduce electricity consumption will have a direct and obvious effect on the emissions reductions estimated in this work plan but will not impact the system loss rates.

| Consumption - Business as Usual (BAU) Scenario |
| --- |
|  | Average Growth Rate per EDC |  |
|  | 1.07% | 1.96% | 1.30% | 0.32% | 2.11% | 1.25% | 1.38% | 1.74% |  |
|  | Duquesne | MetEd | Penelec | PennPower | PECO | PPL | UGI | West Penn | Total MWh |
| Consumption (MWh) by Compliance Year | 2007 | 13,931,078 | 14,110,681 | 14,243,800 | 4,699,190 | 39,666,440 | 38,204,688 | 1,009,857 | 21,371,462 | 147,237,195 |
|  | 2008 | 14,079,593 | 14,387,398 | 14,429,540 | 4,714,284 | 40,503,909 | 38,680,531 | 1,023,812 | 21,743,813 | 149,562,879 |
|  | 2009 | 14,229,691 | 14,669,541 | 14,617,703 | 4,729,426 | 41,359,060 | 39,162,301 | 1,037,960 | 22,122,651 | 151,928,332 |
|  | 2010 | 14,381,389 | 14,957,216 | 14,808,319 | 4,744,617 | 42,232,266 | 39,650,071 | 1,052,303 | 22,508,089 | 154,334,271 |
|  | 2011 | 14,534,704 | 15,250,534 | 15,001,421 | 4,759,857 | 43,123,907 | 40,143,917 | 1,066,845 | 22,900,242 | 156,781,428 |
|  | 2012 | 14,689,654 | 15,549,603 | 15,197,041 | 4,775,146 | 44,034,374 | 40,643,914 | 1,081,587 | 23,299,229 | 159,270,547 |
|  | 2013 | 14,846,256 | 15,854,537 | 15,395,212 | 4,790,484 | 44,964,063 | 41,150,138 | 1,096,533 | 23,705,166 | 161,802,389 |
|  | 2014 | 15,004,527 | 16,165,451 | 15,595,967 | 4,805,871 | 45,913,380 | 41,662,667 | 1,111,686 | 24,118,176 | 164,377,726 |
|  | 2015 | 15,164,486 | 16,482,463 | 15,799,340 | 4,821,308 | 46,882,740 | 42,181,580 | 1,127,048 | 24,538,382 | 166,997,346 |
|  | 2016 | 15,326,149 | 16,805,691 | 16,005,365 | 4,836,794 | 47,872,566 | 42,706,956 | 1,142,623 | 24,965,909 | 169,662,052 |
|  | 2017 | 15,489,536 | 17,135,257 | 16,214,076 | 4,852,330 | 48,883,290 | 43,238,875 | 1,158,412 | 25,400,885 | 172,372,662 |
|  | 2018 | 15,654,665 | 17,471,287 | 16,425,509 | 4,867,916 | 49,915,353 | 43,777,420 | 1,174,420 | 25,843,439 | 175,130,010 |
|  | 2019 | 15,821,555 | 17,813,906 | 16,639,699 | 4,883,551 | 50,969,206 | 44,322,672 | 1,190,649 | 26,293,704 | 177,934,944 |
|  | 2020 | 15,990,223 | 18,163,244 | 16,856,683 | 4,899,238 | 52,045,308 | 44,874,716 | 1,207,103 | 26,751,814 | 180,788,329 |
|  | 2021 | 16,160,690 | 18,519,433 | 17,076,495 | 4,914,974 | 53,144,130 | 45,433,635 | 1,223,784 | 27,217,905 | 183,691,047 |
|  | 2022 | 16,332,974 | 18,882,607 | 17,299,175 | 4,930,761 | 54,266,152 | 45,999,516 | 1,240,695 | 27,692,117 | 186,643,996 |
|  | 2023 | 16,507,094 | 19,252,903 | 17,524,758 | 4,946,599 | 55,411,862 | 46,572,444 | 1,257,840 | 28,174,591 | 189,648,091 |
|  | 2024 | 16,683,071 | 19,630,461 | 17,753,282 | 4,962,488 | 56,581,762 | 47,152,509 | 1,275,222 | 28,665,471 | 192,704,264 |
|  | 2025 | 16,860,924 | 20,015,422 | 17,984,787 | 4,978,427 | 57,776,361 | 47,739,798 | 1,292,844 | 29,164,903 | 195,813,466 |

| System Losses - Business as Usual (BAU) Scenario |
| --- |
|  | Average System Loss Rate per EDC |  |
|  | 5.77% | 7.87% | 8.87% | 6.49% | 6.65% | 7.18% | 5.65% | 6.53% |  |
|  | Duquesne | MetEd | Penelec | PennPower | PECO | PPL | UGI | West Penn | Total MWh |
| System Losses (MWh) by Compliance Year | 2007 | 803,683 | 1,110,810 | 1,263,229 | 304,805 | 2,637,920 | 2,744,325 | 57,075 | 1,394,798 | 10,316,645 |
|  | 2008 | 812,251 | 1,132,593 | 1,279,702 | 305,784 | 2,693,614 | 2,778,506 | 57,863 | 1,419,100 | 10,479,412 |
|  | 2009 | 820,910 | 1,154,804 | 1,296,390 | 306,766 | 2,750,484 | 2,813,112 | 58,663 | 1,443,824 | 10,644,952 |
|  | 2010 | 829,662 | 1,177,450 | 1,313,295 | 307,751 | 2,808,554 | 2,848,150 | 59,474 | 1,468,980 | 10,813,315 |
|  | 2011 | 838,507 | 1,200,540 | 1,330,420 | 308,740 | 2,867,850 | 2,883,624 | 60,296 | 1,494,573 | 10,984,550 |
|  | 2012 | 847,446 | 1,224,083 | 1,347,769 | 309,731 | 2,928,399 | 2,919,540 | 61,129 | 1,520,613 | 11,158,709 |
|  | 2013 | 856,480 | 1,248,088 | 1,365,344 | 310,726 | 2,990,226 | 2,955,903 | 61,973 | 1,547,106 | 11,335,846 |
|  | 2014 | 865,611 | 1,272,564 | 1,383,148 | 311,724 | 3,053,358 | 2,992,719 | 62,830 | 1,574,061 | 11,516,014 |
|  | 2015 | 874,839 | 1,297,519 | 1,401,184 | 312,726 | 3,117,822 | 3,029,993 | 63,698 | 1,601,486 | 11,699,268 |
|  | 2016 | 884,165 | 1,322,964 | 1,419,456 | 313,730 | 3,183,648 | 3,067,732 | 64,578 | 1,629,388 | 11,885,662 |
|  | 2017 | 893,591 | 1,348,908 | 1,437,966 | 314,738 | 3,250,864 | 3,105,941 | 65,471 | 1,657,777 | 12,075,255 |
|  | 2018 | 903,117 | 1,375,360 | 1,456,717 | 315,749 | 3,319,499 | 3,144,626 | 66,375 | 1,686,660 | 12,268,104 |
|  | 2019 | 912,745 | 1,402,332 | 1,475,713 | 316,763 | 3,389,583 | 3,183,793 | 67,293 | 1,716,046 | 12,464,267 |
|  | 2020 | 922,475 | 1,429,832 | 1,494,956 | 317,780 | 3,461,147 | 3,223,447 | 68,223 | 1,745,944 | 12,663,805 |
|  | 2021 | 932,310 | 1,457,872 | 1,514,451 | 318,801 | 3,534,221 | 3,263,595 | 69,165 | 1,776,364 | 12,866,779 |
|  | 2022 | 942,249 | 1,486,461 | 1,534,199 | 319,825 | 3,608,838 | 3,304,244 | 70,121 | 1,807,313 | 13,073,250 |
|  | 2023 | 952,294 | 1,515,611 | 1,554,205 | 320,852 | 3,685,031 | 3,345,399 | 71,090 | 1,838,801 | 13,283,284 |
|  | 2024 | 962,446 | 1,545,333 | 1,574,472 | 321,883 | 3,762,832 | 3,387,066 | 72,073 | 1,870,838 | 13,496,943 |
|  | 2025 | 972,706 | 1,575,638 | 1,595,004 | 322,917 | 3,842,276 | 3,429,252 | 73,068 | 1,903,433 | 13,714,295 |

| CO2 Emissions Associated with System Losses Reduced by 1% |
| --- |
|  |  | Total MWh | CO2 Tons | MMTCO2 |
| System Losses (MWh) by Compliance Year | 2007 | 9,284,980 | 5,937,745 | 5.39 |
|  | 2008 | 9,431,471 | 6,031,426 | 5.47 |
|  | 2009 | 9,580,457 | 6,126,702 | 5.56 |
|  | 2010 | 9,731,983 | 6,223,603 | 5.64 |
|  | 2011 | 9,886,095 | 6,322,158 | 5.73 |
|  | 2012 | 10,042,838 | 6,422,395 | 5.83 |
|  | 2013 | 10,202,262 | 6,524,346 | 5.92 |
|  | 2014 | 10,364,413 | 6,628,042 | 6.01 |
|  | 2015 | 10,529,341 | 6,733,513 | 6.11 |
|  | 2016 | 10,697,096 | 6,840,793 | 6.20 |
|  | 2017 | 10,867,730 | 6,949,913 | 6.30 |
|  | 2018 | 11,041,293 | 7,060,907 | 6.40 |
|  | 2019 | 11,217,840 | 7,173,809 | 6.51 |
|  | 2020 | 11,397,424 | 7,288,653 | 6.61 |
|  | 2021 | 11,580,101 | 7,405,474 | 6.72 |
|  | 2022 | 11,765,925 | 7,524,309 | 6.82 |
|  | 2023 | 11,954,955 | 7,645,194 | 6.93 |
|  | 2024 | 12,147,249 | 7,768,166 | 7.05 |
|  | 2025 | 12,342,865 | 7,893,262 | 7.16 |
| CO2 Reduction BAU vs. 1% Reduction in System Losses |
|  | MMTCO2 |
|  | BAU | 1% Red. | Delta |
| Consumption (MWh) by Compliance Year | 2007 | 5.98 | 5.39 | 0.60 |
|  | 2008 | 6.08 | 5.47 | 0.61 |
|  | 2009 | 6.17 | 5.56 | 0.62 |
|  | 2010 | 6.27 | 5.64 | 0.63 |
|  | 2011 | 6.37 | 5.73 | 0.64 |
|  | 2012 | 6.47 | 5.83 | 0.65 |
|  | 2013 | 6.58 | 5.92 | 0.66 |
|  | 2014 | 6.68 | 6.01 | 0.67 |
|  | 2015 | 6.79 | 6.11 | 0.68 |
|  | 2016 | 6.89 | 6.20 | 0.69 |
|  | 2017 | 7.00 | 6.30 | 0.70 |
|  | 2018 | 7.12 | 6.40 | 0.71 |
|  | 2019 | 7.23 | 6.51 | 0.72 |
|  | 2020 | 7.35 | 6.61 | 0.73 |
|  | 2021 | 7.46 | 6.72 | 0.75 |
|  | 2022 | 7.58 | 6.82 | 0.76 |
|  | 2023 | 7.70 | 6.93 | 0.77 |
|  | 2024 | 7.83 | 7.05 | 0.78 |
|  | 2025 | 7.95 | 7.16 | 0.80 |
| CO2 Emissions Associated with System Losses BAU |
|  |  | Total MWh | CO2 Tons | MMTCO2 |
| System Losses (MWh) by Compliance Year | 2007 | 10,316,645 | 6,597,494 | 5.98 |
|  | 2008 | 10,479,412 | 6,701,584 | 6.08 |
|  | 2009 | 10,644,952 | 6,807,447 | 6.17 |
|  | 2010 | 10,813,315 | 6,915,115 | 6.27 |
|  | 2011 | 10,984,550 | 7,024,619 | 6.37 |
|  | 2012 | 11,158,709 | 7,135,995 | 6.47 |
|  | 2013 | 11,335,846 | 7,249,274 | 6.58 |
|  | 2014 | 11,516,014 | 7,364,491 | 6.68 |
|  | 2015 | 11,699,268 | 7,481,682 | 6.79 |
|  | 2016 | 11,885,662 | 7,600,881 | 6.89 |
|  | 2017 | 12,075,255 | 7,722,126 | 7.00 |
|  | 2018 | 12,268,104 | 7,845,452 | 7.12 |
|  | 2019 | 12,464,267 | 7,970,899 | 7.23 |
|  | 2020 | 12,663,805 | 8,098,503 | 7.35 |
|  | 2021 | 12,866,779 | 8,228,305 | 7.46 |
|  | 2022 | 13,073,250 | 8,360,344 | 7.58 |
|  | 2023 | 13,283,284 | 8,494,660 | 7.70 |
|  | 2024 | 13,496,943 | 8,631,295 | 7.83 |
|  | 2025 | 13,714,295 | 8,770,292 | 7.95 |