Alternative Energy Portfolio Standard (AEPS) Tier I at 15%

Work Plan for Potential GHG Reduction Measure

Lead Staff Contact: Joe Sherrick (717-772-8944)

Summary:  This work plan examines the potential CO2 emissions reductions associated with an increase in the AEPS Tier I by 7% (from the existing 8%) to a total of 15%.

Other Involved Agencies: PUC and DEP have shared roles in administering the AEPS

Possible New Measure(s):  Due to uncertainties of cost-effectiveness, no increase in the solar PV share of the AEPS is proposed under this work plan.  Under the proposed scenario, the AEPS would mature in 2025 instead of 2021.   The implementation schedule under this scenario would change in year 2016 from the current format by increasing the annual requirement by 1.0% through 2025 instead of the 0.5% annual increase under the existing standard.

Projected GHG Reduction:  7.95 MMTCO2 additional; 17.60 MMTCO2 total

This was determined by establishing a consumption-based load growth projection for each electric distribution company (EDC) and applying that factor to the 2006 actual consumption for each EDC, out to 2025.  Under the proposed scenario, the AEPS would mature in 2025 instead of 2021.  The implementation schedule under this scenario would change in year 2016 from the current format by increasing the annual requirement by 1.0% through 2025 instead of the 0.5% annual increase under the existing standard.  The total estimated electricity consumption was multiplied by a five-year (2000 through 2004) statewide, grid average, CO2 emissions factor of 1,279 pounds per MWH.  This was then converted to million metric tons of carbon dioxide (MMTCO2).

There will be some additional reductions through Tier II from sources such as hydro and energy efficiency.  The contribution of these resources to meeting the Tier II obligation is somewhat uncertain but we already know that sufficient credits from waste coal have been generated to meet the entire Tier II requirements through at least 2021.   The impact is that little incentive exists for the generation of electricity from new, zero carbon emitting sources due to the over-supply created by waste coal.  It also needs to be noted that any energy efficiency work plans that reduce the overall consumption of electricity within PA will result in a direct reduction of the emissions associated with the AEPS.

The result is an estimated additional reduction of 7.95 MMTCO2 above the anticipated 9.65 MMTCO2 from the current AEPS Tier I @ 8% structure.

Economic Cost:

- Cost to DEP – Administration of programs for the continued support of energy efficiency and renewables, particularly solar PV (ex. Energy Harvest, PEDA, Alternative Energy Investment Act, etc.)

- Cost to the Commonwealth – Continued support of renewables, particularly solar

- Cost to regulated community or consumer – Distribution companies pass compliance costs on to the rate-payers.  Until all of the EDC rate caps are removed the impact will remain uncertain.  The removal of the rate caps will have a far more pronounced impact on electricity rates than will the requirements of the AEPS.

- Are there Federal funds available? USDA Farm Bill appropriations can and have provided limited support.  Moreover, as the total appropriations are increasing, the amount available via grant funding is being significantly scaled back in favor of loans.

- Do these costs fund other programs? No.

- Are cost savings realized from this initiative? Not directly.  Indirect savings to the Commonwealth will accrue subject to in-state renewables development (manufacturing, installation, sales and service, etc.)

Implementation Steps:

- An analysis, including an economic impacts assessment to warrant support for this initiative should be conducted.  This analysis should take into consideration other state renewable portfolio standards that may compete for the same resources.

- New legislation would have to be drafted to modify the existing AEPS.

Potential Overlap:

- AEPS Tier I @ 20%

- HB 2200

- Reduced Load Growth

- All Electricity Efficiency Initiatives

- Transmission and Distribution Loss Reductions

- High Performance Building Standards

- Energy Audits

- Others

| AEPS Requirements (Tier I 15%) |  | AEPS CO2 Reductions |
| --- | --- | --- |
| Compliance Year | Tier I | PV | Tier II | Projected PA Consumption (MWH) | Tier I MWH | PV MWH | Tier II MWH | Total AEPS MWH |  | Total Tier I + PV MWH | Total MMTCO2 |
| 2007 | 1.50% | 0.0013% | 4.2% | 147,237,195 | 2,208,558 | 1,914 | 6,183,962 | 8,394,434 |  | 2,210,472 | 1.28 |
| 2008 | 1.50% | 0.0030% | 4.2% | 149,562,879 | 2,243,443 | 4,487 | 6,281,641 | 8,529,571 |  | 2,247,930 | 1.30 |
| 2009 | 2.00% | 0.0063% | 4.2% | 151,928,332 | 3,038,567 | 9,571 | 6,380,990 | 9,429,128 |  | 3,048,138 | 1.77 |
| 2010 | 2.50% | 0.0120% | 4.2% | 154,334,271 | 3,858,357 | 18,520 | 6,482,039 | 10,358,916 |  | 3,876,877 | 2.25 |
| 2011 | 3.00% | 0.0203% | 6.2% | 156,781,428 | 4,703,443 | 31,827 | 9,720,449 | 14,455,718 |  | 4,735,269 | 2.75 |
| 2012 | 3.50% | 0.0325% | 6.2% | 159,270,547 | 5,574,469 | 51,763 | 9,874,774 | 15,501,006 |  | 5,626,232 | 3.26 |
| 2013 | 4.00% | 0.0510% | 6.2% | 161,802,389 | 6,472,096 | 82,519 | 10,031,748 | 16,586,363 |  | 6,554,615 | 3.80 |
| 2014 | 4.50% | 0.0840% | 6.2% | 164,377,726 | 7,396,998 | 138,077 | 10,191,419 | 17,726,494 |  | 7,535,075 | 4.37 |
| 2015 | 5.00% | 0.1440% | 6.2% | 166,997,346 | 8,349,867 | 240,476 | 10,353,835 | 18,944,179 |  | 8,590,343 | 4.98 |
| 2016 | 6.00% | 0.2500% | 8.2% | 169,662,052 | 10,179,723 | 424,155 | 13,912,288 | 24,516,167 |  | 10,603,878 | 6.15 |
| 2017 | 7.00% | 0.2933% | 8.2% | 172,372,662 | 12,066,086 | 505,569 | 14,134,558 | 26,706,214 |  | 12,571,655 | 7.29 |
| 2018 | 8.00% | 0.3400% | 8.2% | 175,130,010 | 14,010,401 | 595,442 | 14,360,661 | 28,966,504 |  | 14,605,843 | 8.47 |
| 2019 | 9.00% | 0.3900% | 8.2% | 177,934,944 | 16,014,145 | 693,946 | 14,590,665 | 31,298,757 |  | 16,708,091 | 9.69 |
| 2020 | 10.00% | 0.4433% | 8.2% | 180,788,329 | 18,078,833 | 801,435 | 14,824,643 | 33,704,910 |  | 18,880,268 | 10.95 |
| 2021 | 11.00% | 0.5000% | 10.0% | 183,691,047 | 20,206,015 | 918,455 | 18,369,105 | 39,493,575 |  | 21,124,470 | 12.25 |
| 2022 | 12.00% | 0.5000% | 10.0% | 186,643,996 | 22,397,280 | 933,220 | 18,664,400 | 41,994,899 |  | 23,330,499 | 13.53 |
| 2023 | 13.00% | 0.5000% | 10.0% | 189,648,091 | 24,654,252 | 948,240 | 18,964,809 | 44,567,301 |  | 25,602,492 | 14.85 |
| 2024 | 14.00% | 0.5000% | 10.0% | 192,704,264 | 26,978,597 | 963,521 | 19,270,426 | 47,212,545 |  | 27,942,118 | 16.21 |
| 2025 | 15.00% | 0.5000% | 10.0% | 195,813,466 | 29,372,020 | 979,067 | 19,581,347 | 49,932,434 |  | 30,351,087 | 17.60 |