Alternative Energy Portfolio (Act 213 of 2004) Tier I Standard

Work Plan for Potential GHG Reduction Measure

Lead Staff Contact: Joe Sherrick (717-772-8944)

Summary:  Identifies GHG reductions associated with the existing AEPS Tier I requirement at 8%.

Other Involved Agencies:  PUC and DEP have shared roles in administering the AEPS

Existing Measure: The AEPS requires that all electricity consumed within PA by 2021 be comprised of at least 0.5% solar PV, 8% from other renewable (Tier I) sources and 10% from other alternative energy (Tier II) sources.  The AEPS matures in 2021 after which, no further increase in renewable generation is required but the standards from 2021 remain in effect.

Projected GHG Reduction:  9.65 MMTCO2

The CO2 emissions reductions associated with this AEPS structure was calculated by first establishing a consumption-based load growth projection for each electric distribution company (EDC) and applying that factor to the 2006 actual consumption for each EDC, projecting out to 2025.  The total estimated electricity consumption was multiplied by a five-year (2000 through 2004) statewide, grid average, CO2 emissions factor of 1,279 pounds per MWH.  This was then converted to million metric tons of carbon dioxide (MMTCO2).

There will be some additional reductions through Tier II from sources such as large hydro and energy efficiency.  The contribution of these resources to meeting the Tier II obligation is somewhat uncertain because we already know that sufficient credits from waste coal have been generated to meet the entire Tier II requirements through at least 2021.   The impact is that little incentive exists for the generation of electricity from new, zero carbon emitting sources due to the over-supply created by waste coal.  It also needs to be noted that any energy efficiency work plans that reduce the overall consumption of electricity within PA will result in a direct reduction of the emissions associated with the AEPS.

Economic Cost:

- Cost to DEP – Administration of programs for the continued support of energy efficiency and renewables, particularly solar PV (ex. Energy Harvest, PEDA, Alternative Energy Investment Act, etc.)

- Cost to the Commonwealth – Continued support of renewables, particularly solar

- Cost to regulated community or consumer – Distribution companies pass compliance costs on to the rate-payers.  Until all of the EDC rate caps are removed the impact will remain uncertain.  The removal of the rate caps will have a far more pronounced impact on electricity rates than will the requirements of the AEPS.

- Are there Federal funds available? USDA Farm Bill appropriations can and have provided limited support.  Moreover, as the total appropriations are increasing, the amount available via grant funding is being significantly scaled back in favor of loans.

- Do these costs fund other programs? No.

- Are cost savings realized from this initiative? Not directly.  Indirect savings to the Commonwealth will accrue subject to in-state renewables development (manufacturing, installation, sales and service, etc.)

Implementation Steps:

- Already being implemented.

- Legislation continues to be drafted that would require additional increases in the amount of alternative energy.  Pennsylvania has the lowest percentage requirements of any surrounding state renewable portfolio standards.  Because the geographic scope from which projects may be considered eligible (Illinois to North Carolina) for Act 213 compliance is much broader than was originally intended and in order to ensure that more renewable energy and associated new jobs are created in PA, the requirements of the AEPS could be increased.

Potential Overlap:

- HB 2200

- Reduced Load Growth

- Al Electricity Efficiency Initiatives

- Transmission and Distribution Loss Reductions

- High Performance Building Standards

- Energy Audits

- Others

| AEPS Requirements |  | AEPS CO2 Reductions |
| --- | --- | --- |
| Compliance Year | Tier I | PV | Tier II | Projected PA Consumption (MWH) | Tier I MWH | PV MWH | Tier II MWH | Total AEPS MWH |  | Total Tier I + PV MWH | Total MMTCO2 |
| 2007 | 1.50% | 0.0013% | 4.2% | 147,237,195 | 2,208,558 | 1,914 | 6,183,962 | 8,394,434 |  | 2,210,472 | 1.28 |
| 2008 | 1.50% | 0.0030% | 4.2% | 149,562,879 | 2,243,443 | 4,487 | 6,281,641 | 8,529,571 |  | 2,247,930 | 1.30 |
| 2009 | 2.00% | 0.0063% | 4.2% | 151,928,332 | 3,038,567 | 9,571 | 6,380,990 | 9,429,128 |  | 3,048,138 | 1.77 |
| 2010 | 2.50% | 0.0120% | 4.2% | 154,334,271 | 3,858,357 | 18,520 | 6,482,039 | 10,358,916 |  | 3,876,877 | 2.25 |
| 2011 | 3.00% | 0.0203% | 6.2% | 156,781,428 | 4,703,443 | 31,827 | 9,720,449 | 14,455,718 |  | 4,735,269 | 2.75 |
| 2012 | 3.50% | 0.0325% | 6.2% | 159,270,547 | 5,574,469 | 51,763 | 9,874,774 | 15,501,006 |  | 5,626,232 | 3.26 |
| 2013 | 4.00% | 0.0510% | 6.2% | 161,802,389 | 6,472,096 | 82,519 | 10,031,748 | 16,586,363 |  | 6,554,615 | 3.80 |
| 2014 | 4.50% | 0.0840% | 6.2% | 164,377,726 | 7,396,998 | 138,077 | 10,191,419 | 17,726,494 |  | 7,535,075 | 4.37 |
| 2015 | 5.00% | 0.1440% | 6.2% | 166,997,346 | 8,349,867 | 240,476 | 10,353,835 | 18,944,179 |  | 8,590,343 | 4.98 |
| 2016 | 5.50% | 0.2500% | 8.2% | 169,662,052 | 9,331,413 | 424,155 | 13,912,288 | 23,667,856 |  | 9,755,568 | 5.66 |
| 2017 | 6.00% | 0.2933% | 8.2% | 172,372,662 | 10,342,360 | 505,569 | 14,134,558 | 24,982,487 |  | 10,847,929 | 6.29 |
| 2018 | 6.50% | 0.3400% | 8.2% | 175,130,010 | 11,383,451 | 595,442 | 14,360,661 | 26,339,553 |  | 11,978,893 | 6.95 |
| 2019 | 7.00% | 0.3900% | 8.2% | 177,934,944 | 12,455,446 | 693,946 | 14,590,665 | 27,740,058 |  | 13,149,392 | 7.63 |
| 2020 | 7.50% | 0.4433% | 8.2% | 180,788,329 | 13,559,125 | 801,435 | 14,824,643 | 29,185,202 |  | 14,360,559 | 8.33 |
| 2021 | 8.00% | 0.5000% | 10.0% | 183,691,047 | 14,695,284 | 918,455 | 18,369,105 | 33,982,844 |  | 15,613,739 | 9.06 |
| 2022 | 8.00% | 0.5000% | 10.0% | 186,643,996 | 14,931,520 | 933,220 | 18,664,400 | 34,529,139 |  | 15,864,740 | 9.20 |
| 2023 | 8.00% | 0.5000% | 10.0% | 189,648,091 | 15,171,847 | 948,240 | 18,964,809 | 35,084,897 |  | 16,120,088 | 9.35 |
| 2024 | 8.00% | 0.5000% | 10.0% | 192,704,264 | 15,416,341 | 963,521 | 19,270,426 | 35,650,289 |  | 16,379,862 | 9.50 |
| 2025 | 8.00% | 0.5000% | 10.0% | 195,813,466 | 15,665,077 | 979,067 | 19,581,347 | 36,225,491 |  | 16,644,145 | 9.65 |