Stabilized Load Growth

Work Plan for Potential GHG Reduction Measure

Strategy Name: Stabilized Load Growth

Lead Staff Contact: Joe Sherrick (717-772-8944)

Summary:  This measure builds upon the very modest reductions required via Act 129 of 2008.  Act 129 requires reductions in consumption of 1.0% by 2011 and 2.0% by 2013, measured against 2010 consumption.  The Stabilized Load Growth (SLG) scenario further investigates the potential impact of annual consumption reductions of 1.5% in 2015 and 2017 followed by a rate of consumption that is held static from 2018 through 2025.  These reductions are less than what would be achieved as compared to the Reduced Load work plan in that the Reduced Load work plan scenario continues to require additional reductions in consumption through 2025.  It is estimated that the Stabilized Load Growth work plan realizes a reduction in gross-level GHG emissions of 26.05 MMTCO2.  The net total, subtracting out the impact of Act 129 reductions (8.01 MMTCO2) is 18.04 MMTCO2.

Please note that this analysis does not include the very modest consumption and associated system losses from municipalities that are service providers or the rural electric cooperatives.

Other Involved Agencies: PUC

Possible New Measure(s): As required in Act 129, a study must be undertaken to identify the full suite of cost-effective measures that should be given consideration.  A report from the American Council for an Energy Efficient Economy (ACEEE) is being drafted for the PUC and DEP and should serve well to inform this process.

Potential GHG Reduction: 18.04 MMTCO2 additional to Act 129 reductions (26.05 MMTCO2 total for this measure)

The following steps were used in calculating the emissions reduction:

- Consumption and system loss data was obtained for each of the eight electric distribution companies (EDCs) in PA for years 2001 through 2006.  This data was obtained from the PUC’s Electric Power Annual Outlook reports.

- Average rates of consumption and system losses were calculated for each EDC under two different scenarios; Stabilized Load Growth (SLG) that includes Act 129 reductions and business as usual (BAU) that assumes no reductions are realized.  Average growth rates in consumption ranged from 0.32% to 2.11%.  Average rates for systems losses, by EDC, ranged from 5.65% to 8.87%.

- Projections for BAU rates of consumption were made beginning with the last year of reported data to the PUC (2006).

- Under the Stabilized Load Growth scenario, consumption in years 2019 through 2025 is held equal to that in 2018 which represents a sustained, annual reduction of approximately 1.55%, as compared to the BAU scenario.

- The sum total MWh for consumption and system losses for each scenario (SLG and BAU) was then multiplied by a five-year (2000 through 2004) statewide average CO2 emission factor (1,279 pounds of CO2 per MWh) for electricity produced in PA.  The emissions rates were calculated from generation and emissions data reported to the EIA.

- The difference between these two scenarios yields the anticipated reduction in CO2 emissions in year 2025 of 12.47 MMTCO2 (incremental) beyond those provided solely by Act 129 or a total of 15.98 MMTCO2 in association with Act 129 implementation.

A series of tables summarizing the estimated CO2 reductions potential of this initiative are included in this work plan immediately following “Potential Overlap.”

Assumptions:

- Adequate cost-effective reductions exist or will exist, through year 2025, to provide the approximate 25 million MWh of curtailment, as compared to the unchecked, projected rate of growth in electricity consumption.

- No reductions would be required if not supported through an analysis of cost-effective measures.

Economic Cost:

- Cost to DEP - None

- Cost to the Commonwealth – Act 129 requires the PUC to hire a program administrator to oversee this process and to provide assessments as to the cost-effectiveness and level of additional reductions that may be possible within PA.  The cost for this service is unknown.  It is further assumed that the PUC would perform similar services to oversee the reductions that may be required if such a Stabilized Load Growth initiative were to be implemented.

- Cost to regulated community or consumer – Not quantified, as of yet.  Short-term capital costs may be experienced, depending on a host of issues but short and long-term savings are anticipated.  Requires detailed analysis.

- Are there Federal funds available? – Federal funding is not required nor is it available at this time.  Limited assistance may be available through the U.S. DOE State Energy Plan but this would most likely be limited to policy analysis and possibly technical support.

- Do these costs fund other programs? No.  Any costs are expected to result in changes to consumer behavior.

- Are cost savings realized from this initiative? Cost savings are expected but this does require a detailed analysis.  The assumption is that reductions will only be required such that can be sustained through cost-effective measures.

Implementation Steps:  The following, and other, considerations should be examined as policy tools to support this measure:

- Act 129 provides the PUC with the necessary authority to require additional cost-effective reductions in electricity consumption.

- An assessment of electricity consumption reduction potential is necessary to determine if the requirements suggested within this work plan conform to Act 129 requisites.  Such a study is underway by the ACEEE.

- The PUC may have the authority within Act 129 of 2008 that would facilitate realization of this reduction measure.

- A legislative amendment to the AEPS establishing a dedicated market share for energy efficiency credits (new tier or carve out) might facilitate achieving this reduction measure by rewarding over-compliance and providing a cost-effective manner to achieve greater reductions.

- Require electric distribution companies to invest in demand side response initiatives, including rebates to consumers.

- Require that all cost-effective supply side and demand side measures have been identified and acted upon before approvals for new generation are granted.  In a February 5, 2007 press release http://www.aceee.org/press/e072pr.htm ACEEE reported that, “States from Texas to Vermont are finding energy efficiency resources available at less than 4 cents per kilowatt-hour, compared to the expected cost of power from new plants of 5 to 10 cents.”

- Implementing advanced building standards for the commercial, institutional, state and municipal government sectors that establish minimum green building practices and energy efficiency standards.

- Coupled with the advanced building standard, consider a requirement that all commercial, institutional, state and municipal government buildings perform annual benchmarking, similar to that established by the U.S. EPA that documents the gains or losses in energy consumption on a per square foot basis, based on the type of activity occurring.  This information is publicly accessible.  It educates and encourages building owners and operators to achieve higher performance.

- Work with neighboring states on establishing regional efficiency standards for appliances and electronics where none currently exist or where minimum standards are less than optimal.

- Establish an aggressive phase-out of incandescent lights and/or establish a pricing/tax structure that preferentially treats lighting with a higher lumens to watts ratio.

- Rate decoupling

Potential Overlap:

- Act 129 Work Plan

- Reduced Load Growth Work Plan

| Stabilized Load Growth (SLG) Scenario |
| --- |
|  | Average Growth Rate per EDC |  |
|  | 1.07% | 1.96% | 1.30% | 0.32% | 2.11% | 1.25% | 1.38% | 1.74% |  |
|  | Duquesne | MetEd | Penelec | PennPower | PECO | PPL | UGI | West Penn | Total MWh |
| Consumption (MWh) by Compliance Year | 2007 | 13,931,078 | 14,110,681 | 14,243,800 | 4,699,190 | 39,666,440 | 38,204,688 | 1,009,857 | 21,371,462 | 147,237,195 |
|  | 2008 | 14,079,593 | 14,387,398 | 14,429,540 | 4,714,284 | 40,503,909 | 38,680,531 | 1,023,812 | 21,743,813 | 149,562,879 |
|  | 2009 | 14,229,691 | 14,669,541 | 14,617,703 | 4,729,426 | 41,359,060 | 39,162,301 | 1,037,960 | 22,122,651 | 151,928,332 |
|  | 2010 | 14,381,389 | 14,957,216 | 14,808,319 | 4,744,617 | 42,232,266 | 39,650,071 | 1,052,303 | 22,508,089 | 154,334,271 |
|  | 2011 | 14,237,575 | 14,807,644 | 14,660,236 | 4,697,171 | 41,809,943 | 39,253,571 | 1,041,780 | 22,283,008 | 152,790,928 |
|  | 2012 | 14,389,357 | 15,098,028 | 14,851,407 | 4,712,258 | 42,692,668 | 39,742,478 | 1,056,176 | 22,671,240 | 155,213,613 |
|  | 2013 | 14,093,757 | 14,658,068 | 14,512,148 | 4,649,720 | 41,387,616 | 38,857,065 | 1,031,252 | 22,057,923 | 151,247,549 |
|  | 2014 | 14,244,006 | 14,945,518 | 14,701,388 | 4,664,655 | 42,261,425 | 39,341,034 | 1,045,503 | 22,442,233 | 153,645,763 |
|  | 2015 | 14,030,346 | 14,721,336 | 14,480,867 | 4,594,686 | 41,627,503 | 38,750,919 | 1,029,821 | 22,105,600 | 151,330,748 |
|  | 2016 | 14,179,919 | 15,010,027 | 14,669,699 | 4,609,444 | 42,506,376 | 39,233,565 | 1,044,052 | 22,490,741 | 153,743,823 |
|  | 2017 | 13,967,220 | 14,784,877 | 14,449,654 | 4,540,302 | 41,868,781 | 38,645,062 | 1,028,391 | 22,153,380 | 151,437,665 |
|  | 2018 | 14,116,120 | 15,074,814 | 14,638,078 | 4,554,886 | 42,752,748 | 39,126,390 | 1,042,602 | 22,539,353 | 153,844,992 |
|  | 2019 | 14,116,120 | 15,074,814 | 14,638,078 | 4,554,886 | 42,752,748 | 39,126,390 | 1,042,602 | 22,539,353 | 153,844,992 |
|  | 2020 | 14,116,120 | 15,074,814 | 14,638,078 | 4,554,886 | 42,752,748 | 39,126,390 | 1,042,602 | 22,539,353 | 153,844,992 |
|  | 2021 | 14,116,120 | 15,074,814 | 14,638,078 | 4,554,886 | 42,752,748 | 39,126,390 | 1,042,602 | 22,539,353 | 153,844,992 |
|  | 2022 | 14,116,120 | 15,074,814 | 14,638,078 | 4,554,886 | 42,752,748 | 39,126,390 | 1,042,602 | 22,539,353 | 153,844,992 |
|  | 2023 | 14,116,120 | 15,074,814 | 14,638,078 | 4,554,886 | 42,752,748 | 39,126,390 | 1,042,602 | 22,539,353 | 153,844,992 |
|  | 2024 | 14,116,120 | 15,074,814 | 14,638,078 | 4,554,886 | 42,752,748 | 39,126,390 | 1,042,602 | 22,539,353 | 153,844,992 |
|  | 2025 | 14,116,120 | 15,074,814 | 14,638,078 | 4,554,886 | 42,752,748 | 39,126,390 | 1,042,602 | 22,539,353 | 153,844,992 |

| Consumption - Business as Usual (BAU) Scenario |
| --- |
|  | Average Growth Rate per EDC |  |
|  | 1.07% | 1.96% | 1.30% | 0.32% | 2.11% | 1.25% | 1.38% | 1.74% |  |
|  | Duquesne | MetEd | Penelec | PennPower | PECO | PPL | UGI | West Penn | Total MWh |
| Consumption (MWh) by Compliance Year | 2007 | 13,931,078 | 14,110,681 | 14,243,800 | 4,699,190 | 39,666,440 | 38,204,688 | 1,009,857 | 21,371,462 | 147,237,195 |
|  | 2008 | 14,079,593 | 14,387,398 | 14,429,540 | 4,714,284 | 40,503,909 | 38,680,531 | 1,023,812 | 21,743,813 | 149,562,879 |
|  | 2009 | 14,229,691 | 14,669,541 | 14,617,703 | 4,729,426 | 41,359,060 | 39,162,301 | 1,037,960 | 22,122,651 | 151,928,332 |
|  | 2010 | 14,381,389 | 14,957,216 | 14,808,319 | 4,744,617 | 42,232,266 | 39,650,071 | 1,052,303 | 22,508,089 | 154,334,271 |
|  | 2011 | 14,534,704 | 15,250,534 | 15,001,421 | 4,759,857 | 43,123,907 | 40,143,917 | 1,066,845 | 22,900,242 | 156,781,428 |
|  | 2012 | 14,689,654 | 15,549,603 | 15,197,041 | 4,775,146 | 44,034,374 | 40,643,914 | 1,081,587 | 23,299,229 | 159,270,547 |
|  | 2013 | 14,846,256 | 15,854,537 | 15,395,212 | 4,790,484 | 44,964,063 | 41,150,138 | 1,096,533 | 23,705,166 | 161,802,389 |
|  | 2014 | 15,004,527 | 16,165,451 | 15,595,967 | 4,805,871 | 45,913,380 | 41,662,667 | 1,111,686 | 24,118,176 | 164,377,726 |
|  | 2015 | 15,164,486 | 16,482,463 | 15,799,340 | 4,821,308 | 46,882,740 | 42,181,580 | 1,127,048 | 24,538,382 | 166,997,346 |
|  | 2016 | 15,326,149 | 16,805,691 | 16,005,365 | 4,836,794 | 47,872,566 | 42,706,956 | 1,142,623 | 24,965,909 | 169,662,052 |
|  | 2017 | 15,489,536 | 17,135,257 | 16,214,076 | 4,852,330 | 48,883,290 | 43,238,875 | 1,158,412 | 25,400,885 | 172,372,662 |
|  | 2018 | 15,654,665 | 17,471,287 | 16,425,509 | 4,867,916 | 49,915,353 | 43,777,420 | 1,174,420 | 25,843,439 | 175,130,010 |
|  | 2019 | 15,821,555 | 17,813,906 | 16,639,699 | 4,883,551 | 50,969,206 | 44,322,672 | 1,190,649 | 26,293,704 | 177,934,944 |
|  | 2020 | 15,990,223 | 18,163,244 | 16,856,683 | 4,899,238 | 52,045,308 | 44,874,716 | 1,207,103 | 26,751,814 | 180,788,329 |
|  | 2021 | 16,160,690 | 18,519,433 | 17,076,495 | 4,914,974 | 53,144,130 | 45,433,635 | 1,223,784 | 27,217,905 | 183,691,047 |
|  | 2022 | 16,332,974 | 18,882,607 | 17,299,175 | 4,930,761 | 54,266,152 | 45,999,516 | 1,240,695 | 27,692,117 | 186,643,996 |
|  | 2023 | 16,507,094 | 19,252,903 | 17,524,758 | 4,946,599 | 55,411,862 | 46,572,444 | 1,257,840 | 28,174,591 | 189,648,091 |
|  | 2024 | 16,683,071 | 19,630,461 | 17,753,282 | 4,962,488 | 56,581,762 | 47,152,509 | 1,275,222 | 28,665,471 | 192,704,264 |
|  | 2025 | 16,860,924 | 20,015,422 | 17,984,787 | 4,978,427 | 57,776,361 | 47,739,798 | 1,292,844 | 29,164,903 | 195,813,466 |

| System Losses - Stabilized Load Growth (SLG) Scenario |
| --- |
|  | Average System Loss Rate per EDC |  |
|  | 5.77% | 7.87% | 8.87% | 6.49% | 6.65% | 7.18% | 5.65% | 6.53% |  |
|  | Duquesne | MetEd | Penelec | PennPower | PECO | PPL | UGI | West Penn | Total MWh |
| System Losses (MWh) by Compliance Year | 2007 | 803,683 | 1,110,810 | 1,263,229 | 304,805 | 2,637,920 | 2,744,325 | 57,075 | 1,394,798 | 10,316,645 |
|  | 2008 | 812,251 | 1,132,593 | 1,279,702 | 305,784 | 2,693,614 | 2,778,506 | 57,863 | 1,419,100 | 10,479,412 |
|  | 2009 | 820,910 | 1,154,804 | 1,296,390 | 306,766 | 2,750,484 | 2,813,112 | 58,663 | 1,443,824 | 10,644,952 |
|  | 2010 | 829,662 | 1,177,450 | 1,313,295 | 307,751 | 2,808,554 | 2,848,150 | 59,474 | 1,468,980 | 10,813,315 |
|  | 2011 | 821,365 | 1,165,675 | 1,300,162 | 304,674 | 2,780,469 | 2,819,668 | 58,879 | 1,454,290 | 10,705,181 |
|  | 2012 | 830,122 | 1,188,535 | 1,317,116 | 305,652 | 2,839,172 | 2,854,787 | 59,693 | 1,479,628 | 10,874,704 |
|  | 2013 | 813,068 | 1,153,900 | 1,287,028 | 301,596 | 2,752,383 | 2,791,186 | 58,284 | 1,439,600 | 10,597,046 |
|  | 2014 | 821,736 | 1,176,529 | 1,303,811 | 302,565 | 2,810,493 | 2,825,951 | 59,089 | 1,464,682 | 10,764,856 |
|  | 2015 | 809,410 | 1,158,881 | 1,284,254 | 298,026 | 2,768,336 | 2,783,562 | 58,203 | 1,442,711 | 10,603,383 |
|  | 2016 | 818,039 | 1,181,607 | 1,301,001 | 298,983 | 2,826,783 | 2,818,231 | 59,007 | 1,467,847 | 10,771,500 |
|  | 2017 | 805,768 | 1,163,883 | 1,281,486 | 294,499 | 2,784,381 | 2,775,958 | 58,122 | 1,445,830 | 10,609,927 |
|  | 2018 | 814,359 | 1,186,707 | 1,298,197 | 295,445 | 2,843,167 | 2,810,533 | 58,925 | 1,471,020 | 10,778,352 |
|  | 2019 | 814,359 | 1,186,707 | 1,298,197 | 295,445 | 2,843,167 | 2,810,533 | 58,925 | 1,471,020 | 10,778,352 |
|  | 2020 | 814,359 | 1,186,707 | 1,298,197 | 295,445 | 2,843,167 | 2,810,533 | 58,925 | 1,471,020 | 10,778,352 |
|  | 2021 | 814,359 | 1,186,707 | 1,298,197 | 295,445 | 2,843,167 | 2,810,533 | 58,925 | 1,471,020 | 10,778,352 |
|  | 2022 | 814,359 | 1,186,707 | 1,298,197 | 295,445 | 2,843,167 | 2,810,533 | 58,925 | 1,471,020 | 10,778,352 |
|  | 2023 | 814,359 | 1,186,707 | 1,298,197 | 295,445 | 2,843,167 | 2,810,533 | 58,925 | 1,471,020 | 10,778,352 |
|  | 2024 | 814,359 | 1,186,707 | 1,298,197 | 295,445 | 2,843,167 | 2,810,533 | 58,925 | 1,471,020 | 10,778,352 |
|  | 2025 | 814,359 | 1,186,707 | 1,298,197 | 295,445 | 2,843,167 | 2,810,533 | 58,925 | 1,471,020 | 10,778,352 |

| System Losses - Business as Usual (BAU) Scenario |
| --- |
|  | Average System Loss Rate per EDC |  |
|  | 5.77% | 7.87% | 8.87% | 6.49% | 6.65% | 7.18% | 5.65% | 6.53% |  |
|  | Duquesne | MetEd | Penelec | PennPower | PECO | PPL | UGI | West Penn | Total MWh |
| System Losses (MWh) by Compliance Year | 2007 | 803,683 | 1,110,810 | 1,263,229 | 304,805 | 2,637,920 | 2,744,325 | 57,075 | 1,394,798 | 10,316,645 |
|  | 2008 | 812,251 | 1,132,593 | 1,279,702 | 305,784 | 2,693,614 | 2,778,506 | 57,863 | 1,419,100 | 10,479,412 |
|  | 2009 | 820,910 | 1,154,804 | 1,296,390 | 306,766 | 2,750,484 | 2,813,112 | 58,663 | 1,443,824 | 10,644,952 |
|  | 2010 | 829,662 | 1,177,450 | 1,313,295 | 307,751 | 2,808,554 | 2,848,150 | 59,474 | 1,468,980 | 10,813,315 |
|  | 2011 | 838,507 | 1,200,540 | 1,330,420 | 308,740 | 2,867,850 | 2,883,624 | 60,296 | 1,494,573 | 10,984,550 |
|  | 2012 | 847,446 | 1,224,083 | 1,347,769 | 309,731 | 2,928,399 | 2,919,540 | 61,129 | 1,520,613 | 11,158,709 |
|  | 2013 | 856,480 | 1,248,088 | 1,365,344 | 310,726 | 2,990,226 | 2,955,903 | 61,973 | 1,547,106 | 11,335,846 |
|  | 2014 | 865,611 | 1,272,564 | 1,383,148 | 311,724 | 3,053,358 | 2,992,719 | 62,830 | 1,574,061 | 11,516,014 |
|  | 2015 | 874,839 | 1,297,519 | 1,401,184 | 312,726 | 3,117,822 | 3,029,993 | 63,698 | 1,601,486 | 11,699,268 |
|  | 2016 | 884,165 | 1,322,964 | 1,419,456 | 313,730 | 3,183,648 | 3,067,732 | 64,578 | 1,629,388 | 11,885,662 |
|  | 2017 | 893,591 | 1,348,908 | 1,437,966 | 314,738 | 3,250,864 | 3,105,941 | 65,471 | 1,657,777 | 12,075,255 |
|  | 2018 | 903,117 | 1,375,360 | 1,456,717 | 315,749 | 3,319,499 | 3,144,626 | 66,375 | 1,686,660 | 12,268,104 |
|  | 2019 | 912,745 | 1,402,332 | 1,475,713 | 316,763 | 3,389,583 | 3,183,793 | 67,293 | 1,716,046 | 12,464,267 |
|  | 2020 | 922,475 | 1,429,832 | 1,494,956 | 317,780 | 3,461,147 | 3,223,447 | 68,223 | 1,745,944 | 12,663,805 |
|  | 2021 | 932,310 | 1,457,872 | 1,514,451 | 318,801 | 3,534,221 | 3,263,595 | 69,165 | 1,776,364 | 12,866,779 |
|  | 2022 | 942,249 | 1,486,461 | 1,534,199 | 319,825 | 3,608,838 | 3,304,244 | 70,121 | 1,807,313 | 13,073,250 |
|  | 2023 | 952,294 | 1,515,611 | 1,554,205 | 320,852 | 3,685,031 | 3,345,399 | 71,090 | 1,838,801 | 13,283,284 |
|  | 2024 | 962,446 | 1,545,333 | 1,574,472 | 321,883 | 3,762,832 | 3,387,066 | 72,073 | 1,870,838 | 13,496,943 |
|  | 2025 | 972,706 | 1,575,638 | 1,595,004 | 322,917 | 3,842,276 | 3,429,252 | 73,068 | 1,903,433 | 13,714,295 |

| Climate Impact ((Consumption + Losses) X CO2)) (SLG) Scenario |
| --- |
|  | Consumption | Losses | Total MWh | CO2 Tons | MMTCO2 |
| Consumption (MWh) by Compliance Year | 2007 | 147,237,195 | 10,316,645 | 157,553,840 | 100,755,681 | 91.39 |
|  | 2008 | 149,562,879 | 10,479,412 | 160,042,292 | 102,347,045 | 92.83 |
|  | 2009 | 151,928,332 | 10,644,952 | 162,573,284 | 103,965,615 | 94.30 |
|  | 2010 | 154,334,271 | 10,813,315 | 165,147,585 | 105,611,881 | 95.79 |
|  | 2011 | 152,790,928 | 10,705,181 | 163,496,109 | 104,555,762 | 94.83 |
|  | 2012 | 155,213,613 | 10,874,704 | 166,088,317 | 106,213,479 | 96.34 |
|  | 2013 | 151,247,549 | 10,597,046 | 161,844,595 | 103,499,619 | 93.87 |
|  | 2014 | 153,645,763 | 10,764,856 | 164,410,619 | 105,140,591 | 95.36 |
|  | 2015 | 151,330,748 | 10,603,383 | 161,934,132 | 103,556,877 | 93.93 |
|  | 2016 | 153,743,823 | 10,771,500 | 164,515,322 | 105,207,549 | 95.42 |
|  | 2017 | 151,437,665 | 10,609,927 | 162,047,593 | 103,629,435 | 93.99 |
|  | 2018 | 153,844,992 | 10,778,352 | 164,623,344 | 105,276,629 | 95.49 |
|  | 2019 | 153,844,992 | 10,778,352 | 164,623,344 | 105,276,629 | 95.49 |
|  | 2020 | 153,844,992 | 10,778,352 | 164,623,344 | 105,276,629 | 95.49 |
|  | 2021 | 153,844,992 | 10,778,352 | 164,623,344 | 105,276,629 | 95.49 |
|  | 2022 | 153,844,992 | 10,778,352 | 164,623,344 | 105,276,629 | 95.49 |
|  | 2023 | 153,844,992 | 10,778,352 | 164,623,344 | 105,276,629 | 95.49 |
|  | 2024 | 153,844,992 | 10,778,352 | 164,623,344 | 105,276,629 | 95.49 |
|  | 2025 | 153,844,992 | 10,778,352 | 164,623,344 | 105,276,629 | 95.49 |

| Climate Impact ((Consumption + Losses) X CO2)) BAU Scenario |
| --- |
|  | Consumption | Losses | Total MWh | CO2 Tons | MMTCO2 |
| Consumption (MWh) by Compliance Year | 2007 | 147,237,195 | 10,316,645 | 157,553,840 | 100,755,681 | 91.39 |
|  | 2008 | 149,562,879 | 10,479,412 | 160,042,292 | 102,347,045 | 92.83 |
|  | 2009 | 151,928,332 | 10,644,952 | 162,573,284 | 103,965,615 | 94.30 |
|  | 2010 | 154,334,271 | 10,813,315 | 165,147,585 | 105,611,881 | 95.79 |
|  | 2011 | 156,781,428 | 10,984,550 | 167,765,977 | 107,286,342 | 97.31 |
|  | 2012 | 159,270,547 | 11,158,709 | 170,429,257 | 108,989,510 | 98.85 |
|  | 2013 | 161,802,389 | 11,335,846 | 173,138,235 | 110,721,901 | 100.42 |
|  | 2014 | 164,377,726 | 11,516,014 | 175,893,740 | 112,484,047 | 102.02 |
|  | 2015 | 166,997,346 | 11,699,268 | 178,696,613 | 114,276,484 | 103.65 |
|  | 2016 | 169,662,052 | 11,885,662 | 181,547,714 | 116,099,763 | 105.30 |
|  | 2017 | 172,372,662 | 12,075,255 | 184,447,917 | 117,954,443 | 106.98 |
|  | 2018 | 175,130,010 | 12,268,104 | 187,398,113 | 119,841,094 | 108.70 |
|  | 2019 | 177,934,944 | 12,464,267 | 190,399,210 | 121,760,295 | 110.44 |
|  | 2020 | 180,788,329 | 12,663,805 | 193,452,134 | 123,712,639 | 112.21 |
|  | 2021 | 183,691,047 | 12,866,779 | 196,557,826 | 125,698,729 | 114.01 |
|  | 2022 | 186,643,996 | 13,073,250 | 199,717,246 | 127,719,179 | 115.84 |
|  | 2023 | 189,648,091 | 13,283,284 | 202,931,375 | 129,774,614 | 117.71 |
|  | 2024 | 192,704,264 | 13,496,943 | 206,201,208 | 131,865,672 | 119.60 |
|  | 2025 | 195,813,466 | 13,714,295 | 209,527,761 | 133,993,003 | 121.53 |

| CO2 Reduction SLG vs. BAU |
| --- |
|  | Total MWh | MMTCO2 |
|  | SLG | BAU | Delta | SLG | BAU | Delta |
| Consumption (MWh) by Compliance Year | 2007 | 157,553,840 | 157,553,840 | 0 | 91.39 | 91.39 | 0.00 |
|  | 2008 | 160,042,292 | 160,042,292 | 0 | 92.83 | 92.83 | 0.00 |
|  | 2009 | 162,573,284 | 162,573,284 | 0 | 94.30 | 94.30 | 0.00 |
|  | 2010 | 165,147,585 | 165,147,585 | 0 | 95.79 | 95.79 | 0.00 |
|  | 2011 | 163,496,109 | 167,765,977 | 4,269,868 | 94.83 | 97.31 | 2.48 |
|  | 2012 | 166,088,317 | 170,429,257 | 4,340,939 | 96.34 | 98.85 | 2.52 |
|  | 2013 | 161,844,595 | 173,138,235 | 11,293,640 | 93.87 | 100.42 | 6.55 |
|  | 2014 | 164,410,619 | 175,893,740 | 11,483,121 | 95.36 | 102.02 | 6.66 |
|  | 2015 | 161,934,132 | 178,696,613 | 16,762,482 | 93.93 | 103.65 | 9.72 |
|  | 2016 | 164,515,322 | 181,547,714 | 17,032,392 | 95.42 | 105.30 | 9.88 |
|  | 2017 | 162,047,593 | 184,447,917 | 22,400,325 | 93.99 | 106.98 | 12.99 |
|  | 2018 | 164,623,344 | 187,398,113 | 22,774,769 | 95.49 | 108.70 | 13.21 |
|  | 2019 | 164,623,344 | 190,399,210 | 25,775,866 | 95.49 | 110.44 | 14.95 |
|  | 2020 | 164,623,344 | 193,452,134 | 28,828,789 | 95.49 | 112.21 | 16.72 |
|  | 2021 | 164,623,344 | 196,557,826 | 31,934,481 | 95.49 | 114.01 | 18.52 |
|  | 2022 | 164,623,344 | 199,717,246 | 35,093,902 | 95.49 | 115.84 | 20.36 |
|  | 2023 | 164,623,344 | 202,931,375 | 38,308,030 | 95.49 | 117.71 | 22.22 |
|  | 2024 | 164,623,344 | 206,201,208 | 41,577,863 | 95.49 | 119.60 | 24.12 |
|  | 2025 | 164,623,344 | 209,527,761 | 44,904,417 | 95.49 | 121.53 | 26.05 |

| Climate Impact ((Consumption + Losses) X CO2)) (SLG) Scenario |
| --- |
|  | Consumption | Losses | Total MWh | CO2 Tons | MMTCO2 |
| Consumption (MWh) by Compliance Year | 2007 | 147,237,195 | 10,316,645 | 157,553,840 | 100,755,681 | 91.39 |
|  | 2008 | 149,562,879 | 10,479,412 | 160,042,292 | 102,347,045 | 92.83 |
|  | 2009 | 151,928,332 | 10,644,952 | 162,573,284 | 103,965,615 | 94.30 |
|  | 2010 | 154,334,271 | 10,813,315 | 165,147,585 | 105,611,881 | 95.79 |
|  | 2011 | 155,238,085 | 10,876,416 | 166,114,501 | 106,230,224 | 96.35 |
|  | 2012 | 157,702,733 | 11,048,864 | 168,751,597 | 107,916,646 | 97.88 |
|  | 2013 | 157,122,998 | 11,007,993 | 168,130,991 | 107,519,769 | 97.52 |
|  | 2014 | 159,624,073 | 11,182,965 | 170,807,038 | 109,231,101 | 99.07 |
|  | 2015 | 162,168,158 | 11,360,933 | 173,529,091 | 110,971,854 | 100.65 |
|  | 2016 | 164,756,031 | 11,541,953 | 176,297,984 | 112,742,561 | 102.26 |
|  | 2017 | 167,388,487 | 11,726,078 | 179,114,565 | 114,543,765 | 103.89 |
|  | 2018 | 170,066,336 | 11,913,366 | 181,979,702 | 116,376,019 | 105.55 |
|  | 2019 | 170,066,336 | 11,913,366 | 181,979,702 | 116,376,019 | 105.55 |
|  | 2020 | 170,066,336 | 11,913,366 | 181,979,702 | 116,376,019 | 105.55 |
|  | 2021 | 170,066,336 | 11,913,366 | 181,979,702 | 116,376,019 | 105.55 |
|  | 2022 | 170,066,336 | 11,913,366 | 181,979,702 | 116,376,019 | 105.55 |
|  | 2023 | 170,066,336 | 11,913,366 | 181,979,702 | 116,376,019 | 105.55 |
|  | 2024 | 170,066,336 | 11,913,366 | 181,979,702 | 116,376,019 | 105.55 |
|  | 2025 | 170,066,336 | 11,913,366 | 181,979,702 | 116,376,019 | 105.55 |

| Climate Impact ((Consumption + Losses) X CO2)) BAU Scenario |
| --- |
|  | Consumption | Losses | Total MWh | CO2 Tons | MMTCO2 |
| Consumption (MWh) by Compliance Year | 2007 | 147,237,195 | 10,316,645 | 157,553,840 | 100,755,681 | 91.39 |
|  | 2008 | 149,562,879 | 10,479,412 | 160,042,292 | 102,347,045 | 92.83 |
|  | 2009 | 151,928,332 | 10,644,952 | 162,573,284 | 103,965,615 | 94.30 |
|  | 2010 | 154,334,271 | 10,813,315 | 165,147,585 | 105,611,881 | 95.79 |
|  | 2011 | 156,781,428 | 10,984,550 | 167,765,977 | 107,286,342 | 97.31 |
|  | 2012 | 159,270,547 | 11,158,709 | 170,429,257 | 108,989,510 | 98.85 |
|  | 2013 | 161,802,389 | 11,335,846 | 173,138,235 | 110,721,901 | 100.42 |
|  | 2014 | 164,377,726 | 11,516,014 | 175,893,740 | 112,484,047 | 102.02 |
|  | 2015 | 166,997,346 | 11,699,268 | 178,696,613 | 114,276,484 | 103.65 |
|  | 2016 | 169,662,052 | 11,885,662 | 181,547,714 | 116,099,763 | 105.30 |
|  | 2017 | 172,372,662 | 12,075,255 | 184,447,917 | 117,954,443 | 106.98 |
|  | 2018 | 175,130,010 | 12,268,104 | 187,398,113 | 119,841,094 | 108.70 |
|  | 2019 | 177,934,944 | 12,464,267 | 190,399,210 | 121,760,295 | 110.44 |
|  | 2020 | 180,788,329 | 12,663,805 | 193,452,134 | 123,712,639 | 112.21 |
|  | 2021 | 183,691,047 | 12,866,779 | 196,557,826 | 125,698,729 | 114.01 |
|  | 2022 | 186,643,996 | 13,073,250 | 199,717,246 | 127,719,179 | 115.84 |
|  | 2023 | 189,648,091 | 13,283,284 | 202,931,375 | 129,774,614 | 117.71 |
|  | 2024 | 192,704,264 | 13,496,943 | 206,201,208 | 131,865,672 | 119.60 |
|  | 2025 | 195,813,466 | 13,714,295 | 209,527,761 | 133,993,003 | 121.53 |

| CO2 Reduction SLG vs. BAU |
| --- |
|  | Total MWh | MMTCO2 |
|  | SLG | BAU | Delta | SLG | BAU | Delta |
| Consumption (MWh) by Compliance Year | 2007 | 157,553,840 | 157,553,840 | 0 | 91.39 | 91.39 | 0.00 |
|  | 2008 | 160,042,292 | 160,042,292 | 0 | 92.83 | 92.83 | 0.00 |
|  | 2009 | 162,573,284 | 162,573,284 | 0 | 94.30 | 94.30 | 0.00 |
|  | 2010 | 165,147,585 | 165,147,585 | 0 | 95.79 | 95.79 | 0.00 |
|  | 2011 | 166,114,501 | 167,765,977 | 1,651,476 | 96.35 | 97.31 | 0.96 |
|  | 2012 | 168,751,597 | 170,429,257 | 1,677,660 | 97.88 | 98.85 | 0.97 |
|  | 2013 | 168,130,991 | 173,138,235 | 5,007,244 | 97.52 | 100.42 | 2.90 |
|  | 2014 | 170,807,038 | 175,893,740 | 5,086,702 | 99.07 | 102.02 | 2.95 |
|  | 2015 | 173,529,091 | 178,696,613 | 5,167,523 | 100.65 | 103.65 | 3.00 |
|  | 2016 | 176,297,984 | 181,547,714 | 5,249,731 | 102.26 | 105.30 | 3.04 |
|  | 2017 | 179,114,565 | 184,447,917 | 5,333,352 | 103.89 | 106.98 | 3.09 |
|  | 2018 | 181,979,702 | 187,398,113 | 5,418,411 | 105.55 | 108.70 | 3.14 |
|  | 2019 | 181,979,702 | 190,399,210 | 8,419,509 | 105.55 | 110.44 | 4.88 |
|  | 2020 | 181,979,702 | 193,452,134 | 11,472,432 | 105.55 | 112.21 | 6.65 |
|  | 2021 | 181,979,702 | 196,557,826 | 14,578,124 | 105.55 | 114.01 | 8.46 |
|  | 2022 | 181,979,702 | 199,717,246 | 17,737,544 | 105.55 | 115.84 | 10.29 |
|  | 2023 | 181,979,702 | 202,931,375 | 20,951,673 | 105.55 | 117.71 | 12.15 |
|  | 2024 | 181,979,702 | 206,201,208 | 24,221,506 | 105.55 | 119.60 | 14.05 |
|  | 2025 | 181,979,702 | 209,527,761 | 27,548,059 | 105.55 | 121.53 | 15.98 |