Waste

Summary List of Work Plans Analyzed

| Work Plan No. | Work Plan Name | Annual Results (2020) | Cumulative Results (2009-2020) |
| --- | --- | --- | --- |
|  |  | GHG Reductions (MMtCO2e) | Costs (Million $) | Cost-Effectiveness ($/tCO2e) | GHG Reductions (MMtCO2e) | Costs (NPV, Million $) | Cost-Effectiveness ($/tCO2e) |
| 1 | Landfill Methane Displacement of Fossil Fuels | 0.71 |  |  | 4.14 |  |  |
| 2 | Statewide Recycling Initiative | 8.67 |  |  | 54.3 |  |  |
| 3 | Solid Waste Management Initiative |  |  |  |  |  |  |
| 4 | Improved Efficiency at Wastewater Treatment Facilities | 8.3 x 10-4 | (0.56) | (1,300) | 0.010 | (4.4) | (440) |
| 5 | Waste-to-Energy Digesters |  |  |  |  |  |  |
| 6 | Waste-to-Energy MSW |  |  |  |  |  |  |
| Sector Total After Adjusting for Overlaps |  |  |  |  |  |  |
| Reductions From Recent Actions |  |  |  |  |  |  |
| Sector Total Plus Recent Actions |  |  |  |  |  |  |

GHG = greenhouse gas; MMtCO2e = million metric tons of carbon dioxide equivalent; $/tCO2e = dollars per metric ton of carbon dioxide equivalent; NPV = net present value; TBD = to be determined.

Negative values in the Cost and the Cost-Effectiveness columns represent net cost savings.

The numbering used to denote the above draft work plans is for reference purposes only; it does not reflect prioritization among these important draft work plans.

Waste-1

Landfill Methane Displacement of Fossil Fuels

Work Plan for Potential GHG Reduction

Lead Staff Contact:  Richard Illig (717) 772-5834

Summary:  Landfill methane resources and projects will be identified, assessed, and promoted to decrease fossil fuel use in business thermal applications, or otherwise displace the use of commercial natural gas resources.  Maximizing the use of landfill methane as a fuel reduces greenhouse gas emission of methane and serves to offset emissions of carbon dioxide from the use of fossil fuels such as coal, oil, and natural gas.

Goals:  Increase landfill gas utilization by 16% (from the current 69% beneficial use to 80% beneficial use).

Implementation Period:  Achieve 80% beneficial use of landfill gas collected by 2025.

Parties Affected/Implementing Parties:  Pennsylvania Department of Environmental Protection (DEP), PENNDOT, PUC, & DCED, Landfill owners/operators

Data sources/Assumptions/Methods for GHG:

Landfill gas resources will be assessed to determine the degree to which fossil fuel use for the purpose of generating heat can be displaced.  Landfill gas thermal use projects include conversion to commercial grade “pipeline-quality” methane (natural gas) and direct use applications in industrial or commercial equipment.

For the purposes of this report landfill gas electricity generation projects will not be addressed.

Operating municipal waste landfills are evaluated annually.  Key data collected from DEP Solid Waste Program Landfill Annual Operation Reports includes:

- site total waste capacity and the volume of disposed waste

- landfill gas collection rates and gas quality relative to methane content

- details of landfill gas projects, and

- thermal energy benefits

Landfill gas collection systems efficiency is estimated between 60 to 85 percent by the U.S. EPA.  Efficiencies up to 90 and 95 percent have been calculated using gas measurements taken at modern landfill operations1.  For the purposes of this report landfill gas collection efficiency will be estimated at 75 percent for the following reasons:

- Landfill gas project investments rely on optimizing landfill gas volume and quality relative to methane content.

- PA landfills are well maintained.  Installed gas collection systems are relatively new.

- Improved technologies and operational practices are used in landfill construction.  Gas wells are routinely monitored and calibrated.

Historical Inventory of Landfill Emissions

A historical GHG emissions inventory was developed based on DEP waste reports from 1990-2008 and historical per capita waste generation.  Historical landfilling rates were estimated by back-calculating from current rates.  Figure 1 illustrates GHG emissions including fugitive emissions after accounting for 10% oxidation and thermal destruction  of methane through flaring and gas-to-energy (GTE) projects.  Landfills with GTE projects and flares (backup or otherwise) accounted for about 94% of emissions in 2000 while landfills with flares alone accounted for about 3.7% and uncontrolled landfills accounted for about 2.5%,, according to DEP records.

Figure 1  Historical Emissions by Landfill Control Type

Collection efficiency at the landfills is assumed to be 75%.  Emissions for GTE and Flared landfills include 25% escaped (fugitive) emissions.  Table 1 shows the 2000 emissions broken down by landfill control type.

Table 1  2000 Emissions  by Landfill Control Type

|  | Gross Methane Generation by WIP (cubic meters CH4) | Fugitive and Net Emissions after Themal Destruction and Oxidation (MMTCO2e) |
| --- | --- | --- |
| GTE, Flare | 698 | 3.17 |
| Flare | 46 | 0.21 |
| Uncontrolled | 51.0 | 0.66 |
| Total | 795 | 4.04 |

(note 1 cubic meter = 35.3 cubic feet)

Emissions Estimates

The goal of this workplan is to increase the percent of landfill gas applied to a beneficial use (rather than flaring) from 69% to 80% by 2025.

Based on 2007 report data Pennsylvania landfills collect over 62,700MMscfy (million standard cubic feet per year) of landfill gas.  (This equals 1776 million cubic meters; Landfill gas is ~50% CH4; the inventory records 743 million cubic meters of CH4 were generated in 2007,)  Landfill gas contains 450 Btu per cubic foot.  Currently over 11,700MMscfy (~19%) is used in thermal projects that displace fossil fuel use, over 19,500MMscfy ( 31%) is flared, and about 31,500MMscfy (50%) is used to generate electricity.

The 2009-2020 landfill gas emissions were estimated using the waste management scenario outlined in workplan 2 (see below).  It was assumed that any uncontrolled landfills would be converted to GTE/flared collection over the policy period.  Table 2 summarizes the methane emissions that would be captured by GTE projects and flares for beneficial use according to the new goal.

Table 2  Methane Emissions Captured by GTE and Flares for Beneficial Use

|  | Emissions captured by GTE & Flares (million m3 CH4) | Beneficial Use Goal | BAU beneficial use | Emissions applied to beneficial use (million m3 CH4) | Beneficial use savings over BAU (million m3 CH4) | MMtCO2e of savings after thermal destruction |
| --- | --- | --- | --- | --- | --- | --- |
| 2009 | 577 | 69% | 69% | 398 | 0.00 | 0.00 |
| 2010 | 587 | 70% | 69% | 409 | 4.04 | 0.06 |
| 2011 | 596 | 70% | 69% | 419 | 8.19 | 0.12 |
| 2012 | 604 | 71% | 69% | 430 | 12.47 | 0.18 |
| 2013 | 613 | 72% | 69% | 440 | 16.85 | 0.24 |
| 2014 | 621 | 72% | 69% | 450 | 21.34 | 0.30 |
| 2015 | 628 | 73% | 69% | 459 | 25.92 | 0.37 |
| 2016 | 635 | 74% | 69% | 469 | 30.57 | 0.44 |
| 2017 | 642 | 75% | 69% | 478 | 35.32 | 0.50 |
| 2018 | 649 | 75% | 69% | 488 | 40.15 | 0.57 |
| 2019 | 655 | 76% | 69% | 497 | 45.06 | 0.64 |
| 2020 | 662 | 77% | 69% | 507 | 50.06 | 0.71 |
|  |  |  |  | TOTAL | 290 | 4.14 |

The total GHG savings from the increase in beneficial use would be 4.14 MMtCO2e.  Note that these GHG savings would not be deducted from the waste sector since the methane diverted to beneficial use would have been destroyed through flaring.  These savings would be seen in the industry or residential/commercial sectors depending on what kind of beneficial use project they are applied to.  The total of 290 million m3 of CH4 would have a heat content of 10.4x1012 Btus, the equivalent of 10.4billion scfy of natural gas, or 73 million gallons heating oil, or 516,000 shorts tons of coal.

Data sources/Assumptions/Methods for Costs:

- Estimating direct use project costs at $10/MMBtu, plus $0.45/MMBtu operation & maintenance costs per year.  Developing an additional 5,528MMscfy or 2,487,600MMBtu would cost over $24,876,000 plus $3,607,000 or nearly $30 million.

- Approximately $1 million per mile of pipeline based on direct use projects in PA.

- Retrofit costs for burners and boilers to utilize landfill gas for fuel approximately $30,000 - $300,000 depending on size and type of retrofit.

- State permitting costs are undetermined but may include:

  - Solid Waste beneficial use permit for landfill gas utilization

  - Air Quality Program notifications and operational permit for landfill gas processing and gas end-use equipment.

  - Storm water permitting and/or erosion and sedimentation controls may be needed.

  - Historic preservation or endangered species act may apply to pipeline right-of-ways.  Pipeline costs would increase accordingly.

- Local permitting may also apply.

Other Considerations/Notes/Implementation Mechanisms:

- Provide tax credits to municipalities for the installation of beneficial use projects.

- Should not apply to closed landfills.

- Dependent on landfill permitting.

- Require all active and recently closed landfills containing greater than 1 million tons of disposed waste to install gas collection systems.

- Prioritize right of way access for landfill gas pipeline projects.

- Work with landfill gas project developers to identify the nearest economical end uses.

- Prioritize landfill gas projects presenting economic development benefits or that otherwise enhance the application of renewable energy technologies.

- Require landfill gas electrical and thermal use projects to incorporate waste heat recovery.  This could help maximize fossil fuel displacement.

- Encourage projects that utilize all landfill gas generated at a site and/or projects able to grow with landfill site gas generation.

- Promote the high reliability of landfill gas projects.  Most projects are able to operate continuously over extended periods of time other than for periodic maintenance.

- Prioritize self-powered thermal landfill gas projects that include an electric generation component.

Potential Overlap

- Solid Waste Work Plan

- Recycling Work Plan

- Industry and/or Residential/Commercial sectors depending on what fuels the beneficial use projects would replace

Waste-2

Statewide Recycling Initiative

Work Plan for Potential GHG Reduction Measure

Lead Staff Contact:	Gregory Harder (717) 787-0114

Larry Holley (717) 787-7382

Initiative Summary:  Support the expansion of statewide recycling to increase the amount of materials recycled.  Achieve GHG reductions equivalent to 86% of the Commonwealth’s total recycling potential. This goal is equivalent to a 52.7% recycling rate, based on interpolation of 2005 baseline data and composition studies of landfilled and recycled waste.

Goals:  Achieve 86% of Pennsylvania's recycling potential by 2025.

Implementation Period:

| YEAR | ACTION | % OF GOAL* | GHG REDUCTION | GHG REDUCTION |
| --- | --- | --- | --- | --- |
| 2000 | Historical |  | 2.1 MMTCE | 7.7 MMTCO2 |
| 2012 | Legislation and Regulations in Place | 20% | 3.0 MMTCE | 11 MMTCO2 |
| 2015 | Increased Non-regulatory Enhancements | 50% | 3.8 MMTCE | 14 MMTCO2 |
| 2020 | Program Maintained and Improvement | 80% | 4.5 MMTCE | 17 MMTCO2 |
| 2025 | Completion | 100% | 5.0 MMTCE | 18 MMTCO2* |

* Total in Pennsylvania, including reductions due to recycling that is already happening. The incremental reduction in 2025 is estimated to be approximately 2.9 MMTCE, or 11 MMTCO2.

Parties Affected/Implementing Parties:  DEP

Data Sources/Assumptions/Methods for GHG:

Baseline Recycling Composition Data Source:  PA DEP. 2005. “Pennsylvania Recovered Material Composition Study.” Available on-line at: http://www.dep.state.pa.us/dep/deputate/airwaste/wm/RECYCLE/document/Rec_Mat_Comp.pdf

Baseline Landfill Waste Composition Source: PA DEP. 2003. “Statewide Municipal Waste Composition Study.”  Section 4. Available on-line at: http://www.dep.state.pa.us/dep/deputate/airwaste/wm/RECYCLE/Waste_Comp/Study.htm.

CCS utilized the landfill and recycling composition studies to determine the percentage of the total waste disposed of in landfills or recycled. These percentages were multiplied by the waste landfilled and waste recycled in 2005 shown in Table 2. After adding 86% of the landfilled recyclables from Attachment 3 (recycling for material types adjusted to 2005 disposal and recycling data) to the baseline recycling, the resulting recycling rate was 52.7%. Assuming that the composition of waste landfilled and recycled does not change through 2025, the recycling rate needed to meet the goals of this Work Plan is 52.7% (recycling proportion of all waste generated).

Based on data analyzed by the Northeast Recycling Council’s (NERC) Environmental Benefits Calculator, Pennsylvania saved 2.5 million metric tons of carbon equivalent (MMTCE) or 9 million metric tons of carbon dioxide equivalent (MMTCO2e) as a result of recycling approximately 4.9 million tons of materials in 2005.  There is potential to reduce an additional 2.9 MMTCE or 11 MMTCO2e assuming the recycling of an additional 4 million tons of Pennsylvania generated recyclables identified as discarded in landfills and incinerators by the Statewide Municipal Waste Composition Study (April 2003).

More than 5.4 million MMTCE or 20 MMTCO2e could be avoided annually if recyclable materials being disposed were added to the materials presently recovered from the municipal waste stream through recycling programs in the Commonwealth.  These materials include newspaper, corrugated cardboard, office paper, magazines, mixed paper, plastic bottles, film plastic, rigid plastic, glass, steel and aluminum cans, steel scrap and other metals.  Additional savings above and beyond this projection could be realized if comprehensive programs were developed for the collection and recycling of wood waste, textiles, and carpet.

Energy conserved from manufacturing products using recycled feedstock rather than virgin raw materials, or non-renewable resources, resulted in the savings of 98 trillion British Thermal Units of energy in 2005, enough to power over 941,000 Pennsylvania homes for year or the equivalent of conserving 786 million gallons of gasoline.

Emission and energy credit accrued by our recycling efforts could be recognized as a tradable commodity that may help achieve the Commonwealth's sustainability goals.

PA DEP could target recycling programs to specifically begin or increase collecting those materials that provide the maximum greenhouse gas reductions.  To further stimulate recycling opportunities, PA DEP could ultimately ban those materials from disposal or processing.  Aluminum, steel, plastics, cardboard and paper should be initially targeted as these materials will yield the greatest reductions.

Act 101, the Municipal Waste, Planning Recycling and Waste Act Reduction of 1988, provides the foundation for recycling that has resulted in comprehensive environmental and economic benefits for Pennsylvania.  The Act provides for a $2 per ton recycling fee on waste disposed or processed at municipal waste landfills and resource recovery facilities in the Commonwealth.  The Recycling Fee generates approximately $47 million dollars annually to a Recycling Fund administered by Pa. DEP.  The Recycling Fund provides support to local governments for implementation of recycling programs.  The Recycling Fee also supports the stimulation of markets for recyclable materials. The Department is focusing Act 101 funds on programs geared towards financial sustainability including those that are targeting new materials that were previously disposed.  Increasing the amount of materials recycled will provide direct reduction in greenhouse gas emissions.

Pennsylvania’s recycling program provides annual economic benefits in excess of $23 billion and nearly 82,000 jobs (National Recycling Council, REI Study, 2001).  The program also provides extensive environmental benefits.  The 2.5 MMTCE eliminated in 2005 by recycling amounted to a savings of approximately 3 percent of all greenhouse gas emissions in the Commonwealth.  Also, recycling conserved considerable natural resources.  By recycling almost 1.2 million tons of steel cans, appliances and similar materials in 2005, Pennsylvania industries saved almost 1.5 million tons of iron ore, 829,786 tons of coal and 71,124 tons of limestone.  Through recycling newspapers, phone books, office paper, cardboard and mixed paper, the Commonwealth saved the equivalent of 78 million tree seedlings grown for 10 years.  These trees would sequester carbon dioxide from the atmosphere and store it in their wood.

Listed below in Table 1 is the baseline data that reflects the reduction of carbon equivalent since 2001.

Table 1: GHG Reduction under Historical Recycling

| YEAR | GHG REDUCTION |
| --- | --- |
| 2001 | 2.1 MMTCE |
| 2002 | 1.7 MMTCE |
| 2003 | 2.1 MMTCE |
| 2004 | 1.9 MMTCE |
| 2005 | 2.5 MMTCE |

Historically, data reported to PA DEP demonstrates an annual modest increase in the tonnage of materials recycled.  In 1989, the first full year of Act 101 recycling reporting, approximately 378,000 tons of materials were recycled.  Since then the program has grown to nearly 4.9 million tons of materials recycled in 2005 (Table 2).  These annual increases provide a proven track record of quantifiable environmental and economic benefits.

Table 2 Historical Disposal and Recycling Data

| YEAR | POPULATION | DISPOSAL | PER CAPITA DISPOSAL PER DAY | RECYCLING |
| --- | --- | --- | --- | --- |
|  |  | IN TONS | IN TONS | IN TONS |
| 2000 | 12,281,054 | 9,324,468 | 0.76 | 3,791,433 |
| 2001 | 12,281,054 | 9,477,159 | 0.77 | 3,941,949 |
| 2002 | 12,281,054 | 9,613,250 | 0.78 | 3,927,048 |
| 2003 | 12,281,054 | 10,201,821 | 0.83 | 4,448,937 |
| 2004 | 12,281,054 | 10,373,136 | 0.84 | 4,747,332 |
| 2005 | 12,440,621 | 10,181,392 | 0.82 | 4,865,923 |

Include average annual growth rate and projected population.

Landfill capacity. PA currently has 16 years capacity. Under review for expansion would add another 7. (as communicated by Rick Illig, quoting Tom Siller?)

Larry Holley - may have data on State waste generation and import/export

Pennsylvania’s recycling data was analyzed in the NERC Environmental Benefits Calculator.  The raw 2005 data inputs used for the analysis are displayed in Attachment 1.   Attachment 2 shows GHG reductions estimated by the calculator for 2005.  Attachment 3 shows GHG reductions based on the recycling of recyclable materials that were identified as disposed in the Statewide Waste Characterization Study (April 2003).  Attachment 4 is the NERC Environmental Benefits Calculator in spreadsheet form including five worksheets reflecting 2005 Pa. recycling data.

### Total Reduction: 10.3 MMTCO2e

18 MMTCO2e represents 86% of the state’s total recycling potential of 20 MMTCO2e.  This has been determined to be a feasible goal.  Baseline reductions have been subtracted to reveal the additional reductions gained by this measure (10.3 MMTCO2e).

Waste Management Scenario Projections

NOTE: THE SECTION BELOW DESCRIBES THE WASTE MANAGEMENT FORECAST BASED ON SCENARIO 3A (SEE ATTACHMENT 5), WHICH WAS SELECTED AT THE LAST SUBCOMMITTEE MEETING.

Waste disposal data are available on the PA DEP website that display the amount of waste deposited at PA landfills and waste-to-energy / resource recovery facilities (hereafter referred to as WTE). This data also provides information on the origin of waste disposed, allowing for the identification of imported waste deposited at landfill and WTE facilities. CCS utilized this disposal data for 2000 through 2005, in conjunction with the recycling total from Table 2, to develop the waste management business-as-usual (BAU) projection. The amount of MSW exported from PA (600,000 tons) is provided by an article in Biocycle magazine.

Table 3 displays the waste management baseline that serves as the basis for the waste management scenario projections. The “MSW In-State Generation” total includes all in-state MSW deposited in PA landfills and WTE facilities that originated in PA, MSW exported from PA, and MSW recycled. The “In-State MSW Disposed in Landfills” is the sum of the “In-State MSW Disposed in PA Landfills” and “Reported MSW Exported.” The baseline diversion rate was calculated by dividing the tonnage of MSW recycled by the in-state MSW generation. In order to maintain consistency with other Work Plans in Pennsylvania, the Industry and Waste Subcommittee utilizes 2000 as the baseline year for waste management in Pennsylvania.  According to available disposal and recycling data, the recycling rate in 2000 was 28.2%.  This baseline recycling rate was applied to actual disposal data for the year 2006 to provide a starting point for the waste management BAU projection.

Table 3: Pennsylvania Baseline Waste Management

| Item | 2006 |
| --- | --- |
| MSW In-State Generation (tons) | 15,199,459 |
| Total MSW Disposed in PA Landfills (tons) | 14,805,019 |
| Imported MSW Disposed in PA Landfills (tons) | 6,773,180 |
| In-state MSW Disposed in PA Landfills (tons) | 8,031,839 |
| Reported MSW Exported (tons, assumed landfilled) | 601,706 |
| In-State MSW Disposed in Landfills (tons) | 8,633,545 |
| Total MSW Combusted in PA WTE Facilities (tons) | 2,752,084 |
| Imported MSW Disposed in PA WTE Facilities (tons) | 479,643 |
| In-state MSW Combusted PA WTE Facilities (tons) | 2,272,442 |
| Total In-State MSW Disposal (LF + WTE, tons) | 10,905,987 |
| MSW Diverted (tons) | 4,293,472 |

The waste management baseline scenario for  2006 was utilized to project the business-as-usual and policy (implementation goal of 52.7% recycling rate) scenarios through 2025. The growth in waste generation (disposal + diversion) was assumed to follow the average annual growth in per-capita generation from the  2000 – 2008 data described above ( 0.52%).  The business-as-usual (BAU) waste management projection was generated by increasing the “In-State MSW Generation” annually by multiplying the projected population by the average annual per capita generation growth rate of 0.52% and assuming a constant recycling rate of 28.2% of in-state generation. Additional recycling in each year is assumed to reduce in-state waste landfilled, so waste disposed at WTE facilities increases constantly at 0.52%. The results of the BAU projection are displayed in Table 4.

Table 4: BAU Pennsylvania Waste Management, 2005 – 2025

| Item | 2005 | 2010 | 2012 | 2015 | 2020 | 2025 |
| --- | --- | --- | --- | --- | --- | --- |
| MSW In-State Generation (tons) | 15,630,089 | 14,450,125 | 14,655,662 | 14,969,013 | 15,444,567 | 15,858,076 |
| Total MSW Disposed in PA Landfills (tons) | 15,385,112 | 12,568,151 | 12,934,198 | 13,503,354 | 14,508,146 | 15,587,705 |
| Imported MSW Disposed in PA Landfills (tons) | 7,515,388 | 5,024,535 | 5,280,806 | 5,682,571 | 6,435,047 | 7,297,708 |
| In-state MSW Disposed in PA Landfills (tons) | 7,869,725 | 7,543,616 | 7,653,392 | 7,820,783 | 8,073,100 | 8,289,998 |
| Reported MSW Exported (tons, assumed landfilled) | 600,000 | 609,782 | 615,980 | 625,395 | 641,407 | 657,829 |
| In-State MSW Disposed in Landfills (tons) | 8,469,725 | 8,153,398 | 8,269,372 | 8,446,178 | 8,714,507 | 8,947,827 |
| Total MSW Combusted in PA WTE Facilities (tons) | 2,728,123 | 2,841,537 | 2,870,418 | 2,914,291 | 2,988,907 | 3,065,433 |
| Imported MSW Disposed in PA WTE Facilities (tons) | 433,681 | 626,615 | 623,991 | 619,832 | 621,555 | 634,699 |
| In-state MSW Combusted PA WTE Facilities (tons) | 2,294,442 | 2,214,923 | 2,246,428 | 2,294,458 | 2,367,351 | 2,430,734 |
| Total In-State MSW Disposal (LF + WTE, tons) | 10,764,166 | 10,368,321 | 10,515,799 | 10,740,636 | 11,081,858 | 11,378,561 |
| MSW Diverted (tons) | 4,865,923 | 4,081,804 | 4,139,863 | 4,228,377 | 4,362,709 | 4,479,515 |

Table 5 displays the implementation of the Work Plan goal through 2025, including the incremental change in the recycling rate throughout the project period. The “Target Recycling Rate” from Table 5 was multiplied by the “MSW In-State Generation” from each year in Table 4 to yield the total tons recycled under the policy scenario, shown in Table 6. It was assumed that all incremental recycling will offset “In-state MSW Disposed in PA Landfills.”

Table 5: Implementation of Targets, 2010 – 2025.

| Goal Implementation | 2010 | 2012 | 2015 | 2020 | 2025 |
| --- | --- | --- | --- | --- | --- |
| Percent Implementation | 7% | 20% | 50% | 80% | 100% |
| Target Recycling Rate | 29.9% | 33.1% | 40.5% | 47.8% | 52.7% |
| Incremental Increase in Recycling Rate | 1.6% | 4.9% | 12.2% | 19.6% | 24.5% |

Table 6: Policy Pennsylvania Waste Management, 2005 – 2025

| Item | 2005 | 2010 | 2012 | 2015 | 2020 | 2025 |
| --- | --- | --- | --- | --- | --- | --- |
| MSW In-State Generation (tons) | 15,630,089 | 14,450,125 | 14,655,662 | 14,969,013 | 15,444,567 | 15,858,076 |
| In-State MSW Disposed in Landfills (tons) | 8,469,725 | 7,917,838 | 7,552,637 | 6,616,032 | 5,693,245 | 5,070,136 |
| In-state MSW Combusted PA WTE Facilities (tons) | 2,294,442 | 2,214,923 | 2,246,428 | 2,294,458 | 2,367,351 | 2,430,734 |
| MSW Diverted (tons) | 4,865,923 | 4,317,365 | 4,856,597 | 6,058,524 | 7,383,971 | 8,357,206 |
| Incremental MSW Diverted (tons) | - | 235,561 | 716,734 | 1,830,146 | 3,021,262 | 3,877,691 |

GHG Benefit Methodology and Results

CCS utilized the Northeast Recycling Council (NERC) Environmental Benefits Calculator (EBC) to estimate the net GHG benefit of incremental MSW diversion, described by Table 6. This model presents both a life-cycle GHG benefit and a direct landfill GHG benefit for diversion, as opposed to disposal of waste in landfills. The EBC is informed by the EPA Waste Reduction Model (WARM), but only requires the user to input material-specific tonnage of MSWte diverted, whereas WARM requires composition detail for landfill disposal and combustion of each waste material, in addition to the composition of diverted MSW.

CCS utilized the recycling composition provided in Attachments 1 and 3 by PA DEP. The material categories for Attachment 1 were re-grouped, as necessary, in order to place all diverted waste into one of the categories accepted by the EBC. The composition based on Attachment 1 is considered to be the BAU diversion composition (Table 7). Table 7 also displays the “Policy” diversion composition. This column was derived by adding the additional diversion for each material from Attachment 3 to the BAU diversion composition derived from Attachment 1.

Table 7: Material-specific MSW Diversion Composition – BAU and “Policy”

| Material Type | BAU Recycling Composition (% of Diversion) | Policy Recycling Composition (% of Diversion) |
| --- | --- | --- |
| Aluminum Cans | 0.4% | 0.8% |
| Steel Cans | 0.4% | 1.4% |
| Glass | 1.5% | 0.0% |
| HDPE | 0.2% | 0.9% |
| LDPE | 0.0% | 0.0% |
| PET | 0.2% | 1.1% |
| Corrugated Cardboard | 18.2% | 18.9% |
| Magazines/Third-class Mail | 0.6% | 3.3% |
| Newspaper | 6.2% | 7.9% |
| Office Paper | 1.9% | 5.1% |
| Phonebooks | 0.0% | 0.0% |
| Textbooks | 0.0% | 0.0% |
| Whole Computers | 0.1% | 0.0% |
| Food Scraps | 1.7% | 0.9% |
| Yard Trimmings | 14.9% | 7.9% |
| Grass | 0.0% | 0.0% |
| Leaves | 0.0% | 0.0% |
| Branches | 0.0% | 0.0% |
| Ferrous Scrap Metal | 14.8% | 11.1% |
| Aluminum Scrap Metal | 0.0% | 0.5% |
| Copper Wire | 0.0% | 0.0% |
| Tires | 0.0% | 0.0% |
| Construction & Demolition | 0.0% | 0.0% |
| Carpet | 0.0% | 0.0% |
| Dimensional Lumber | 5.4% | 2.9% |
| Medium-density Fiberboard | 0.0% | 0.0% |
| Clay Bricks | 0.0% | 0.0% |
| Aggregate | 0.0% | 0.0% |
| Fly Ash | 0.0% | 0.0% |
| Mixed Paper, Broad Definition | 6.1% | 8.3% |
| Mixed Metals | 12.6% | 7.0% |
| Mixed Plastics | 1.3% | 11.4% |
| Mixed Recyclables | 13.5% | 10.7% |
| Mixed Organics | 0.0% | 0.0% |
| Other Recyclables | 0.0% | 0.0% |

The BAU and Policy recovered materials composition from Table 7 for each material type was multiplied by the BAU and Policy waste diversion from Tables 4 and 6, respectively. This calculation yielded the inputs for the NERC EBC. CCS ran the EBC for the years 2015, 2020, and 2025, inputting the material-specific waste diversion, as well as the total in-state waste landfill disposal and WTE combustion for that year. The EBC was used twice for each year – once for the BAU diversion and once for the Policy diversion. The difference between the two results yielded the net GHG benefit.

As previously stated, the EBC provides the net landfill GHG benefit, as well as the total life-cycle GHG benefit. The landfill benefit takes into account the reduction in carbon sequestered in landfills, as well as the reduction in energy-producing LFG due to reduced waste disposal. Therefore, it is possible that the incremental GHG benefit at landfills from increased waste diversion will be very small, or possible negative.

Table 8 displays a summary of the incremental waste diversion, life-cycle GHG benefit and direct landfill GHG benefit.  In total, this Work Plan would result in an additional 36 million tons diverted through 2025, with a cumulative life-cycle and direct landfill GHG benefit of 103.5 and 0.14 MMtCO2e, respectively.

Table 8: Incremental MSW Diversion GHG Benefit

| Year | Incremental Diversion (tons) | Life-cycle GHG Benefit (MMtCO2e) | Direct Landfill GHG Benefit (MMtCO2e) |
| --- | --- | --- | --- |
| 2009 | - | - | - |
| 2010 | 235,561 | 0.73 | 0.03 |
| 2011 | 474,461 | 1.46 | 0.06 |
| 2012 | 716,734 | 2.21 | 0.09 |
| 2013 | 1,082,714 | 3.33 | 0.13 |
| 2014 | 1,453,835 | 4.48 | 0.17 |
| 2015 | 1,830,146 | 5.63 | 0.22 |
| 2016 | 2,062,631 | 5.92 | 0.01 |
| 2017 | 2,297,960 | 6.60 | 0.01 |
| 2018 | 2,536,157 | 7.28 | 0.01 |
| 2019 | 2,777,249 | 7.97 | 0.01 |
| 2020 | 3,021,262 | 8.67 | 0.01 |
| 2021 | 3,189,134 | 8.88 | -0.03 |
| 2022 | 3,358,699 | 9.36 | -0.08 |
| 2023 | 3,529,971 | 9.83 | -0.12 |
| 2024 | 3,702,964 | 10.3 | -0.16 |
| 2025 | 3,877,691 | 10.8 | -0.20 |
| Total | 36,147,170 | 103.5 | 0.14 |

Data Sources/Assumptions/Methods for Costs:

The overall cost to the Commonwealth needed to increase recycling to achieve the increased greenhouse gas reductions could be funded partially through the Recycling Fund, provided it is reauthorized by the General Assembly. The Commonwealth should realize an overall economic benefit from avoided waste disposal cost, increased numbers of jobs from an increased recycling industry, taxes from new business and some increased revenues from the sales of the new materials being recycled.

Industry may need to make some capital investments to facilitate increased collection.  The capital expenditures should be recouped in a reasonable amount of time based on the avoided disposal costs.  The avoided disposal costs in concert with the greenhouse gas reductions make any increased recycling expenditures a solid investment.

Implementation Steps:  Pa. DEP has a three-pronged strategy to facilitate increased recycling in the Commonwealth.  The separation into distinct areas will allow the Department to better monitor government progress with internal mechanisms.  To ensure that industry and the general public have meaningful input into the new recycling mandates the Department will utilize the regulatory process.

- The first prong is focused on ensuring that we as state government are taking a leadership role and maximizing our recycling efforts.  These efforts will be initiated with a new comprehensive management directive that will ensure all Commonwealth Agencies, Boards and Commissions are implementing recycling and waste reduction programs, as well as purchasing environmentally preferable products.

- Secondly, the Department depends on county governments to report recycling activities within their jurisdiction, as required by Act 101.  To facilitate more timely and improved reporting the Department will implement or procure a new or modified reporting system to capture much of the recycling data that currently goes unreported.

- The third prong is focused on industry and waste companies.  The Department will be making significant changes to the municipal and residual waste regulations that will prevent the disposal of certain materials and require new collection programs for a host of materials.  This regulatory reform will take 18-36 months until a final rulemaking is in place.   During that time the Department will continue its work in building increased capacity to recycle those materials banned from disposal.  The Department will use existing Recycling Fund monies to support the development of infrastructure.

In addition to the three steps identified above, some consideration could be given to the elimination of the Sunset date (December 31, 2011) for the recycling fees.  This would increase available funds for this and other related initiatives.

Table 9 depicts targeted achievements for additional Greenhouse Gas Reductions by increased recycling through 2025:

Table 9: GHG Reduction Targets

| YEAR | ACTION | % OF GOAL* | % RECOVERY OF DISCARDED RECYCLABLES | GHG REDUCTION | GHG REDUCTION |
| --- | --- | --- | --- | --- | --- |
| 2000 | Historical |  |  | 2.1 MMTCE | 7.7 MMTCO2 |
| 2012 | Legislation and Regulations in Place | 20% | 17% | 3.0 MMTCE | 11 MMTCO2 |
| 2015 | Increased Non-regulatory Enhancements | 50% | 43% | 3.8 MMTCE | 14 MMTCO2 |
| 2020 | Program Maintained and Improvement | 80% | 69% | 4.5 MMTCE | 17 MMTCO2 |
| 2025 | Completion | 100% | 86% | 5.0 MMTCE | 18 MMTCO2** |

* Assumes achievement of additional reductions of 2.5 MMTCE or 9.2 MMTCO2, 86% of the potential reduction of 2.9 MMTCE or 11 MMTCO2.

**18 MMTCO2e represents 86% of the state’s total recycling potential of 20 MMTCO2e.  Baseline reductions have been subtracted to reveal additional reductions gained by this measure.

Potential Overlap:

- Increased Capture and Use of Landfill Methane

- Solid Waste Initiative

Other Considerations/Notes:

Attachment 1:

| Pa. Materials Recycled, 2005 |  |  |  |
| --- | --- | --- | --- |
| MATERIAL | DEP Code(s) | Breakout | TONS |
| FOOD WASTE | FW1 |  | 66,481.70 |
| GLASS |  |  |  |
| GLASS: CLEAR | GL1 | 15,577.80 |  |
| GLASS: MIXED | GL2 | 21,866.30 |  |
| GLASS: GREEN | GL3 | 6,311.40 |  |
| GLASS: BROWN | GL4 | 6,681.50 |  |
| GLASS: PLATE | GL5 | 5,153.20 |  |
| GLASS: OTHER | GL6 | 1,929.30 |  |
| Subtotal Glass |  |  | 57,519.50 |
| BATTERY: LEAD-ACID | B01 |  | 22,169.90 |
| METALS |  |  |  |
| ALUMINUM CANS | AA1 | 17,590.00 |  |
| FERROUS | F01 | 580,142.10 |  |
| STEEL & BIMETALLIC (TIN) CANS | F02 | 13,935.90 |  |
| WHITE GOODS | F03 | 56,383.30 |  |
| MIXED METALS | MM1 | 174,797.40 |  |
| MIXED CANS | MX2 | 2,547.00 |  |
| NON FERROUS | N01 | 48,413.40 |  |
| COPPER | N02 | 4,524.60 |  |
| BRASS | N03 | 2,349.60 |  |
| LEAD | N04 | 167.5 |  |
| STAINLESS STEEL | N05 | 203,794.40 |  |
| NICKEL | N10 | 48.7 |  |
| WIRE/CABLE | W01 | 1,455.30 |  |
| Subtotal Metals |  |  | 1,106,149.20 |
| PAPER |  |  |  |
| PAPER: CARDBOARD | C01 | 713,552.00 |  |
| PAPER: BROWN BAGS & SACKS | C02 | 3,749.60 |  |
| PAPER: MAGAZINE | PA1 | 24,682.80 |  |
| PAPER: NEWSPRINT | PA2 | 244,252.40 |  |
| PAPER: MIX | PA3 | 230,483.50 |  |
| PAPER: OFFICE PAPER | PA4 | 76,303.80 |  |
| PAPER: COMPUTER | PA5 | 3,807.70 |  |
| PAPER: PHONE BOOKS | PA6 | 1,242.50 |  |
| Subtotal Papers |  |  | 1,298,074.30 |
| PLASTICS |  |  |  |
| DRUM PLASTIC | DR1 | 791.2 |  |
| PLASTIC: PET | PL1 | 6,754.60 |  |
| PLASTIC: HDPE | PL2 | 6,955.40 |  |
| PLASTIC: PVC (POLYVINYL/CHLORIDE) | PL3 | 15,206.50 |  |
| PLASTIC: LPDE (LOW DENSITY POLYETHYLENE) | PL4 | 2,598.90 |  |
| PLASTIC: PP (POLYPROPLENE) | PL5 | 3,236.20 |  |
| PLASTIC: PS (POLYSTYRENE) | PL6 | 1850.2 |  |
| PLASTIC: MIXED | PL7 | 16,225.60 |  |
| PLASTIC: FILM | PL8 | 5,747.40 |  |
| PLASTIC: OTHER | PL9 | 4,594.90 |  |
| Subtotal Plastics |  |  | 63,960.90 |
| SINGLE STREAM | SS1 |  | 43,645.80 |
| TEXTILES | M03 |  | 25,182.70 |
| TIRES | M01 |  | 55,416.50 |
| WOOD | WW1 |  | 213,284.90 |
| YARD TRIMMAGE | Y03 |  | 585,681.50 |
| OTHER RECYCLABLES |  |  |  |
| CIRCUIT BOARDS | CB1 | 61.6 |  |
| CONSUMER ELECTRONICS | CRT | 2,900.00 |  |
| FLUORESCENT TUBES | FL1 | 261 |  |
| HOUSEHOLD HAZARDOUS WASTE | HHW | 1,353.90 |  |
| MATTRESSES | MT1 | 116.6 |  |
| ANTIFREEZE | O02 | 1,342.20 |  |
| OIL FILTERS | OL3 | 798.9 |  |
| COMMINGLED MATERIALS | XXX | 228,699.80 |  |
| Subtotal Other Recyclables |  |  | 235,534.00 |
| 904 excess |  |  | 25,929.00 |
| Tire excess |  |  | 72,770.00 |
| ISRI excess |  |  | 51,795.00 |
| Lancaster County (RE-Trac) | INCORPORATED |  |  |
| TOTAL STANDARD |  |  | 3,923,594.90 |
| TOTAL NON-STANDARD |  |  | 942,328.10 |
| GRAND TOTAL |  |  | 4,865,923.00 |

Attachment 2:

| Reductions in Greenhouse Gas Emissions as a Result of 2005 Recycling Tons Recycled Greenhouse Gas Emissions Associated with Recycling (MTCE) Greenhouse Gas Emissions if Recyclables Had Been Disposed (MTCE) Net Greenhouse Gas Emissions from Recycling as Compared to Disposal (MTCE) Reporting Year 2005 Aluminum Cans 33,619 -124,418 381 -124,799 Steel Cans 44,590 -21,817 -2,494 -19,323 Glass 201,097 -15,239 2,194 -17,433 HDPE 40,115 -15,230 1,923 -17,152 LDPE 2,599 -1,201 125 -1,326 PET 39,736 -16,667 2,161 -18,828 Corrugated Cardboard 714,526 -606,295 46,378 -652,673 Magazines/Third-class Mail 25,935 -21,718 -2,313 -19,405 Newspaper 276,048 -210,163 -63,883 -146,280 Office Paper 76,652 -59,629 32,309 -91,939 Phonebooks 1,721 -1,246 -398 -848 Textbooks 0 0 0 0 Whole Computers 0 0 0 0 Food Scraps 66,482 -3,600 10,599 -14,199 Yard Trimmings 585,682 -31,717 -35,002 3,286 Grass 0 0 0 0 Leaves 0 0 0 0 Branches 213,285 -11,550 -25,957 14,407 Ferrous Scrap Metal 650,458 -318,251 -36,376 -281,875 Aluminum Scrap Metal 31,681 -117,246 359 -117,605 Copper Wire 0 0 0 0 Tires 128,187 -63,783 2,101 -65,884 Construction & Demolition 688,211 NA NA NA Carpet 0 0 0 0 Dimensional Lumber 0 0 0 0 Medium-density Fiberboard 0 0 0 0 Clay Bricks 0 NA NA NA Aggregate 0 0 0 0 Fly Ash 0 0 0 0 Mixed Paper, Broad Definition 244,234 -235,593 12,891 -248,484 Mixed Metals 490,360 -703,102 -17,722 -685,380 Mixed Plastics 47,652 -19,418 2,407 -21,825 Mixed Recyclables 0 0 0 0 Mixed Organics 0 0 0 0 Other Recyclables 263,279 NA NA NA Total as a Result of Recycling 4,866,149 -2,597,884 -70,318 -2,527,566 |  |  |  |
| --- | --- | --- | --- |

Attachment 3:

# Potential GHG Reductions if recyclable materials disposed were recycled

|  | Potential Tons Recyclable | Greenhouse Gas Emissions Associated with Recycling (MTCE) |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Reporting Year | (MSW Composition Study, April 2003) |  |  |  |  |
| Aluminum Cans | 48,844 | -180,763 |  |  |  |
| Steel Cans | 102,532 | -50,166 |  |  |  |
| Glass | 234,629 | -17,780 |  |  |  |
| HDPE | 68,082 | -25,848 |  |  |  |
| LDPE | 0 | 0 |  |  |  |
| PET | 87,601 | -36,743 |  |  |  |
| Corrugated Cardboard | 785,032 | -666,121 |  |  |  |
| Magazines/Third-class Mail | 251,027 | -210,208 |  |  |  |
| Newspaper | 389,263 | -296,357 |  |  |  |
| Office Paper | 341,975 | -266,029 |  |  |  |
| Phonebooks | 0 | 0 |  |  |  |
| Textbooks | 0 | 0 |  |  |  |
| Whole Computers | 0 | 0 |  |  |  |
| Food Scraps | 0 | 0 |  |  |  |
| Yard Trimmings | 0 | 0 |  |  |  |
| Grass | 0 | 0 |  |  |  |
| Leaves | 0 | 0 |  |  |  |
| Branches | 0 | 0 |  |  |  |
| Ferrous Scrap Metal | 282,131 | -138,039 |  |  |  |
| Aluminum Scrap Metal | 43,057 | -159,347 |  |  |  |
| Copper Wire | 0 | 0 |  |  |  |
| Tires | 0 | 0 |  |  |  |
| Construction & Demolition | 0 | NA |  |  |  |
| Carpet | 0 | 0 |  |  |  |
| Dimensional Lumber | 0 | 0 |  |  |  |
| Medium-density Fiberboard | 0 | 0 |  |  |  |
| Clay Bricks | 0 | NA |  |  |  |
| Aggregate | 0 | 0 |  |  |  |
| Fly Ash | 0 | 0 |  |  |  |
| Mixed Paper, Broad Definition | 433,821 | -418,473 |  |  |  |
| Mixed Metals | 32,138 | -46,081 |  |  |  |
| Mixed Plastics | 906,653 | -369,457 |  |  |  |
| Mixed Recyclables | 0 | 0 |  |  |  |
| Mixed Organics | 0 | 0 |  |  |  |
| Other Recyclables | 0 | NA |  |  |  |
| Total as a Result of Recycling | 4,006,785 | -2,881,412 |  |  |  |

Attachment 4:

NERC Environmental Benefits Calculator, 2005 Pa. Recycling Data

Attachment 5:

WASTE MANAGEMENT PROJECTION SCENARIOS

CCS was provided historical disposal data for 1990 through 2008 by PA DEP. These data show the amount of waste disposed at each facility in Pennsylvania, as well as the origin of that waste.  CCS used these data, in addition to the recycling data provided in Table 2. The methods used to develop these scenarios are similar to those used to develop the Waste Management Projection (highlighted above), except for the application of the average annual growth (AAG) in per-capita generation as the growth factor for waste generation.  Once the subcommittee has selected a preferred waste projection scenario, CCS will finalize the waste management projection and proceed with the GHG benefit and cost-effectiveness quantification.

Scenario 3a was selected by the Industry and Waste Subcommittee on a public teleconference, which took place on May 6, 2009.

Note for Scenario 1: the AAG in the diversion rate from 2000 through 2005 was used to simulate an increase in the business-as-usual diversion rate. Under this scenario, the BAU diversion rate in 2025 would be 46.6%.

| Scenario 1 - BAU Growth in Diversion Rate (AAG 2000-2005) |
| --- |
| Scenario 1a - 2000-2008 AAG in per-capita generation | Baseline Diversion Rate | 31.1% |  |  |  |
|  | AAG Diversion Rate (2000-2005) | 2.0% |  |  |  |
|  | AAG Per-Capita Generation (2000-2008) | 1.4% |  |  |  |
|  |  | 2005 | 2010 | 2015 | 2025 |
|  | Total MSW Generation (tons) | 15,630,089 | 15,784,007 | 17,128,905 | 19,914,458 |
|  | BAU In-State MSW Landfilled (tons) | 8,469,725 | 8,137,042 | 8,336,915 | 8,355,735 |
|  | BAU MSW Diverted (tons) | 4,865,923 | 5,436,486 | 6,527,214 | 9,288,834 |
|  | Incremental MSW Diversion (tons) | - | 192,112 | 1,249,859 | 1,206,085 |
| Scenario 1b - 2000-2005 AAG in per-capita generation | Baseline Diversion Rate | 31.1% |  |  |  |
|  | AAG Diversion Rate (2000-2005) | 2.0% |  |  |  |
|  | AAG Per-Capita Generation (2000-2005) | 3.1% |  |  |  |
|  |  | 2005 | 2010 | 2015 | 2025 |
|  | Total MSW Generation (tons) | 15,630,089 | 16,292,711 | 19,140,177 | 26,077,464 |
|  | BAU In-State MSW Landfilled (tons) | 8,469,725 | 8,399,291 | 9,315,834 | 10,941,617 |
|  | BAU MSW Diverted (tons) | 4,865,923 | 5,611,699 | 7,293,638 | 12,163,486 |
|  | Incremental MSW Diversion (tons) | - | 198,304 | 1,396,618 | 1,579,337 |
| Scenario 1c - 2003-2008 AAG in per-capita generation | Baseline Diversion Rate | 31.1% |  |  |  |
|  | AAG Diversion Rate (2000-2005) | 2.0% |  |  |  |
|  | AAG Per-Capita Generation (2000-2008) | 0.1% |  |  |  |
|  |  | 2005 | 2010 | 2015 | 2025 |
|  | Total MSW Generation (tons) | 15,630,089 | 15,369,086 | 15,604,049 | 15,879,252 |
|  | BAU In-State MSW Landfilled (tons) | 8,469,725 | 7,923,140 | 7,594,743 | 6,662,638 |
|  | BAU MSW Diverted (tons) | 4,865,923 | 5,293,575 | 5,946,146 | 7,406,666 |
|  | Incremental MSW Diversion (tons) | - | 187,062 | 1,138,594 | 961,700 |

| Scenario 2 - 2005 Baseline Recycling Rate |
| --- |
| Scenario 2a - 2000-2008 AAG in per-capita generation | Baseline Diversion Rate | 31.1% |  |  |  |
|  | AAG Per-Capita Generation (2000-2008) | 1.1% |  |  |  |
|  |  | 2005 | 2010 | 2015 | 2025 |
|  | Total MSW Generation (tons) | 15,630,089 | 15,218,941 | 16,197,327 | 18,112,373 |
|  | BAU In-State MSW Landfilled (tons) | 8,469,725 | 8,242,019 | 8,771,877 | 9,808,995 |
|  | BAU MSW Diverted (tons) | 4,865,923 | 4,737,925 | 5,042,514 | 5,638,702 |
|  | Incremental MSW Diversion (tons) | - | 218,830 | 1,746,739 | 3,906,519 |
| Scenario 2b - 2000-2005 AAG in per-capita generation | Baseline Diversion Rate | 31.1% |  |  |  |
|  | AAG Per-Capita Generation (2000-2008) | 3.1% |  |  |  |
|  |  | 2005 | 2010 | 2015 | 2025 |
|  | Total MSW Generation (tons) | 15,630,089 | 15,832,224 | 18,599,211 | 25,340,425 |
|  | BAU In-State MSW Landfilled (tons) | 8,469,725 | 8,574,150 | 10,072,648 | 13,723,442 |
|  | BAU MSW Diverted (tons) | 4,865,923 | 4,928,851 | 5,790,263 | 7,888,922 |
|  | Incremental MSW Diversion (tons) | - | 227,649 | 2,005,760 | 5,465,482 |
| Scenario 2c - 2003-2008 AAG in per-capita generation | Baseline Diversion Rate | 31.1% |  |  |  |
|  | AAG Per-Capita Generation (2000-2008) | -0.5% |  |  |  |
|  |  | 2005 | 2010 | 2015 | 2025 |
|  | Total MSW Generation (tons) | 15,630,089 | 14,765,643 | 14,570,723 | 14,007,246 |
|  | BAU In-State MSW Landfilled (tons) | 8,469,725 | 7,996,529 | 7,890,968 | 7,585,809 |
|  | BAU MSW Diverted (tons) | 4,865,923 | 4,596,806 | 4,536,124 | 4,360,703 |
|  | Incremental MSW Diversion (tons) | - | 212,313 | 1,571,324 | 3,021,115 |

| Scenario 3 - 2000 Baseline Recycling Rate |
| --- |
| Scenario 3a - 2000-2008 AAG in per-capita generation | Baseline Diversion Rate | 28.2% |  |  |  |
|  | AAG Per-Capita Generation (2000-2008) | 0.5% |  |  |  |
|  |  | 2005 | 2010 | 2015 | 2025 |
|  | Total MSW Generation (tons) | 15,630,089 | 14,450,125 | 14,969,013 | 15,858,076 |
|  | BAU In-State MSW Landfilled (tons) | 8,469,725 | 8,153,398 | 8,446,178 | 8,947,827 |
|  | BAU MSW Diverted (tons) | 4,865,923 | 4,081,804 | 4,228,377 | 4,479,515 |
|  | Incremental MSW Diversion (tons) | - | 235,561 | 1,830,146 | 3,877,691 |
| Scenario 3b - 2000-2005 AAG in per-capita generation | Baseline Diversion Rate | 28.2% |  |  |  |
|  | AAG Per-Capita Generation (2000-2008) | 3.1% |  |  |  |
|  |  | 2005 | 2010 | 2015 | 2025 |
|  | Total MSW Generation (tons) | 15,630,089 | 15,195,816 | 17,851,578 | 24,321,816 |
|  | BAU In-State MSW Landfilled (tons) | 8,469,725 | 8,574,150 | 10,072,648 | 13,723,442 |
|  | BAU MSW Diverted (tons) | 4,865,923 | 4,292,443 | 5,042,630 | 6,870,313 |
|  | Incremental MSW Diversion (tons) | - | 247,717 | 2,182,576 | 5,947,284 |
| Scenario 3c - 2003-2008 AAG in per-capita generation | Baseline Diversion Rate | 28.2% |  |  |  |
|  | AAG Per-Capita Generation (2000-2008) | -1.2% |  |  |  |
|  |  | 2005 | 2010 | 2015 | 2025 |
|  | Total MSW Generation (tons) | 15,630,089 | 13,949,375 | 13,230,742 | 11,750,525 |
|  | BAU In-State MSW Landfilled (tons) | 8,469,725 | 7,870,853 | 7,465,369 | 6,630,165 |
|  | BAU MSW Diverted (tons) | 4,865,923 | 3,940,354 | 3,737,358 | 3,319,233 |
|  | Incremental MSW Diversion (tons) | - | 227,398 | 1,617,621 | 2,873,293 |

Waste-3

Solid Waste Management Initiative

Work Plan for Potential GHG Reduction Measure

Lead Staff Contact: Mike Texter (717) 783-6006

Initiative Summary:  The Solid Waste Management Initiative is comprised of three (3) strategies:

- Reduced Transportation of Waste

These strategies aim to utilize the energy potential of residual and municipal waste and decrease the energy used to transport waste to landfills.  Reduction numbers result as conventional energy sources (fossil fuels) are displaced by energy derived from waste, and reductions of transportation energy.  Utilizing these waste materials for energy will also prevent a significant amount of material from being disposed of in landfills.

Goals:  Need goal for the third element - Reduced Transportation of Waste. See examples from FL that were shared with Subcommittee.

Waste-to-Energy element moved to Waste-6.

Alternative Fuels will be considered under the auspices of the Industry workplans

Implementation Period:  See table for implementation for the first two elements.

Parties Affected/Implementing Parties:  DEP

Data Sources/Assumptions/Methods for GHG:

Waste Transportation: In 2006, the transportation of waste from the Allentown/Bethlehem/Easton area, New Jersey, New York and Philadelphia to disposal facilities in Pennsylvania outside of these areas consumed 39.2 million gallons of fuel. Providing waste management options near the point of generation would save 0.42 MMTCOe.

Waste Transportation: Excessive waste disposal capacity and low tipping fees in western Pennsylvania encourage the long distance transportation of waste. The Waste Futures initiative will identify legislative, regulatory and other actions the Department can take to reduce excess waste disposal capacity. These actions will result in the reduction of 0.42 MMTCOe.

Data Sources/Assumptions/Methods for Costs:

The Waste Futures initiative will identify legislative, regulatory and other actions the Department can take to reduce excess waste disposal capacity.

Potential Overlap:

- Increased Landfill Methane Capture Work Plan

- Statewide Recycling Initiative

- Fuels for Schools Work Plan

- Recycling Work Plan

- AEPS Tier I (@8%, 15%, 20%) Work Plans

Other Considerations/Notes:

Waste-4

Improved Efficiency at Wastewater Treatment Facilities

Work Plan for Potential GHG Reduction Measure

Lead Staff Contact: Nicki Kasi (717) 772-4053

Initiative Summary:  Improving Efficiency at Wastewater Treatment Facilities through outreach programs based on Sustainable Infrastructure principals.

Goals:  Assist 50% more treatment plans per year to improve efficiency (50% improvement over the current 6-8 treatment plants)

Implementation Period:  3-4 additional  treatment plans per year from 2009 through 2020

Parties Affected/Implementing Parties:  DEP, Outreach Assistance Provider Program (OAPP), Wastewater system owners/operators

Implementation steps:

- DEP - increase personnel assigned to OAPP outreach by 50%

- Provide grant funding for wastewater plant upgrades

Improve ease of permitting for wastewater plant upgrades

Data sources/Assumptions/Methods for GHG:

Based on past program performance, treatment facilities visited by this program tend to treat around 1 to 2 million gallons of water per day.  Calculations on GHG savings are as follows:

- 6,000 KWH/Million gallons treated x 1.5 million gallon/day facility = 9,000 Kwh/day

- 9,000 KWH x 365 days = 3,285,000 kWH/yr

Savings at these facilities is estimated at 10%, so

- 3,285,000 kWH/yr x 0.10 = 328,500 kWH/yr savings per facility

Converting to CO2 emissions

- 328,500 kWH/yr x 7.18 x 10-4 metric tons CO2 / kWh= 236 mtCO2/yr per facility

Table 1 summarizes the GHG savings possible from implementing a 50% increase in treatment plant upgrades.  By upgrading an average of 3-4 additional facilities per year a total of 9.9 x 10-3 million metric tons of CO2e can be saved.

Table 1.  GHG savings and costs of treatment plant upgrades

| Year | Average Additional Treatment Plants Improved | Savings per Facility (metric tons CO2e/year) | Total Savings above BAU (metric tons CO2e/year) | Cost of Implemen-tation ($) | Cost Savings to Plants ($) | NPV Costs (2007$) | Cost Effec-tiveness ($/tCO2e) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2009 | 3.5 | 236 | 826 | 17,500 | (87,500) | (79,365) |  |
| 2010 | 3.5 | 236 | 826 | 17,500 | (175,000) | (151,172) |  |
| 2011 | 3.5 | 236 | 826 | 17,500 | (262,500) | (215,959) |  |
| 2012 | 3.5 | 236 | 826 | 17,500 | (350,000) | (274,234) |  |
| 2013 | 3.5 | 236 | 826 | 17,500 | (437,500) | (326,469) |  |
| 2014 | 3.5 | 236 | 826 | 17,500 | (525,000) | (373,108) |  |
| 2015 | 3.5 | 236 | 826 | 17,500 | (612,500) | (414,564) |  |
| 2016 | 3.5 | 236 | 826 | 17,500 | (700,000) | (451,226) |  |
| 2017 | 3.5 | 236 | 826 | 17,500 | (787,500) | (483,457) |  |
| 2018 | 3.5 | 236 | 826 | 17,500 | (875,000) | (511,594) |  |
| 2019 | 3.5 | 236 | 826 | 17,500 | (962,500) | (535,956) |  |
| 2020 | 3.5 | 236 | 826 | 17,500 | (1,050,000) | (556,837) |  |
|  |  | TOTAL | 9,912 |  |  | (4,373,942) | (441) |

Data Sources/Assumptions/Methods for Costs:

The cost of implementation of treatment plant upgrades is estimated at $5,000 per plant and upgrades result in an average cost savings of $25,000 per plant per year.  The total costs savings over the policy period is $4.4 million discounted to 2007 dollars, as summarized in Table 1.

Need cost of hiring additional DEP personnel.

Notes/Other Considerations:

The Office of Water Management proposes several methods to improve efficiency in order to maintain sustainable infrastructure (SI) within wastewater treatment systems.  The efficient use of energy is crucial for sustaining infrastructure and national security.  Electrical energy rate cap expirations set for 2010 further exacerbate this issue.

Wastewater treatment plants typically are the largest consumer of electricity on most municipal bills, often consuming more than 1/3 of the energy consumed for all municipal services.  In many instances, opportunities exist to reduce energy consumption at these facilities.  In order to assist treatment plants in improving efficiency, DEP provides outreach to these facilities, teaching system operators how to use the system in the most efficient manner for treatment and suggesting ways to reduce the amount of energy required to operate the facility.

There are three basic types of treatment plants in use today, activated sludge, fixed film and lagoon systems.  Of the many treatment facilities in Pennsylvania, approximately 70% are activated sludge facilities.  These facilities inject diffused air into an aeration basin to sustain a biological growth in order to treat the wastewater.  The aeration basins that these facilities require are the largest consumer of electricity in wastewater treatment systems.  Opportunities exist to improve efficiency in many of these facilities throughout the state.

The Outreach Assistance Provider Program (OAPP) uses part-time wage payroll instructors who are certified operators or specialists in a given field.  These instructors provide on-site technical, managerial, and financial assistance to wastewater system owners and operators.  The program responds to system needs identified by DEP regional staff, local government associations, or system personnel.  On-site assistance and training is provided through a combination of videos, classroom and web-based training, and one-on-one assistance to address specific system problems.  In the coming fiscal year,  OAPP  plans on accomplishing the following:

- Continuing on-site technical assistance for facilities requesting assistance with energy efficiency.   The average activated sludge wastewater treatment plant consumes 6,000 KWH per million gallons of wastewater treated.  At approximately $0.08 per KWH, the energy consumption is estimated at $500 per million gallons treated.  Using energy audits under the auspices of the OAPP, DEP proposes to assist 6 to 8 wastewater systems in reducing energy consumption in FY 2008-2009, with a focus on doing at least one per DEP region.  On average, these audits will result in an estimated annual energy savings of 10 to 15% in the cost of KWH per treatment plant.   It must be kept in mind that due to the relatively low cost of electricity in the past, the preference for wastewater treatment has been aerobic treatment processes.  This will no longer be the most cost-effective solution once the expected sharp increases in costs per KWHs take place.  Therefore, a further focus of this outreach effort will be to encourage and re-educate the owners and operators of wastewater treatment systems on the benefits of more energy efficient and effective wastewater treatment processes related to anaerobic treatment.

- Continuing collaboration with Central and Regional staff in providing training opportunities for operators in conjunction with various associations.

- Integrating the principles of SI in all technical assistance provided by the Outreach Assistance Provider Program.  This would include providing training in regard to all aspects of SI.

- Distributing the DVD on energy efficiency and other tools for SI.

- In conjunction with the Pennsylvania Water Environment Association, another special Nutrient Reduction Technology conference is scheduled for this fall in the Scranton area on September 10 - 12, 2008. This year’s conference will include energy efficiency, improvements to water quality and other principals of SI.

- Enhancements to the operator information center website "Technical Corner" as it relates to SI, energy efficiency and other operational issues.

The DEP Wastewater Outreach Program has provided assistance in energy efficiency since 1993.  Unfortunately, in the 1990's energy costs were not high enough to cause a significant amount of interest.  While we had several success stories in the past, many people simply were not tuned into the idea of energy efficiency.  In one case, we saved a municipality over $100,000 annually (approximately 6.0 MGD system).  By today's standards this type of savings would be greatly magnified.  With the pending expiration of electrical energy rate caps and the spiraling cost of oil, people are now starting to pay attention and ask questions.

Below are examples of our past accomplishments:

- On site technical assistance to Ridgeway Borough on energy efficiency and process control.  This project utilized the process of denitrification to save energy and chemical costs.  This process utilizes the nitrate that is produced in the process of nitrification for facultative organism respiration.   This results in improved water quality by reducing total nitrogen released to the receiving stream and saves money.  With an investment of $500, Ridgeway was able to document savings of $31,000 annually in energy and chemical costs in addition to improving the quality of their effluent.

- On site technical assistance to the City of Warren in regard to energy efficiency.  In this system older sparge ring diffusers were used for mixing and aeration.   By changing the cycles of mixing and aeration, the system could realize a savings of several thousand dollars per month.  This project is still underway.

- DEP Central and Regional office staff collaborated to produce a continuing education training program titled "Flush Away High Energy Costs".  In conjunction with PA Rural Water, this training session was piloted in the NW region and was well received by operators all over the region.  This session provides the operators with the tools they need to reduce energy costs within their system while maintaining or improving water quality.

- In 1996, a video was produced jointly between DEP, and the Maryland Center for Environmental Training in regard to energy efficiency in wastewater treatment systems.  In the past year, this video was upgraded and digitized to a DVD format so it can be widely distributed.

- A training session was held for DEP Central and Regional Office staff on energy efficiency in water/wastewater systems. This session was held in the State College area and followed a format similar to the operator training session known as "Flush Away High Energy Costs". This session will help regional staff to further spread the word in regard to energy efficiency.

- A special conference on Total Nutrient Reduction was held in the Lancaster area last fall.  This sold out event provided operators and managers with tools needed to improve reduction of nutrients and increase efficiency.

- Assistance was provided to program staff involved in a pilot project with Montgomery County Community College to create a certificate program focusing on water and wastewater treatment.   Based on the input provided, the pilot program will be modified to include basics of SI with an emphasis on energy efficiency, as well as effective process control.

All treatments plants produce excess solids, often referred to as sludge or biosolids.  These excess solids have to be treated before ultimate disposal. There are two basic types of treatment for these solids, aerobic digestion and anaerobic digestion.  Anaerobic treatment tends to be more energy neutral or even produce energy as the methane produced through this process can be used as a fuel.  Unfortunately, this technology is not used in many instances in Pennsylvania due to past problems with the operation, mostly due to problems in handling the gases produced in the treatment process.  Technology in this arena has improved in recent years, making the management of these systems safer and more efficient.  PA DEP currently has a pilot project in the works that will use anaerobic treatment and, depending on the outcome of this project, expects that other facilities may consider this option moving forward.

In the past fiscal year, we had several projects in this arena.  These projects are closely tied into the overall goal of SI.  In many cases, treatment systems have operated in a fashion set forth by previous generations where energy consumption was not a large concern.  Taking a moment and asking why we operate in this fashion can lead to significant opportunities for reduced energy costs and improved water quality.   By today's standard, any treatment facility that is required to nitrify should also consider denitrification, as it can lead to reduced operating costs, lower sludge production and improved water quality.

- Cost to DEP

  - Energy efficiency is an integral part of the OAPP, where the cost for implementing this strategy will be minimal.  Interest in this program is expected to increase as people start to realize two factors, the first being that energy prices are rising sharply and second factor is that rate caps expire in 2010.  DEP is starting to receive more requests.

- Cost to Commonwealth

  - The cost here would be to do nothing.  Rising energy prices will force utilities to raise prices.  The most efficient first step is to use energy wisely.

- The savings realized by energy efficient measures could easily be used to fund improved water quality.  In fact, in cases where a facility starts using denitrification for the beneficial uptake of NO3, there would be a recovery of 60% of the cost of nitrification and improved water quality at the same time.  Cost savings are certain, and the savings could escalate as energy costs continue to rise.  It is a goal for systems to be self-sustaining in the water/wastewater industry.  The single largest cost for a wastewater system is the cost of aeration.  Fine bubble aeration could reduce those costs by 50%. This money could be incorporated into sustainable infrastructure.

Potential Overlap:

- Most Electricity Sector Initiatives

- Waste-to-Energy Digesters (for use of biosolids)

Waste-5

Waste-to-Energy Digesters

Work Plan for Potential GHG Reduction Measure

Strategy Name: Waste-to-Energy Digesters

Lead Staff Contact: Kim Hoover (717-772-5161)

Summary:  This initiative encourages an expansion of the basic on-farm or sewage treatment plant digester that can offer larger scale and higher technology treatment.

Goals:   Install three 1-4MW  digesters by 2020,

Implementation Period:  Need to know when goals would be reached

(for example: reach 50% of goal by 2015 and 100% of goal by 2025)

Parties Affected/Implementing Parties:  DEP, communities and local governments, businesses, food companies

Data sources/Assumptions/Methods for GHG:

Need data on digesters - how much they can digest, the amount of biogas produced

From Joe  Sherrick:

Focusing on thermophilic anaerobic digestion rather than the common mesophilic technologies that predominate on U.S. farms and wastewater treatment plants.  Technologies common in Europe provide for mixed feedstocks, yield more gas and are more efficient.  The effluent (digestate) is closely monitored and allows for precision agriculture as the participating farmers receive a guaranteed NPK analysis for fertilizer application.  Depending on the exact technology/vendor selected for these digesters, about 50% of the input is manure and the remainder is some combination of food residues, crop residues, yard wastes, organic fraction of MSW or sewage sludge.

Food prep facilities are disposing of food waste with land application - if food waste is combined with manure it makes it a better fertilizer

Need data on how much is out there - food streams and manure

Need amount of food waste disposed in state - Penn State operates food waste - Mike Mclaughlin will try and get contact

1-4MW  digesters - 3 by 2020, pipeline quality gas.

Alternative energy portfolio standard - meeting those requirements

complete-mix two-stage digesters

treatment for effluent -

need info on food residuals being disposed of

need info on yard waste

which farms don't have digesters - manure would have to be hauled to digester

there has been one feasibility study for York County

licensed vendor in PA - sells the Danish digesters - Niras is danish technology. the vendor is Waste-to energy Solutions John Kunkel - 724-354-3897, Bill Klein

digesters have "recipes" for the best combination of feedstocks

They can store the gas - generate during peak hours

Joe- send food  residuals reports from solid waste

send York County feasibility study

In the regional model,

- New feedstocks for digesters include food waste and yard waste as well as conventional manure and sludge.

- Waste-to-energy digesters produce electrical power along with high grade solid and liquid end-products.

- The business community can participate as both users and investors.

- Food companies would have an outlet for food waste.

- Concept expands upon local on-farm digesters that produce power for farm use and treated solid and liquid fertilizers.

Data Sources/Assumptions/Methods for Costs:  Need costs of implementation and costs of energy replaced

Implementation Steps:

Potential Overlap:

Notes/Other Considerations:

Waste-6

Waste-to-Energy MSW

Work Plan for Potential GHG Reduction Measure

Strategy Name: Waste-to-Energy Municipal Solid Waste

Lead Staff Contact: Kim Hoover (717-772-5161)

Summary:  This initiative encourages more waste-to-energy projects and waste volume in the energy mix.

Goals:  40 % increase in Waste-to-Energy derived from MSW by 2030

From Dave Vallero, York County Solid Waste Authority:

- Currently PA burns 8,730 tons/day waste in 6 waste-to-energy facilities

- 30-40% additional capacity over the next 20 years is feasible

- With the right incentives there could be more growth

- Some thoughts on incentives-

  - Make it easier to flow waste to privately-owned facilities

  - Include waste-to-energy in state  renewable energy standards

  - Make waste-to-energy  Tier I

Implementation Period:  20% increase by 2020, 40% by 2030

Parties Affected/Implementing Parties:  DEP, power stations, private and public WTE facilities

Data sources/Assumptions/Methods for GHG:

Need data on WTE GHG savings once there are specific goals in place

Waste to Energy (WTE): In 2006, Pennsylvania saved 2.3 MMTCOe as a result of recovering energy from 2.92 million tons of municipal and residual waste.  The Commonwealth can reduce an additional 4.1 MMTCOe by recovering energy from an additional 5.2 million tons of Pennsylvania municipal and residual wastes from metropolitan areas with sufficient waste generation to justify a waste to energy facility. These metropolitan areas include Allegheny, Berks, Chester, Lackawanna, Lehigh, Luzerne, Montgomery, Northampton and Philadelphia counties.

There is potential to reduce an additional 10.1 MMTCOe assuming the recovery of energy from all of the remaining 12.9 million tons of municipal and residual waste with energy value currently being land filled in Pennsylvania. This includes 6.6 MMTCOe from 8.4 million tons of out-of-state waste with energy value that could occur outside of Pennsylvania, which is not included in the 2025 goal.

GHG emissions will result from the burning of solid alternative fuel and the operation of waste to energy facilities.  However, reductions in GHGs are realized from avoided landfill emissions and the displacement of traditional energy sources with solid waste derived energy sources.

WTE: The recent Oneida-Herkimer Supreme Court Decision should encourage regional solid waste authorities to revisit the role of waste to energy as a waste management option. As remaining landfill capacity is exhausted in Bucks, Chester, Lehigh, Montgomery and Northampton counties there will be additional incentives for these regions to invest in waste to energy capacity. The Department will work with these counties to update their solid waste management plans to include waste to energy facilities. Concurrently, the Department will also work on legislative and regulatory changes to reduce or ban the disposal of certain types of materials. Subsequent efforts will focus on Allegheny, Berks, Lackawanna, and Luzerne counties as their remaining landfill capacity is exhausted.  These actions will result in the reduction of 4.05 MMTCOe.

Data Sources/Assumptions/Methods for Costs:  Costs of implementing, $ million savings from energy displaced.

Need costs of retrofits of existing WTE facilities.

From 2009-2011(?), WTE facilities will be supported by funds already committed to the solid waste program via the Recycling Fund.  These funds will not divert dollars away from the expanded recycling initiative because they come from a dedicated funding stream that is separate from recycling funding.  In 2015, it is assumed that significant market potential will have been created for WTE facilities that will cause counties and private industry to invest in construction to increase WTE capacity.  This market potential is a result potential profitability from: sale of electricity generated, funds earned through collection of tipping fees, and savings from avoided landfill construction costs.  The Department should work with PA counties to update their solid waste management plans to include waste to energy facilities. Concurrently, the Department should also work on legislative and regulatory changes to reduce or ban the disposal of certain types of materials.

Long-term actions include regulatory changes to further reduce obstacles to use of waste as an energy source.  The Waste Futures initiative will identify legislative, regulatory and other actions the Department can take to reduce excess waste disposal capacity.

The following table depicts implementation steps and targeted achievements for additional greenhouse gas reductions from solid waste management through 2025:

| YEAR | ACTION | % OF GOAL | GHG REDUCTION | COST ESTIMATE |
| --- | --- | --- | --- | --- |
| 2009 | WTE – Work with counties to include WTE in their solid waste plans |  | 2.3 MMTCOe (baseline) | The Department reimburses counties for 90% of the cost to revise county plans from the Recycling Fund. Annual costs are $850,000 |
| 2010 | WTE – Work with counties to include WTE in their solid waste plans. Initiate legislation and regulations to ban disposal of selected materials |  |  | The Department reimburses counties for 90% of the cost to revise county plans from the Recycling Fund. Annual costs are $850,000 |
| 2012 | WTE - Legislation and Regulations in Place, Continue to update county plans. Counties will start process to construct additional WTE | 50% | 9.8 MMTCOe | The Department reimburses counties for 90% of the cost to revise county plans from the Recycling Fund. Annual costs are $850,000 |
| 2015 | WTE - Increased use of Waste to Energy. Additional waste to energy capacity of 2.6 million tons per year in place. | 80% | 12.2 MMTCOe | Approximately $700 - 900 million of public or private funds would be used to construct additional capacity. |
| 2020 | WTE - Increased use of Waste to Energy. Additional waste to energy capacity of 2.6 million tons per year in place. | 100% | 14.7 MMTCOe | Approximately $700 - 900 million of public or private funds would be used to construct additional capacity. |
| 2025 | Completion |  |  |  |

Potential Overlap:

- Increased Landfill Methane Capture Work Plan

- Fuels for Schools Work Plan

- Recycling Work Plan

- AEPS Tier I (@8%, 15%, 20%) Work Plans

Implementation Steps:

Potential Overlap:

Notes/Other Considerations:

# Footnotes

Rick Illig, PA DEP, communicated via email to Brad Strode, CCS, April 2009.

Heat content of methane from http://www.epa.gov/lmop/res/converter.htm; heat content of other fuels from http://www.eia.doe.gov/kids/energyfacts/science/energy_calculator.html, accessed May 2009.

PA DEP. “Municipal Waste Disposal Information.” Data available for 1988 through 2008. Available at: http://www.depweb.state.pa.us/landrecwaste/cwp/view.asp?A=1238&Q=464453.

Lrsova, Ljupka et al. 2008. “The State of Garbage in America – 16th Nationwide Survey of MSW Management in the U.S.” Biocycle. December 2008. Available for a limited time without subscription at www.biocycle.net.

The term “diversion” is used to identify all waste that does not end up at a landfill or incineration  facility as a result of source reduction, recycling, or composting.  For the purposes of this Work Plan, diversion is equal to the sum of recycling and composting.  It is generally assumed that all food and yard waste is diverted to compost facilities, while all other diverted waste materials are recycled.

The Industry and Waste Subcommittee and members of the public have noted that there is currently no additional planned capacity for WTE in Pennsylvania.  For the purposes of this analysis, it is assumed that limitations in capacity will reduce the WTE management of imported waste.

The Environmental Benefits Calculator and associated documentation may be found at http://www.nerc.org/documents/environmental_benefits_calculator.html.

Attachment 1 is informed by data from the PA Recovered Materials Composition Report: http://www.dep.state.pa.us/dep/deputate/airwaste/wm/RECYCLE/document/Rec_Mat_Comp.pdf.

For some of the material types accepted by the EBC, there was not enough information from the available data sources to provide a composition estimate.  The unrepresented diversion was included in such categories as “Mixed Plastics”, “Mixed Metals”, or “Mixed Recyclables.”

Based on 2006 county waste disposal information posted on DEP website.

Kilowatt-hour conversion from http://www.epa.gov/grnpower/pubs/calcmeth.htm,accessed May 2009.

Thomas Brown, PA DEP; communicated via email to Rachel Anderson, CCS, May 2009.

http://www.dep.state.pa.us//dep/subject/advcoun/solidwst/swac2007.htm

May 10, 2007 meeting – link is at “Waste as an Alternative Fuel” presented by Brian Bahor, Covanta Energy (23-slide Power Point presentation).

2.92 million tons of MSW is from slide 10 – 2005 data – EfW (Energy from Waste).

2.3 MMTCO2-e is from slide 13 – EfW 2.34 MMTCO2-e/year (Used a multiplier of 0.788 tons CO2-e generated per ton MSW combusted.).

http://www.depweb.state.pa.us/landrecwaste/cwp/view.asp?A=1216&Q=488974

link is at “2006 Residual Waste Biennial Report Data” (Excel spreadsheet – 2006_rw.xls).

5.3 million tons is probably combustible portion of the total 19.4 million tons of residual waste (“2006 PA RW” tab of spreadsheet).

Additional 4.1 MMTCO2-e is 0.788 times 5.2 million tons residual waste (same multiplier as that used by Covanta).