# Pennsylvania Act 2 Land Recycling Program

# Separate Phase Liquid Screening Checklist

| Immediate Dangers |
| --- |
| Questions | Yes? | No? | N/A? | Comments |
| 1. Was separate phase liquid released or spilled? |  |  |  |  |
| 2. Was separate phase liquid released to surface (e.g., ground surface or water body)? |  |  |  |  |
| 3. Or was the separate phase liquid released to subsurface (i.e., underground)? |  |  |  |  |
| 4. Is separate phase liquid discharging to surface water (e.g., river, lake, pond, stream, etc.)? |  |  |  |  |
| Or is the separate phase liquid release near a surface water body (i.e., within _____ feet)? |  |  |  |  |
| 5. Are separate phase liquids uncontrolled? If yes, contact emergency services. |  |  |  |  |
| 6. Are the source(s) of the separate phase liquids known? If yes, specify source and date of the release. |  |  |  |  |
| 7. Are potential receptors exposed or possibly exposed to separate phase liquids? |  |  |  |  |
| 8. Are there buildings nearby the location of the release that are exposed or possibly exposed to separate phase liquids? |  |  |  |  |
| If yes, do these buildings have basements? |  |  |  |  |
| If yes, monitor for leaching of separate phase liquid and vapor intrusion? |  |  |  |  |
| 9. Have separate phase liquids been observed in soil samples or ground water monitoring wells? |  |  |  |  |
| 10. Is the separate phase liquid plume growing or moving? |  |  |  |  |
| 11. Are the separate phase liquid levels increasing? |  |  |  |  |
| 12. If separate phase liquid plume is growing or moving, do control measures need to be implemented? And where: |  |  |  |  |
| At leading edge of plume? |  |  |  |  |
| Within plume core? |  |  |  |  |
| At site boundary? |  |  |  |  |
| Other controls? And list type. |  |  |  |  |
| 13. Is the subsurface release of separate phase liquid near underground utilities (i.e., within ______ feet)? |  |  |  |  |
| 14. Is there potential of direct contact with the separate phase liquid due to excavation? |  |  |  |  |
| 15. Is mitigation needed to control potential for future releases of separate phase liquids? |  |  |  |  |
| 16. Are basements, under ground crawl spaces, subsurface utilities or any other potential subsurface exposure points present on the property or the adjoining properties? |  |  |  |  |
| 17. Is the separate phase liquid present in wells at the point of compliance? |  |  |  |  |
| If all questions are answered “no”, then immediate dangers are controlled and the site may proceed to conceptual model development. |

| Conceptual Model |
| --- |
| Questions | Yes? | No? | N/A? | Comments |
| 1. Is separate phase liquid plume delineated? |  |  |  |  |
| 2. Has the size of the SPL plume been determined? If yes, note the size under comments. |  |  |  |  |
| 3. Are SPL daughter plumes (i.e., compounds of concern) defined and delineated within ground water? |  |  |  |  |
| 4. Is it known whether the SPL daughter plumes are shrinking, stable or growing? If yes, indicate which applies: |  |  |  |  |
| Shrinking? |  |  |  |  |
| Stable? |  |  |  |  |
| Growing? |  |  |  |  |
| 5. Are the constituents of the Separate phase liquid known? If yes, indicate which applies: |  |  |  |  |
| Gasoline? |  |  |  |  |
| Diesel fuel? |  |  |  |  |
| Heating oil? |  |  |  |  |
| Metal working fluid? |  |  |  |  |
| Lubrication oil? |  |  |  |  |
| Mineral Oil |  |  |  |  |
| Other? |  |  |  |  |
| 6. Are the potential receptors defined? |  |  |  |  |
| 7. Are the potential pathways of SPL migration defined? |  |  |  |  |
| 8. Have the following site-specific SPL characteristics been estimated or measured: |  |  |  |  |
| Specific gravity/density? |  |  |  |  |
| Viscosity? |  |  |  |  |
| Interfacial/Surface Tension? |  |  |  |  |
| Others?: (indicate which) |  |  |  |  |
| 9. Is the SPL defined horizontally? |  |  |  |  |
| 10. Is the SPL defined vertically? |  |  |  |  |
| 11. Has any vapor plume from SPL been defined, if applicable? |  |  |  |  |
| 12. Are aquifer parameters defined? |  |  |  |  |
| 13. Are ground water use defined (e.g., used or non-use aquifer)? |  |  |  |  |
| If all questions are answered “yes”, then the conceptual model is complete and the site should evaluate whether response triggers have been exceeded. |

| Response Action Triggers |
| --- |
| Questions | Yes? | No? | N/A? | Comments |
| 1. Has separate phase liquid been observed on the ground surface? |  |  |  |  |
| 2. Has separate phase liquid or a sheen been detected on surface waters? |  |  |  |  |
| 3. Have vapors been detected in buildings, sewers, utility trenches or other preferential pathways? |  |  |  |  |
| 4. Has separate phase liquid been observed in groundwater monitoring wells or water supply wells? |  |  |  |  |
| 5. Do concentrations of dissolved phase contaminants in groundwater samples approach levels that suggest the nearby presence of separate phase liquids? |  |  |  |  |
| 6. Has a fate & transport analysis been completed? (if no move to question 10) |  |  |  |  |
| 7. Does fate & transport analysis show that separate phase liquid or sheen will migrate to surface waters? |  |  |  |  |
| 8. Does fate & transport analysis show that vapors will migrate to buildings, sewers, utility trenches or other preferential pathways? |  |  |  |  |
| 9. Does fate & transport analysis show that separate phase liquids will migrate to groundwater monitoring or water supply wells? |  |  |  |  |
| 10. |  |  |  |  |
| If all questions are answered “no”, then triggers are not exceeded and the separate phase liquid concerns may proceed to closure.. |