| REGULATED SUBSTANCE | CASRN | Used Aquifers | Non-use Aquifers |
| --- | --- | --- | --- |
|  |  | TDS ≤ 2500 | TDS > 2500 |  |
|  |  | R | NR | R | NR | R | NR |
| ARSENIC* | 7440-38-2 |  | [50] 10 | M | [50] 10 | M | [5,000] 1,000 | M | [5,000] 1,000 | M | [50,000] 10,000 | M | [50,000] 10,000 | M |
| MANGANESE | 7439-96-5 |  | 300 | H | 300 | H | 30,000 | H | 30,000 | H | 300,000 | H | 300,000 | H |

* This standard became effective 1/23/2006

| SECONDARY CONTAMINANTS |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| REGULATED SUBSTANCE | CASRN | SMCL | UNITS |  |  |  |  |  |  |  |  |
| COLOR |  |  | 15 | color units |  |  |  |  |  |  |  |  |  |
| CORROSIVITY |  |  | non-corrosive |  |  |  |  |  |  |  |  |  |  |
| FOAMING AGENTS |  |  | 500 | µg/L |  |  |  |  |  |  |  |  |  |
| ODOR |  |  | 3 | threshold odor numbers |  |  |  |  |  |  |  |  |
| pH |  |  | 6.5-8.5 |  |  |  |  |  |  |  |  |  |  |
| SULFATE | 7757-82-6 |  | 250,000 | µg/L |  |  |  |  |  |  |  |  |  |
| TOTAL DISSOLVED SOLIDS (TDS) |  |  | 500,000 | µg/L |  |  |  |  |  |  |  |  |  |