## Slide 1: Concepts for Proposed General Permit for Well Pads and Proposed GP-5 Modifications Citizens Advisory Council March 15, 2016
Tom Wolf, Governor John Quigley, Secretary

## Slide 2: Headings : White Text 40 pt. Calibri
Purpose of the Final RACT Rulemaking
  On January 19, 2016, Governor Tom Wolf announced a four- point methane emission reduction strategy for Oil and Gas operations.
    DEP will develop a new general permit for new unconventional well pad operations.
    DEP will revise its current general permit (GP-5) updating the permitting requirements.
    DEP will develop a regulation for existing sources for consideration by the Environmental Quality Board.
    DEP will establish best management practices, including leak detection and repair programs to reduce emissions along production, gathering, transmission and distribution lines.
Background

## Slide 3: Headings : White Text 40 pt. Calibri
Purpose of the Final RACT Rulemaking
  Oil and natural gas wells are currently exempted from permitting requirements provided the owner or operator complies with the Category No. 38 exemption criteria specified in DEP’s list of “Air Quality Permit Exemptions.” (Document No. 275-2101-003).
  As part of the DEP’s Methane Emission Reduction Strategy, DEP is developing a new general permit to replace the Category No. 38 exemption criteria for well pad operations.
Concepts for the General Permit for Well Pad Operations

## Slide 4: Headings : White Text 40 pt. Calibri
What is Reasonably Available Control Technology?
  Most of the substantive requirements for the Category No. 38 exemption criteria will be proposed in the new general permit for well pads operations.
  The DEP is also exploring the possibility of proposing that diesel-fired engines used on drill rigs meet the EPA’s Tier 4 standards.
  The leak detection and repair (LDAR) requirements proposed may be similar to the current GP-5, including quarterly LDAR inspections using an optical gas imaging system and monthly Audio Video Olfactory (AVO) inspections.
Concepts for the General Permit for Well Pad Operations

## Slide 5: Headings : White Text 40 pt. Calibri
Re-evaluation of RACT
  The first attempt at a leak repair would be done within five (5) calendar days of leak detection. If purchase of parts is necessary, the leak must be repaired within 15 calendar days after the purchase of parts.
  VOC emissions from storage tanks must be controlled by at least 95%.
  The proposed general permit for well pads will also include fugitive dust control measures.
Concepts for the General Permit for Well Pad Operations
Notes: Edited for grammar.

## Slide 6: Headings : White Text 40 pt. Calibri
Re-evaluation of RACT
The DEP intends to propose no-bleed and/or low-bleed requirements for pneumatic controllers and pumps.
Emissions from pumps may also be controlled through routing pump discharge streams into a closed loop system or a vapor recovery unit.
  The proposed GP may also require the operation of pig launchers without venting hydrocarbons into the atmosphere.
Concepts for the General Permit for Well Pad Operations

## Slide 7: Headings : White Text 40 pt. Calibri
Re-evaluation of RACT
The proposed GP may require plunger lifts or flaring to reduce methane emissions from wellbore liquid unloading.
The DEP is examining strategies to reduce emissions from produced water impoundment tanks. The DEP is considering add-on controls on enclosed storage tanks or a closed loop system for an efficient reuse of produced water.
Annual compliance certifications may be required to be submitted to the DEP by a Responsible Official, as is the case under the current GP-5.
Concepts for the General Permit for Well Pad Operations

## Slide 8: Headings : White Text 40 pt. Calibri
Final RACT Rulemaking Impacts
  An owner or operator of natural gas compressor stations may request authorizations to use DEP’s General Plan Approval and General Operating Permit for Natural Gas Compression and/or Processing Facilities (GP-5).
  Modifications to existing GP-5 are being developed for public review and comment.
The applicability of GP-5 may be extended to natural gas transmission operations.
Concepts for GP-5 Modifications

## Slide 9: Headings : White Text 40 pt. Calibri
Final RACT Rulemaking Impacts
The DEP may require no-bleed and/or low-bleed pneumatic controllers.
  The first attempt at leak repair would be required within five (5) calendar days of leak detection. If the purchase of parts is necessary, the leak must be repaired within 15 calendar days after the purchase of parts.
Concepts for GP-5 Modifications

## Slide 10: Headings : White Text 40 pt. Calibri
Final Rulemaking: Affected Facilities
The DEP intends to require owners and operators to prevent venting of VOCs and methane during all compressor maintenance and operational activities.
  The proposed GP-5 modifications will require the control of air contaminant emissions from storage tanks by at least 95%.
  The general permit may require the operation of pig launchers without venting hydrocarbons into the atmosphere.
Concepts for GP-5 Modifications

## Slide 11: Headings : White Text 40 pt. Calibri
Final Rulemaking: Affected Facilities
The DEP intends to propose the use of electric pumps or routing pumps discharged to closed systems when electricity is not available.
Emissions from pneumatic pumps driven by natural gas may also be controlled through routing pump discharge streams into a closed loop system or a vapor recovery unit, or the pumps may be replaced with zero bleed pumps.
The use of dry seals or control of wet seal venting of methane from each compressor by 95% would also be included in the proposed GP-5 modifications.
Concepts for GP-5 Modifications
Notes: Fixed formatting error.

## Slide 12: Headings : White Text 40 pt. Calibri
Final Rulemaking: Affected Facilities
Methane Reduction Strategy Page
  http://www.dep.pa.gov/Business/Air/Pages/Methane-Reduction-Strategy.aspx
Methane Strategy Briefing Paper
  http://files.dep.state.pa.us/Air/AirQuality/AQPortalFiles/Methane/DEP%20Methane%20Strategy%201-19-2016%20PDF.pdf
  Methane Strategy Briefing Paper Appendix
    http://files.dep.state.pa.us/Air/AirQuality/AQPortalFiles/Methane/Appendix%20A%20-%20Comparison%20of%20PA-%20EPA%20NSPS%20Proposal-%20CSSD%20-%20CO%20Requirements%20for%20the%20Oil%20and%20Gas%20Sector%20%2012-15-2015.pdf
Useful Links

## Slide 13
Krishnan Ramamurthy
Chief, Division of Permits
717-783-9476
kramamurth@pa.gov